## Slide 1: Annual TAC Review of the Market Impacts of Reliability Unit Commitments
ERCOT Market Analysis
Analysis of 1/1/12 through 11/30/12

## Slide 2: RUC Effective MWh by Month
Chart: RUC Effective MWh by Month
| 201201 | 201202 | 201203 | 201204 | 201205 | 201206 | 201207 | 201208 | 201209 | 201210 | 201211
RUC LSL MWh | 855.62 | 0 | 2758.89 | 2929.94 | 573.03 | 378.99 | 22.01 | 0 | 1362.1 | 9512.33 | 15408.79
RUC BP MWh | 1122.59 | 0 | 3678.83 | 4367.7 | 1226.8 | 616.29 | 22.25 | 0 | 3569.22 | 11196.35 | 18898.9

## Slide 3: RUC Commitments and Offers
267 Instructed Effective RUC Unit Hours in 2012
  174 hrs (65.17%) for Voltage/Reactive Support
  86 hrs (32.21%) for Congestion
  7 hrs (2.62%) for Capacity
251 Instructed Effective RUC Unit Hours were required to have an Energy Offer Curve priced at SWCAP for MW above LSL (required since March 1, 2012)
Energy Offer Curve Compliance
  64 hrs (25.50%) properly priced at SWCAP above LSL
  27 hrs (10.76%) not priced at SWCAP above LSL with less than an hours notice to update
  160 hrs (63.75%) not priced at SWCAP above LSL with more than an hours notice to update

## Slide 4: RUC Committed Resources Dispatched for Capacity
  260.18 Effective RUC Unit Hours
    Difference between this number and the 267 is a result of Resources starting up, shutting down, or still being Off-Line for some portion of the RUC committed hours
  LMP<=System Lambda+2 and BP>=LDL+2 used to determine dispatch for capacity
  82.07 hrs (31.54%) were dispatched above LSL for capacity during which:
    81.98 hrs (31.51%) had prices below $100
    0 hrs (0%) had prices between $100 & $500
    0.08 hrs (0.03%) had prices between $500 and $3000
    0 hrs (0%) had prices greater than or equal to $3000
Notes: RN LMP = System lambda & BP> LDL => Resource is moved up for capacity since there is no congestion
RN LMP > System lambda & BP> LDL => Resource can contribute to reducing congestion and hence could be moved up for transmission.

## Slide 5: 0 to LSL Energy from ONRUC Resources
260.18 Effective RUC Unit Hours
    Average ONRUC LDL is 142MW,LSL is 130 MW,BP is 172 MW, HSL is 283 MW
  144.59 hrs (55.57%) are at or below LDL (BP-LDL<2MW)
    Average ONRUC LDL is 103 MW, LSL is 96 MW
  115.59 hrs (44.43%) are above LDL for transmission or capacity
    Average ONRUC LDL is 192 MW, LSL is 173 MW
232.34 Effective RUC Hours with at least one resource on ONRUC status
    Average system total ONRUC capacity for only these hours:
      LDL is 159 MW
      LSL is 146 MW
      HSL is 316 MW
      BP is 193 MW
‘Effective RUC Unit Hours’ is SCED duration, summed up to hour level, for each RUC committed Resource when it was On-Line. ‘Effective RUC Unit Hours’ considers multiple Resources committed for the same hour as different unit hours while ‘Effective RUC Hours’ considers it as single hour.

## Slide 6: RUC Committed Resources - Histogram of RUC LSL

## Slide 7: RUC Committed Resources - Histogram of RUC BP

## Slide 8: RUC Committed Resources - Relationship to Real-time Prices
Notes: Offer floor could increase the system lambda for all intervals with Capacity Headroom <=0

## Slide 9: RUC Committed Resources - Relationship to Real-time Prices

## Slide 10: RUC Committed Resources - Relationship to Real-time Prices

## Slide 11: RUC Committed Resources - Relationship to Real-time Prices

## Slide 12: Estimated PNM Impact of RUC Committed Resources
Month | Actual Incremental PNM | Incremental PNM Adder from Study
1 | 1428.39 | 0.00
2 | 195.14 | 0.00
3 | 7509.02 | 0.00
4 | 4525.34 | 0.00
5 | 1495.18 | 0.48
6 | 6309.35 | 0.00
7 | 2012.48 | 0.05
8 | 3621.49 | 0.00
9 | 1782.58 | 9.44
10 | 2181.55 | 0.59
11 | 1777.33 | 10.84
Total | 32837.85 | 21.41
New PNM | 32859.26 | 
  The monthly incremental Peaker Net Margin (PNM) was analyzed by relaxing the LSL to 0 for all RUC committed Resources and simulating the SCED solution
  The results indicate that the LSL of these Resources did not have a significant impact on the PNM for 2012 thru November