## Slide 1: PLWG Recommendation on PGRR-025
February 14, 2013

## Slide 2: Background
2011
  After February 2011 events, TAC directs ROS to investigate gap between planning and operations.
  ROS directs working groups to identify and address gaps between planning and operations.
  Luminant proposes PGRR-011 revising ERCOT planning criteria assumptions and performance requirements consisting of (but not limited to):
    Load variation
    Generation variation
    Unavailability of an autotransformer
    Transmission line ratings
  ROS action of Fall 2011:
    1) rejects PGRR-011 and creates Operations and Planning Synchronization Task Force (OPSTF) for further investigation; and,
    2) solicits stakeholder input on issues related to planning and operations gap(s).
  Fourteen issues provided by stakeholders are considered.

## Slide 3: Background
April 2012 ROS Meeting
  OPSTF Chair reviewed the draft OPSTF issues list, noting that 14 issues were discussed; that four issues are recommended for referral to PLWG; and that three issues be prioritized for OPSTF.
  CenterPoint moved to approve the issue list and to prioritize Items 5, 7, and 8 for OPSTF. Brazos Electric Cooperative seconded the motion.
    (5) Appropriate Load levels to consider in planning studies;
    (7) Long-term unavailability of autotransformers; and,
    (8)Generator unit unavailability and modeling issues.
  The motion carried unanimously.

## Slide 4: Background
OPSTF recommendation to ROS – September 13, 2012
  Change the ERCOT Planning Criteria to require that with any single 345/138 kV transformer unavailable followed by system adjustments, the loss of a single generator, transmission line circuit, transformer, shunt device, FACTS device, or double circuit transmission line all facilities shall be within their applicable ratings, the system shall be stable with no cascading or uncontrolled islanding, and there shall be no non-consequential load loss. Also, a RAP or SPS may be planned on a permanent basis to resolve a performance deficiency under this condition.
  Refer the proposal to the PLWG to develop a Revision Request to change the ERCOT Planning Criteria with a time-sufficient implementation schedule

## Slide 5: Background
ROS action - September 13, 2012
  LCRA TSC moved to endorse the OPSTF recommendation. Oncor seconded the motion.
  The motion carried with three abstentions from the Independent Power Marketer and Independent Retail Electric Provider Market Segments.
  ROS approved recommendation made by OPSTF.

## Slide 6: PLWG consideration on OPSTF issue (7): Long-term autotransformer unavailability
Potential Benefits | Potential Benefits
Consistent with NERC Reliability Standards revisions approved by NERC Ballot Body and NERC Board of Trustees. Consistent with treatment of other long-lead type equipment (e.g., generator unavailability) in ERCOT. Alignment between planning analysis and real time operational conditions. Increased reliability of the transmission grid. Reduced system impact due to long-term equipment outages. | Increase efficiencies on outage scheduling for construction or maintenance work. Minimize the need for planned load shedding. Reduces transmission congestion. Increase flexibility to utilize available generation capacity.
 | Potential Impacts
 | Transmission Cost of Service (TCOS) charges will increase when projects are implemented due to the proposed criteria change.

## Slide 7: PLWG consideration of potential impacts associated with PGRR-025
ERCOT screening
  Unavailability of a 345/138 kV autotransformer followed by the loss of another autotransformer or a transmission line including a double circuit line sharing a common tower more than 0.5 miles
  Power flow case
    2017 power flow case with a load level of 84,987 MW (includes self-serve loads)
    245 autotransformers (345/138 kV) included in this case
2017 Summer Peak - 69 instances where the unavailability of an autotransformer resulted in a system deficiency
  254 system deficiencies are transmission line overloads (loading >100 % of rating)
  43 system deficiencies are autotransformer overloads (loading >100 % of rating)
  127 system deficiencies are facility loading > 110% of rating

## Slide 8: Factors supporting approval of PGRR -025
Experience on autotransformer unavailability in ERCOT during 2012
  Forced outage loss of 345/138 kV autotransformers
    12 instances of autotransformer outages in 2012
    Autotransformer outage duration range (0.5 – 9.5 months) within 2012
Findings in the ERCOT 2012 “Report on Existing and Potential Electric System Constraints and Needs”
  Loss of autotransformers resulted in three of the top 15 constraints in 2012 . Congestion Rents totaling over $45 million between 01/2012-10/2012 attributed to the unavailability of 345/138 kV autotransformers.
ERCOT Impact Analysis does not indicate a need for significant additional staff / resources

## Slide 9: Factors supporting approval of PGRR -025
Alignment with proposed NERC Reliability Standard TPL-001-2, Transmission System Planning Performance Requirements, R.2.1, 2.1.5 requires Entities to assess the impact of the possible unavailability of major transmission equipment having a lead time of one year or more (such as a transformer) on system performance.
Long-lead delivery times on transformers ranging anywhere between 1 - 2 years.
Impacts to ERCOT system reliability.

## Slide 10: PLWG Recommendation
In response to OPSTF findings and ROS direction, PGRR-025 adds testing and performance requirements to the ERCOT Planning Criteria to address the unavailability of 345/138 kV autotransformers.
PLWG consensus reached at October 25, 2012 with the following entities in attendance:
PLWG recommends ROS approval of PGRR 025 .

## Slide 11
Questions?

## Slide 12: PGRR-25
From ERCOT 2012-2016 Strategic Plan:
Transmission Adequacy
In order to improve grid reliability and power deliverability as well as to reduce congestion and improve grid efficiency, ERCOT completes system planning studies of the ERCOT transmission system. ERCOT will work with transmission owners and stakeholder committees to ensure a transmission system that cost-effectively meets relevant NERC standards and ERCOT Protocol requirements, facilitates the ERCOT market, and appropriately accounts for low probability events that could have significant market impact.
From ROS 2012 Goals:
Complete a review of the Guides, Procedures and Protocols to ensure proper alignment between planning and operational realities.