## Slide 1: Same Transmission Element
Proposed Revision to the Shadow Price Cap and Power Balance Penalties in SCED
Notes: <number>

## Slide 2: What Makes Up a Constraint?
<number> <number>
A “constraint” is defined by the following –
  Transmission Element (“E”)
    Typically lines or transformers
  Contingency (“C”)
    The “What If?”
    Which lines or transformers are out of service
  Direction (“D”)
    Which way is the power flowing?

## Slide 3: For Example
<number> <number>
ODNTH_FMR1/SNCWMOS8/138kV->69kV
  ODNTH_FMR1 = Transmission Element
    In this case, the Odessa North Transformer
  SNCWMOS8 = Contingency
    In this case, three line segments
      1143-1144
      1143-1141
      1143 1019
  138kV->69kV = Direction

## Slide 4: It’s Kind of Like….A Hot Dog!
<number> <number>

## Slide 5: Three Major Components
Instead of -
  Transmission Element/Contingency/Direction
You have –
  Frank/Mustard/Bun
<number> <number>

## Slide 6: But What About Ketchup?
Not everybody likes mustard so what if instead you have –
  Frank/Ketchup/Bun
Is it still a Hot Dog?
OF COURSE, IT IS!
<number> <number>

## Slide 7: Back to Constraints
There are around 36M constraints (E/C/D) but some very similar to others (E/C’/D) or (E/C”/D).
A small change in the network model or other conditions can cause the binding constraint to jump from one constraint (E/C/D) to another very similar constraint (E/C’/D).
In most cases the underlying physical problem on the system (E & D) is actually the same and they have very similar effects on the market.
<number> <number>

## Slide 8: Shift Factor Correlation
This can be measured by the shift factor correlation
  Calculated the shift factor at each pricing bus for Irresolvable Constraint
  Calculated the shift factor at each pricing bus for constraints with same Transmission Element and Direction (E&D)
The correlation between the shift factors for the Irresolvable Constraint and other constraints with same E&D was over 90%
<number> <number>

## Slide 9: For Example
Analysis of 2012 data showed that -
  All binding constraints with a correlation of >90% to ODNTH_FMR1/SNCWMOS8/138->69kv had the same E&D i.e. ODNTH_FMR1/XXXX/138->69kv
  Similarly, all binding constraints with a correlation of >90% to 6215__A/DODEQAL5/CGRSW->BCKSW had the same E&C i.e. 6215__A/XXXXXX/CGRSW->BCKSW
In other words, they all had a frank and a bun but may have had ketchup or relish or chili instead of mustard
<number> <number>

## Slide 10: Same Transmission Element
Currently, a constraint is deemed irresolvable by SCED if:
  A non-competitive constraint violation is not resolved by SCED or overridden for more than two consecutive hours on more than 4 consecutive Operating Days; OR
  A non-competitive constraint violation is not resolved by SCED for more than a total of 20 hours in a rolling thirty day period.
<number> <number>

## Slide 11: AEP’s Proposed Revisions
Our proposal keeps those in place but adds an additional criterion –
  A constraint has the same Transmission Element and Direction as a constraint that has met criterion A or B
The Shadow Price Cap for a such a constraint will be set to the same value as the constraint that met either trigger condition A or B
Also, total $$ tracking towards $95K is tracked by the set of constraints with same Transmission Element and direction rather than the individual constraint
<number> <number>

## Slide 12: Impacts to Market
If our proposal had been in effect in 2012, it would have reduced the HB_WEST->LZ_WEST congestion by 2.6%
That may not seem like a lot but in fact translates into ~$2500/MW
That’s a lot of hot dogs!
<number> <number>

## Slide 13: Ideally We Want…
A motion to recommend approval AEP’s revisions to ERCOT’s Methodology for Setting Maximum Shadow Prices for Network and Power Balance Constraints
<number> <number>

## Slide 14: If Not, Then…
A motion to remand to WMS with instructions to come back with a recommendation at the April TAC meeting.
THANKS FOR YOUR SUPPORT!
<number> <number>

## Slide 15: For the Geeks
And, Let’s Face It, We All Are…

## Slide 16: Quantitative Impact Analysis
Correlation Analysis
  Use set of binding constraints that had Shadow Price > $2000 in RT (241, could not map 23 to FEB CRR case, used 218)
  If contingency was not defined in FEB 2013 case, use BASE CASE
  Find shift factors for each constraint (all planning buses) [labor intensive]
  Find HB_WEST to LZ_WEST shift factors for each constraint
  Calculate correlation factors for each constraint relative to the Non-Competitive/Irresolvable constraints (ODNTH_FMR1 and 6215__A)
<number> <number>

## Slide 17: Quantitative Impact Analysis
Correlation Analysis (cont.)
  For each constraint that had a correlation factor higher than 90% to ODNTH_FMR1, multiply the shift factor by the difference between the ODNTH shadow price cap and the actual shadow price (then by 1/12)
  For each constraint that had a correlation factor higher than 90% to 6215__A and occurred after May 3rd, 2012, multiply the shift factor by the difference between the 6215__A shadow price cap and the actual shadow price (then by 1/12)
  Those numbers added up to $2500.
    Error source – used FEB 2013 CRR model rather than actual daily models – should be low (<20%)
<number> <number>