## Slide 1: NPRR 520 Resmi Surendran ERCOT

## Slide 2: Current CCT Process
Annual CCT (ACCT) is run every year to feed the results to Monthly CCT (MCCT)
MCCT is run every month to feed the results to Daily CCT (DCCT).
Currently ACCT & MCCT results are set to CSC/CRE from 2010
For each Operating Day (OD), DCCT runs the day before the OD using the COP data from peak hour of the OD and post results by 6 AM the day before OD
Evaluate ECI at export and import side with WGR at zero output at import side

## Slide 3: Current SCED 2-Step Process
STEP1 - Resolves competitive constraints using submitted energy offer curves to produce Reference LMPs
Prior to STEP2 – Irrespective of presence of non-competitive constraints, mitigate ALL online resources
  Offer curve capped at Max(Ref LMP, Mitigated Offer Cap)
  Offer curve bounded at Min(Ref LMP, Mitigated Offer Floor)
STEP2 – Resolves both competitive & non-competitive constraints using mitigated (capped/bounded) energy offer curve to produce Base Points and LMPs

## Slide 4: Offer Mitigation

## Slide 5: NPRR 520
Run CCT on active constraints every 5 min to identify which constraints to be considered as competitive and which Resource to be mitigated
Competitiveness in SCED CCT is determined using import side ECI and telemetered HSL of online Resources
Identify DMEs to be mitigated
  DME with negative-side-ECI greater than a threshold for an active non-competitive constraints or
  DME which is pivotal for a non-competitive constraint as the DMEs
For those DMEs, mitigate only Resources with SF > threshold

## Slide 6: NPRR 520
Mitigate based on Min[offer, Max(Ref LMP +K1*MOC at lsl, MOC)]
Apply offer floor to all resources to address predatory pricing
To prevent mitigation from switching between being applied and not being applied,
  once a Resource is identified for mitigation, it will be mitigated for the rest of the operating hour
  Any constraint deemed non-competitive during the operating hour will not be re-evaluated and will be considered non-competitive until the top of the next operating hour

## Slide 7: NPRR 520
Preliminary results for different thresholds

## Slide 8
Appendix
Issues addressed by NPRR 520

## Slide 9: Over Mitigation Issue Price for capacity being set by mitigated offer
Mitigation is currently applied to ALL online resources irrespective of their impact to any active non-competitive constraint
Resources that were economical and hence moved up in STEP1 could be moved down in STEP2 if they have positive Shift Factor to a non-competitive constraint. Resources having no impact on the non-competitive constraints could then be moved up based on their mitigated prices to meet power balance requirement in STEP2.
Offer floors for NSPIN/RUC/RMR, QSGR offers and offers submitted based on Voluntary Mitigation Plan (VMP) could be uneconomical in STEP1 but could become economical in STEP2 and hence get dispatched at mitigated price
Fix: Only mitigate Resource that have significant impact to the active non-competitive constraint

## Slide 10: Offer Mitigation Base Point Oscillation

## Slide 11: Over Mitigation Issue Base Point Oscillation
Marginal Resources could be moved around based on changes in system condition like drop in wind, unit tripping etc
Offer floors for NSPIN/RUC/RMR, QSGR offers, offers submitted based on VMP increases the number of marginal Resources and hence more Resources are moved around
When Reference LMP is higher than typical Mitigated offer cap, Resources with high submitted offers get mitigated at Reference LMP. Under tight system condition Reference LMP could change significantly between consecutive SCED runs causing the offers of these resources to move between economical and uneconomical with respect to other offer resulting in Base Point oscillation
Fix : Base Point oscillation could be minimized by reducing the set of Resources that are subject to mitigation

## Slide 12: Tie Breaking Issue QSGRs brought online when not needed by system
“Tie breaking” logic – Even with no constraints, SCED prorates the energy awarded at Ref LMP in STEP1 to all online resources in STEP2 that have a mitigated price equal to Ref LMP
When Ref LMP > typical mitigated offer cap, mitigation often results in lots of Resource offers at the same price (Ref LMP) in STEP2.
All QSGRs operating with ON status (Protocol 3.8.3 ) may receive small, non-zero Base Points requiring them to come online at LSL when they are not really needed by system which in turn causes price depression
  Fix : Eliminate multiple offers at same price
    Cap EOC at max(MOC, Ref LMP + (MOC at LSL)* K1) instead of max(MOC, Ref LMP) where K1 is significantly small, e.g. 0.001
    Issue: Multiple QSGRs in the same location with the same MOC can still see tie-breaking impact if their MOCs are same.
Notes: Protocol 3.8.3 - QSGRs operating with telemeter status of ON and LSL of 0, when providing NSRS are required to open the capacity to SCED and offer it at or above $180/MWh. They are required to come online when they get a Base Point >0