## Slide 1: ERCOT Dynamic Ratings Application
Wholesale Market Subcommittee
April 12, 2012

## Slide 2: Background
Transmission companies have the option to provide a table of ambient temperature-adjusted line ratings in the ERCOT Network Operations Model
ERCOT systems utilize these tables, along with the Weather Forecast to generate ratings for Real-Time and future studies, including
  Congestion Revenue Rights (CRR)
  Day-Ahead Market (DAM)
  Reliability Unit Commitment (RUC)
  Real-Time (SCED)
Note that not all transmission lines are, or have to be, dynamically rated
Notes: Following the discussion at the March 26 Regional Planning Group meeting, ERCOT was asked to bring to WMS details on how Dynamic Ratings are currently being utilized in ERCOT systems

## Slide 3: How Are Dynamic Ratings Implemented?
CRR
  Monthly Auction: Forecasted maximum on-peak temperature
  Long-Term Auction Sequence: 10-Year historical on-peak average maximum temperature
DAM/DRUC/Operational Studies
  Weather Forecast
HRUC
  Real-Time ratings for first hour; Weather Forecast for future hours
SCED
  Real-Time temperatures (by Load Area), or
  Telemetry (Amps, MVA, local temperature)

## Slide 4: How Are Dynamic Ratings Implemented?
How often do the ratings change?
  Telemetry
    Can be updated in Real-Time
    Ratings can change with each State Estimator execution
      Typically once every five minutes
  Weather Forecast
    The Weather Forecast updates automatically every hour
    With every State Estimator execution, the Weather Forecast is queried to ensure the proper ratings are considered

## Slide 5: Dynamic Rating Example