Discussion on Outage Scheduler SCR

Add the following fields to the Approved and Accepted Outage List -- low impact

o   Nature of Work – Provides users with the stated reason for the outage from a pull down.  Among the reasons in the pull down is a selection for new equipment.

o   Requesting Company Full Name – clears up confusion on who submitted outage

o   Normal State for breakers and switches – useful for distinguishing between an outage and an “innage”

o   Breaker and switch outage status - useful for distinguishing between an outage and an “innage”

o   TEID – useful for referencing back to the CIM posting

o   Start Deviation – This would be a calculated field showing the +/- deviation in Planned and Actual Start

o   End Deviation -- This would be a calculated field showing the +/- deviation in Planned and Actual End

o   TSP Notes – Field dedicated for TSPs to include scheduling information (see below)

Add a Cancelled Outage report – low impact

o   This would include a reason the outage was cancelled from a pull down, but would not include rescheduling information as I believe that would be too complicated to keep up with.  Outages are not officially rescheduled until ERCOT approves them.  Approval may take several days.

o   This report would hold the cancelled outage information for an undetermined amount of time (whatever is needed)

o   Report would include a field that categorized the cancellation as “Before CRR”, “After CRR”, or “After DAM”

The Existing Withdrawn Outage report addition– low impact

o   Only ERCOT can withdraw an outage and the only reason is for reliability.  Therefore the reason for the withdrawal would not be included in the report

o   Report would include a field that categorized the withdrawal as “Before CRR”, “After CRR”, or “After DAM”

	Provide a notes field in the Approved/Accepted list that allows the TSP that has delayed their outage 24 hours to provide their justification.  If the deviated start and end times are public, TSPs will have an incentive to provide the explanation.

Monthly Summary Report

o   Some kind of report that categorizes average TSP “start deviation” and “end deviation”