## Slide 1
Business Practice Proposal to Accommodate NPRR 520 Changes
TAC
May 2, 2013

## Slide 2: Agenda
Background
Concerns with existing language
Description of proposed changes
Discussion of potential impacts

## Slide 3: Background
The Business Practice document “Setting the Shadow Price Caps and Power Balance Penalties in Security Constrained Economic Dispatch” was being reviewed in preparation for SWCAP change taking effect on 6/1/2013
During the review, we identified language in a different section that is inconsistent and cannot be accommodated in the MMS as part of the implementation of NPRR 520
  Section of concern discusses the process for identifying constraints that are consistently irresolvable by SCED and determining shadow price cap adjustments for those constraints
  The process is only applied to constraints when they are deemed non-competitive
  Implementation of NPRR 520 includes the Real-time evaluation of the competitiveness of a constraint

## Slide 4: Concerns with Existing Language
Business Practice document makes reference to Protocol Sections which no longer exist
Implementation of NPRR 520 results in a more dynamic determination of the competitiveness of a constraint
Process of consistently irresolvable in SCED constraints is only applied to non-competitive constraints
Current MMS functionality only designed to have a single shadow price cap for each monitored element
  Shadow price caps cannot be applied as a function of the competitiveness of a constraint
Methodology will be more complicated and it may be less clear to the Market which shadow prices caps are going to be applied to a constraint each SCED run

## Slide 5: Description of Proposed Changes
Proposed changes remove the dependency of the methodology on the competitiveness status of a constraint by removing:
  Term “non-competitive”
  References to Nodal Protocol Section 3.19
  Other language that requires ERCOT to only apply the irresolvability process during periods in which a constraint is deemed non-competitive
Other clarifications and minor changes are:
  Changing an illustrative example in Section 3.5.1 to use $5000/MWh instead of $3000/MWh
  Administrative changes
  Clarifying that the resetting of a shadow price cap for a constraint deemed to be resolvable will be an annual process

## Slide 6: Discussion of Potential Impacts
Proposed edits will avoid the need for systems changes and should have a limited impact on SCED results
Reasoning is that if a constraint is truly competitive under most scenarios, SCED will be able to resolve the constraint and the irresolvablility process will not impact the shadow price cap
  Design is practically applied without new code
Chart: Fraction of Binding Intervals
Duration Curve of 2012 Binding Shadow Prices in SCED for the West to North Stability Limit Constraint