## Slide 1
Recommended Threshold Value for ECI in SCED Constraint Competitiveness Test
May 2, 2013 TAC Meeting

## Slide 2: Background Information
After implementation of the nodal market in December of 2010, the IMM and Market Participants observed that the SCED “Texas Two Step” mitigation process resulted in over-mitigation of prices in real-time. In the IMM’s 2011 State of the Market Report, the following recommendation was made:
  “We recommend a change to the automated mitigation procedures that are part of the real-time dispatch to eliminate the occurrences of over-mitigation … We support introducing a test to determine whether a unit is either contributing to, or helping to resolve a transmission constraint and only subject the relieving units to mitigation.”
Market participants and ERCOT Staff worked throughout 2012 to improve the CCT. On March 19, 2013 the ERCOT Board approved NPRR520, Real-Time Mitigation Rules and Creation of a Real-Time Constraint Competitiveness Test, to address the over-mitigation issue.
Today TAC is considering the proper values for the parameters utilized in NPRR520.

## Slide 3: Today’s TAC Vote -Threshold Values for Competitive Constraint Test
Threshold | Definition | Value
SFP1 | Minimum shift factor threshold for determining which Managed Capacity to include in the ECI calculation | 2%
ECIT1 | Maximum competitive threshold for ECI on the import side of a constraint for the Long-Term CCT process | 2000
SFP2 | Minimum shift factor threshold for a constraint to be eligible to be a Competitive Constraint as part of the Long-term CCT Process | 2%
ECIT2 | Maximum competitive threshold for ECI on the import side of a constraint for the SCED CCT process | ????
SFP3 | Minimum shift factor threshold for a constraint to be eligible to be a Competitive Constraint as part of the SCED CCT Process | 2%
DMEECP | Threshold for the ECI Effective Capacity for an Entity or its Affiliates to determine if their Managed Capacity is eligible to be mitigated as part of SCED Step 2 | 10%
SFP4 | Minimum shift factor threshold below which a Resource will not have mitigation applied in SCED Step 2 | 2%

## Slide 4: Why Today’s Vote for ECIT2 is Important
NRG believes NPRR520 will be a significant improvement over the previous CCT design and does not want to slow down its implementation.
However, an overly conservative value for ECIT2 will combine with significantly conservative design elements of the new CCT methodology to produce undesired results, such as the mitigation of constraints that have historically been solved competitively since the market opened.
Since the primary objective of NPRR520 was to reduce the occurrence of over-mitigation in real-time, a balanced approach to setting the ECI threshold value is necessary to ensure efficient and fair market outcomes.
The purpose of the following slides is to:
  Describe the significantly conservative design elements that are inherent to NPRR520.
  Describe the various and significant protections that are still in place.
  Recommend that TAC set the ECIT2 parameter at 2,500 to balance the methodology.

## Slide 5: New Market Share Calculations are Conservative
NPRR469 introduced, among other things, a significant change in the basic ECI calculation that makes the methodology much more conservative and causes many constraints that have always been considered competitive to become non-competitive.
The ECI was designed based on concepts from the Herfindahl-Hirschman Index (HHI), a metric used by the Dept. of Justice when evaluating market concentration.
Prior to NPRR469, the ECI had been calculated using a unit’s market share based on the unit’s HSL times its shift factor relative to a constraint.
NPRR469 changed the ECI calculation to compute a unit’s market share based on the HSL times the shift factor squared.
This change introduced a significantly conservative bias in the ECI methodology which inflates the market share of higher shift factor units.
NPRR520 inherited the language in NPRR469.

## Slide 6: ECI Calculation Prior to NPRR469/520
 | HSL | SF | Eff Cap | Market Share | ECI
Unit 1 | 650 | 0.1 | 65 | 34.76 | 1208.21
Unit 2 | 400 | 0.08 | 32 | 17.11 | 292.83
Unit 3 | 550 | 0.05 | 27.5 | 14.71 | 216.26
Unit 4 | 350 | 0.06 | 21 | 11.23 | 126.11
Unit 5 | 250 | 0.05 | 12.5 | 6.68 | 44.68
Unit 6 | 100 | 0.08 | 8 | 4.28 | 18.30
Unit 7 | 400 | 0.03 | 12 | 6.42 | 41.18
Unit 8 | 100 | 0.09 | 9 | 4.81 | 23.16
Total |  |  | 187 | 100 | 1971

## Slide 7: ECI Calculation After NPRR469/520
 | HSL | SF^2 | Eff Cap with SF^2 | Market Share | ECI with SF^2
Unit 1 | 650 | 0.01 | 6.5 | 46.00 | 2116.13
Unit 2 | 400 | 0.0064 | 2.56 | 18.12 | 328.24
Unit 3 | 550 | 0.0025 | 1.375 | 9.73 | 94.69
Unit 4 | 350 | 0.0036 | 1.26 | 8.92 | 79.52
Unit 5 | 250 | 0.0025 | 0.625 | 4.42 | 19.56
Unit 6 | 100 | 0.0064 | 0.64 | 4.53 | 20.52
Unit 7 | 400 | 0.0009 | 0.36 | 2.55 | 6.49
Unit 8 | 100 | 0.0081 | 0.81 | 5.73 | 32.86
Total |  |  | 14.13 | 100 | 2698

## Slide 8: In Addition…
There is precedent for a 2,500 ECIT2 value.
  Since nodal go-live, the “competitive” constraints have been set as the 2010 zonal CSCs and CREs.
  Section 3.19.5, Daily Constraint Competitiveness Test, in the protocols since nodal go-live but will be removed with NPRR520 implementation, changes the treatment of the CSCs or CREs to non-competitive constraints if the ECI on the import side of the CSC or CRE is greater than 2,500.
The language in NPRR520 gives the IMM more leeway in overriding any ECI determination.
  “The IMM may designate any constraint as a Competitive Constraint or a Non-Competitive Constraint. ERCOT shall provide notice describing any such designation by the IMM. The notice shall include an effective date, justification for the constraint designation by the IMM and the duration for which the IMM designation will be applied. Any such designation from the IMM shall override the competitiveness status determined by the SCED CCT for the dates for which the IMM override is effective.”

## Slide 9: Conclusion
WMS members, on a split vote (56.7% FOR, 43.3% AGAINST and 2 abstentions), endorsed the threshold value of ECIT2 at a level of 2,000 in order to be “conservative”.
Detailed scenario analysis conducted after WMS led to discovery of the combined effect of applying the conservative ECIT2 parameter to the conservative CCT methodology. The result is many historically competitive constraints being deemed non-competitive (the most obvious are WN and NH).
We don’t believe the WMS members fully appreciated the conservative design elements already in the CCT methodology at the time of the vote on ECIT2.
An ECIT2 value of 2,500 allows NPRR520 to achieve the appropriate balance between protecting against local market power and meeting its objective of reducing chronic over-mitigation.