## Slide 1: RARF Data Completion Project
Woody Rickerson
ROS/WMS Update
June 2013

## Slide 2: RARF = Resource Asset Registration Form
The RARF is used to collect power system modeling data, as well as Registration data, from Resource Entities for the equipment they own. The data is used in various ERCOT models such as those used for real time operations, market management, CRR, Transmission Planning, System Protection, and Dynamics.
Changes to the RARF are submitted into the NOMCR modeling process by ERCOT.

## Slide 3: Brief History and Future of RARF
  Pre-Nodal History
  The RARF was established in 2007 to register resource assets required for the Nodal Market.
  ERCOT Nodal Project collaborated with Nodal Advisory Task Force in the development of the process to collect Resource data and the RARF was approved as the collection tool.
  Nodal Market implementation required ERCOT to create Network Operational Model Change Requests (NOMCR) on behalf of Resource Entities.
  Through and after Nodal Market Implementation, Resource asset requirement changes related to approved NPRRs, ERCOT and TSP operational and planning needs drove the release of revisions to the RARF.

## Slide 4: Brief History and Future of RARF
  RARF releases since Nodal Go-Live in November 2010:
    RARF 4.0 - RARF version at Nodal Go-Live.
    RARF 5.0 - March 2012.
      Implementation of NPRR regarding Governor parameters.
      Market’s need to model more details of WGRs.
      Implementation of Aggregated Generation Resources.
      Market entry of transmission connected Solar.
      Addition of planning data requested by TSPs and ERCOT.
      Separation of Form by Resource Type and format redesign.
    RARF 5.1 - June 2012.
      Release of updated business rules for testing registered data to report back to Resource Entity.
      Fall of 2012: Workshops and Notices regarding completion of RARF 5.1 data.

## Slide 5: Brief History and Future of RARF
  Today :
  Fall of 2012: Recognition by ERCOT and Stakeholders the need for review of the complexity of planning data.
  RARF Data Completion Project – scheduled to be complete in November 2013.
  Wind Resource Form update to implement NPRR 425.

## Slide 6: Current State of the RARF
Starting Numbers (mid-May)
There are 258 power plant RARFs providing data for ~650 individual units
125 RARFs, representing 64% of ERCOT MW capacity, are complete with no validation errors
133 are missing some data
  Average number of data elements missing per incomplete RARF is ~20
Total number of missing data elements is ~2700
  Some of the missing data will be the same for multiple RARFs
Types of Data that are missing
  Data needed for short circuit studies
  Data needed for Dynamic modeling
  Temperature-related operational data

## Slide 7: Reasons for Missing Data
New Technologies – Some existing RARF parameters don’t fit new technologies (e.g. wind, solar). Owners do not know how to translate their data.
Cost – Cost to test a turbine is around $25K (based on estimate provided by GE). Some owners have stated that testing costs are not justifiable for their units. This is especially true for older units.
What’s wrong with what you have? Cases are still being built using old data. However, ERCOT and TSPs are concerned the data is no longer valid for the existing system.
History – RARF data had been traditionally provided by the TSP portion of the old integrated utilities. When the utilities restructured, that expertise left the generating companies and the separate TSPs in some cases question the validity of some data now provided by the Gencos.

## Slide 8: Problem Approach
Six-Month Project that began earlier this month. REs will be contacted in stages based on interconnecting TSP.
At least two workshops are anticipated during the next six months.
ERCOT has contracted with Siemens to propose data to populate the missing RARF fields using existing data using sources currently available to ERCOT and Siemens.
REs will have final approval of proposed new data. The RARF submittal will continue to be the REs submittal.
Utilizing an industry expert will aid in acceptance of data by both TSPs and REs. This approach is similar to what was used for the Voltage Ride Through (VRT) study.
Formulas and processes used to obtain data will be retained and documented as a project deliverable.
Existing data validation processes will keep the RARF content current once it is populated.

## Slide 9: Siemens Team
Nelson Bacalao, PhD, Senior Manager of Consulting, with Siemens PTI in Houston, Texas, will be the Project Manager for the study. Dr. Bacalao is an Electrical Engineer with a Master of Science degree in electrical engineering, a Master of Business Administration degree, and a Ph.D. degree in power systems. With over 30 years of professional experience, Dr. Bacalao has extensive worldwide experience in evaluating the performance and planning of transmission systems in both in developed and developing Corporate Background and Experience Siemens Industry, Inc. – Siemens Power Technologies International P032-13 – Resource Asset Registration F 3-8 orm (RARF) Services Copyright © 2012 Siemens Industry, Inc. All Rights Reserved. countries. His experience is centered in system studies and economic evaluation, including recently advising TSPs in the evaluation of the CREZ transmission expansion plan in Texas as well as in the evaluation of several interconnections of large wind farms to the ERCOT 345 kV system.
John Hanson, PE, Principal Consultant, with Siemens PTI in Houston, Texas. Mr. Hanson is a licensed Professional Engineer (PE) in Texas with 40 years of experience in the power systems industry. His experience covers a wide range of topics including power plant engineering instrumentation and control, transmission planning, system protection, EMTP studies, power flow analysis, short circuit analysis, dynamic stability analysis, voltage stability analysis, and geomagnetic induced current analysis. Mr. Hanson joined Siemens PTI in 2012.
Alicia Dortch, Senior Consultant with Siemens PTI in Houston, Texas, has a solid foundation in electric system operations and transmission system planning. Her 8 years of professional experience covers an extensive range of topics including transmission planning, power flow analysis, dynamic stability analysis, and voltage stability analysis. She has performed numerous power system analyses and simulation studies for system expansions and new system interconnections. She complements her technical skills with experience in NERC and FERC compliance and audit preparedness.
Jack Henry, PE, Senior Staff Consultant, with Siemens PTI in Houston, Texas. Mr. Henry is a licensed Professional Engineer (PE) in Texas with more than 30 years of extensive power systems industry experience in the transmission and generation sectors. He has a solid power system background in transmission planning and distribution, including power flow analysis, post-transient analysis, voltage stability analysis and dynamic stability analysis. His expertise also includes modeling and simulation of transmission projects for long-term development plans, real-time generation operations with respect to the integrated transmission system, and day/month-ahead transmission and generator strategic operations planning integrating real-time and planned transmission maintenance information. Mr. Henry joined Siemens PTI in 2010 and has been conducting power system studies, power system modeling, and generator interconnection assessments, providing engineering solutions for the power industry.

## Slide 10: Monthly Progress Reports
June Upate
Resource Entities with Complete RARF
Capacity Percentage Represented with Complete RARF
Percentage of RARF Data Missing
Chart: 
| REs with complete RARF | REs with Missing Data
 | 64 | 87
Chart: 
| Complete Data | Missing Data
 | 12658 | 2665
Chart: 
| Capacity with complete Rarf | Capacity with incomplete Rarf
 | 63653 | 28798