## Slide 1: Proposed Procurement Methodology for Emergency Response Service

## Slide 2: Purpose for Revised Procurement Methodology
Methodology Proposed for the following:
Remove as much of the subjectivity as possible from the current ERCOT procurement process
Create a methodology that provides the appropriate price signals during higher risk time periods during the ERS contract year
Establish known procurement parameters for ERS Providers
This proposal is being developed with the intent that market clearing prices will apply for all ERS products

## Slide 3: ERS Time period Capacity Demand Curve
MW
ERS Capacity Price
[$/MW per Hr]
ERS Time Period Price Cap
ERS Minimum Capacity Requirement
ERS Capacity Demand Curve
ERS Maximum Capacity Requirement
Time Period Spend Cap
Adjusted ERS Time Period Price Cap

## Slide 4: Proposed ERS Time Period Price Cap
ERS Time Period Price Cap Option
  During contract terms and time periods when the TDSP Load Management Programs are available (currently BH2 and BH3 for the Jun-Sept contract period) use the greater of cost caps set by the PUCT for the TDSP LM programs or the historical cost of Ancillary Services
  During all other contract terms and time periods use historical cost of Ancillary Services
    10-Minute ramp ERS products use 3 year average for RRS
    30-Minute ramp ERS products use 3 year average for Non-Spin

## Slide 5: Establishing ERS Time Period Max Capacity Requirements
ERS Time Period Capacity Requirements:
  Using most current SARA determine ERS Capacity needed for “Capacity Available for Operating Reserves” (Extreme Load/Typical Generation Outages) + ERS Capacity = 2300 MWs, but not less than 500 MWs
  If “Capacity Available for Operating Reserves” (extreme load/Typical Gen Outages) > 2300 use the following:
    500 MWs if Time Period is declared by ERCOT as on-peak time period
    0 MWs if declared as off-peak time period
Feb-May
Jun-Sep
Oct-Jan

## Slide 6: Time Period Spend Constraint
Annual cost cap limit is set at $50 million per year
Applying Spend Constraint
  Create initial time period ERS Procurement assessment prior to beginning of the ERS Budget year
  Allocate $50 million across all time periods
Feb-May
Jun-Sep
Oct-Jan
A B C D E F
A = ERS Time Period Max Cap. Req. from page 7
B = Hours in each ERS Time Period
C = ERS Time Period Price cap from pages 4-6
D = Spend based on Max cap @ price cap
E = Time Period Spend allocation; D/$114M
F = ERS Time Period Spend Constraint; E* $50M

## Slide 7: Other
  Money not spent under the contract period cost cap will be added to next contract period within the same ERS budget year.
  Money not spent at the end of the last contract period in the ERS Budget year will not be carried forward into the next ERS budget year
  Only procure for renewal contract periods if money available
  Offers for each time period will be flagged as either 10-Minute or 30-Minute ERS offer
  Max offer cleared pertaining to 10-Minute flagged offer will set the clearing price for 10-Minute ERS
  Max offer cleared pertaining to 30-Minute flagged offer will set the clearing price for 30-Minute ERS

## Slide 8: Weather Sensitive ERS & WEH Time Period
BH2 and BH3 Time Periods
  Weather Sensitive ERS will be procured under the BH2 and BH3 ERS Capacity Demand Curves for Jun-Sep SCT only
Weekend/Holiday Peak Time Period (WEH)
  Time Period Price cap = greater of TDSP LM program cost cap or 3 year average of NSRS for applicable hours
  Max Capacity requirement = Declared an On peak time period where SARA or 500 MWs would apply
  New Time Period added to Time Period Spend Constraint allocation table
  All ERS products will be eligible to offer into WEH