## Slide 1: NPRR 555 (Loads in SCED 1.0)
July 10, 2013
WMS: NPRR 555
Paul Wattles, Sai Moorty
ERCOT Market Design & Development

## Slide 2: NPRR 555: Loads in SCED 1.0
NPRR 555 represents ERCOT’s effort to find a way for DR to contribute to price formation, with potential for implementation by Summer 2014
WMS: NPRR 555
July 10, 2013

## Slide 3: Timeline
To meet summer 2014 goal, ERCOT will need to meet following market rules timeline:
  May 28 Concept doc distributed to TAC/WMS/DSWG
  May 31 DSWG discussion
  June 6 TAC introduction to concept
  June 10 Loads in SCED Workshop
  June 12 WMS discussion
  June 27 NPRR draft posted
  June 28 DSWG review of draft NPRR
  July 3 NPRR 555 filed (ERCOT sponsored) with preliminary IA
  July 8 DSWG Subgroup – deep dive review
  July 10 WMS NPRR discussion (possible vote)
  July 18 PRS NPRR discussion (possible vote)
  Aug. 14 WMS redux (possible vote)
  Aug. 22 PRS NPRR discussion (vote)
  Sept. 5 TAC NPRR discussion (vote)
  Sept. 17 BOD NPRR discussion (vote)
WMS: NPRR 555
July 10, 2013

## Slide 4: High-level summary
WMS: NPRR 555
July 10, 2013
Eligibility to participate: LSE QSEs representing Load Resources capable of following 5-minute SCED base point instructions
  Existing or new single-site Controllable Load Resources (CLRs)
    SCED qualification will be a new attribute for redefined CLR
  Aggregate Load Resources (ALRs) composed of multiple sites within single ERCOT Load Zone (subset of CLR)
    New interface will allow QSEs to maintain ALR populations
Will not support direct participation by third-party DR QSEs
Will not support DR with temporal constraints or block energy bids
  If LR’s bid is on the margin, base point instructions could require LR to move up or down incrementally every 5 minutes to any level between its LPC and MPC
  SCED will honor LR’s telemetered ramp rates

## Slide 5: High-level summary (cont.)
WMS: NPRR 555
July 10, 2013
QSEs with LRs in SCED will submit Bids to buy (not Offers to sell)
Bids will reflect LR’s willingness to consume “up to” a specified five-minute Load Zone LMP
May be a curve or a MW bid at single strike price
  Bid curve option could allow the QSE to submit bids with different strike prices for separate loads within the LR
Bid will modify the SCED demand curve and have ability to set price
  SCED Generation to be Dispatched (GTBD) will be adjusted to accommodate LR participation
  This will ensure proper price formation and reduce the likelihood of oscillating dispatch instructions
This creates settlement outcomes equivalent to the “volumetric flow” LMP minus G methodology endorsed by TAC, while avoiding need for ERCOT to “send back” the DR value to the LSE

## Slide 6: High-level summary (cont.)
WMS: NPRR 555
July 10, 2013
LR benefits and opportunity:
  Avoided cost of consumption above specified price
  Price certainty due to ERCOT dispatch
  Eligibility to provide Non-spin
Market impacts:
  LR Bids may set price in the RTM
  No make-whole payments
  No load ratio share uplifts to market for DR value
SCED will dispatch LRs for power balance and congestion management using the applicable Load Zone Shift Factor

## Slide 7: High-level summary (cont.)
Eligible LRs may also participate in Non-spin Reserves
  For Offline Non-Spin, energy Bids ≥$180 will need to be released to SCED within 20 minutes following dispatch, similar to Generation Resources providing Offline Non-spin
  For Online Non-Spin, energy Bids ≥$120 will need to be active in SCED for all intervals that the LR is obligated in Non-Spin
  Bids from LRs providing Non-Spin capped at the System Wide Offer Cap
NPRR 555 also proposes that any CLR providing RRS also must be dispatched by SCED
WMS: NPRR 555
July 10, 2013

## Slide 8: High-level summary (cont.)
Implementation of Loads in SCED 1.0 is related to adoption of NPRR 532
  CPS Energy: LR Participation in Non-spin
For ALRs, participation in SCED and Non-spin are both contingent on validation by ERCOT of the QSE’s telemetry at time of LR qualification, and spot-validation thereafter
  OBD associated with NPRR 532 describes this process
Telemetry from LRs providing Non-Spin must include Scheduled Power Consumption and SPC+2 to allow baseline-style M&V
  M&V for LR in SCED for energy only does not require use of SPC and SPC+2
All members of ALR must have revenue-grade premise level 15-minute interval metering
  Via ESI ID or NOIE meter data submission process similar to ERS
WMS: NPRR 555
July 10, 2013

## Slide 9: Changes to Load Resource definitions
Loads in SCED NPRR redefines Controllable Load Resource (CLR)
CLRs will provide Regulation, RRS (as non-UFR type resource) & Non-Spin
RRS and Non-Spin from CLR will be deployed via economic dispatch of DR capacity via SCED
  CLR will have RTM Energy Bid that covers the RRS and/or Non-Spin capacity released to SCED
  Also can optionally bid additional DR capacity for SCED dispatch
SCED will only consider CLR for dispatch if its telemetered Resource status indicates it is On-Line
  Must be On-Line if carrying AS responsiblity
WMS: NPRR 555
July 10, 2013

## Slide 10: CLR (cont.)
CLR qualifications:
  To qualify for providing Regulation and RRS, tested for ability to provide Primary Frequency Response (no change from today)
  To provide RRS, Non-Spin or Real-Time energy only, tested for ability to follow SCED Base Point Instructions
  To provide Non-Spin or Real-Time energy only, not required to provide Primary Frequency Response
Non-Controllable Load Resource (NCLR)
  NCLR participation going forward limited to UFR-type Load Resources providing RRS
WMS: NPRR 555
July 10, 2013

## Slide 11: Miscellaneous
No change to existing participation in RRS by UFR-type Load Resources
  UFR-LR-RRS may still be deployed manually in EEA 2
  Prices will be at SWCAP any time this happens because Gen-RRS is deployed first
No change to existing ERS
Participation Scenarios for LRs were presented as part of DSWG slides on June 28:
  http://www.ercot.com/calendar/2013/06/20130628-DSWG
WMS: NPRR 555
July 10, 2013

## Slide 12: Outstanding Issues (will/may require Comments)
Configurable parameters for Base Point Deviations
  ERCOT looks to MPs to identify meaningful performance metrics that don’t discourage SCED participation
  Should they be the same for LRs with AS responsibility and those with ‘pure SCED’ (energy only) Bids?
Base Point Deviation treatment of settlement intervals for LRs with telemetry status of OUTL for a portion of the interval
Posting requirements and protected information status for RTM Energy Bids
Physical Responsive Capability: should it include all RTM energy bids, or just those with AS responsibility?
Other miscellaneous tweaks and cleanup
WMS: NPRR 555
July 10, 2013

## Slide 13: Questions?
WMS: NPRR 555
July 10, 2013
ON
OFF