## Slide 1: Settlements Analysis due to SFT Deration Issue
Matt Tozer / Pam Shaw
COPS
August 2013

## Slide 2: Issue Overview
A defect was introduced into the Day Ahead Market Simultaneous Feasibility Test (SFT) process with NPRR 322 (Real-Time PTP Option Modeling)
  Issue was in ERCOT systems from OD 2-14-2013 through 6-13-2013
Impact to Settlements from defect was the CRR SFT Violated Constraint bill determinant (CRRSFTVIOL) was not created for all violated constraints or had the incorrect value
  CRRSFTVIOL is used to calculate the Deration Factor (DRF) which is used in the calculation of the CRR Derated Amount
  CRRs can be “derated” when certain paths are oversold in the CRR Auction
  Only CRRs that have a source and/or sink at a Resource Node Settlement Point can be derated
Issue was uncovered by ERCOT staff when investigating the May 2013 CRR Short Fall

## Slide 3: Issue Impact
A portion of CRRs that had a source or sink at a resource node were not derated and should have been
  i.e. Certain CRRs were overvalued in DAM settlements
Also, for most operating days, Shortfall Charges to CRR Owners were higher than they should have been and Balancing Account Deposits were lower than they should have been
  Shortfall Charges are incurred when there is not enough Congestion Rent collected in an hour to cover CRR payments
End of month impact resulted in:
  lower than appropriate monthly refund to short paid CRR Owners
    For months where short paid CRR owners were not fully funded (for example, April and May)
  or lower than appropriate credits to QSEs with Load
    For months where short paid CRR owners were fully funded (for example, February, March and June)

## Slide 4: Results of the Analysis – Resettlement Days
Per Nodal Protocol Section 9.2.5, DAM Resettlement Statement
  ERCOT shall issue a DAM Resettlement Statement for a given DAM due to error in data other than prices when the total of all errors in data other than prices results in an impact greater than 2% of the total payments due to ERCOT for the DAM, excluding bilateral transactions.
Analysis Determined that 14 Operating Days met the 2% threshold
  The last Resettlement (for Operating Day 5-22) was posted on July 29th
Operating Days Requiring DAM Resettlement
4/4/2013
4/30/2013
5/6/2013
5/9/2013
5/10/2013
5/12/2013
5/16/2013
5/17/2013
5/18/2013
5/19/2013
5/20/2013
5/21/2013
5/22/2013
6/5/2013

## Slide 5: Results of the Analysis – Data Impacts & Next Steps
CRRSFTVIOL Bill Determinants that were missing or had incorrect values were imported into Lodestar for all affected Operating Days.
  If Operating Days other than those that met the 2% threshold are subsequently resettled, the corrected data will be used in settlements
The updated data for all affected operating days was made available in SID extracts on July 18th
April and May 2013 Balancing Account will have to be resettled. There are no planned dates as of yet. Market Notices will be sent out.

## Slide 6: Results of the Analysis – Dollar Impact
Below are the dollar impacts if 2% Days are Resettled

## Slide 7: Results of the Analysis – Dollar Impact
Below are the dollar impacts if all Days are Resettled

## Slide 8: Results of the Analysis – Dollar Impact
Below is the difference between Resettling all days versus just 2% days

## Slide 9: Questions?
Any Remaining Questions?