| PGRR Number | 031 | PGRR Title | Implement 95% Facility Rating Limit in the Planning Criteria |
| --- | --- | --- | --- |

| Date | 09/10/2013 |
| --- | --- |

| Submitter’s Information |
| --- |
| Name | Brad Myers, Jeff Billo, Mike Holland, Kenneth Bowen |
| E-mail Address | blmyers@aep.com, jeff.billo@ercot.com, michael.holland@oncor.com, kbowen@cpsenergy.com |
| Company | AEP, ERCOT, ONCOR, CPS Energy |
| Phone Number | 918-599-2690 |
| Cell Number |  |
| Market Segment | Investor Owned Utility (IOU) |

Comments

AEP concurs with the OPSTF analysis and recommendations identifying the need for assessment of the transmission system at 95% of facility loading and the need to introduce reasonable additional margin into the planning timeline for the reasons stated in the PGRR’s Business Case.  Additionally AEP would like to thank ERCOT for drafting 031PGRR-01 and for the opportunity to offer the following alternative implementation of PGRR031 aimed at performing system analysis and enabling project justification at the ‘95% Facility Rating Limit’ external to, and without modification to, the existing Planning Criteria.

- AEP is concerned with the compliance exposure incurred by the broad application of the [proposed] reduced facility rating limit imposed by modifications to the Reliability Performance Criteria.

- AEP submits that the Reliability Performance Criteria can remain the same, but can be appended to trigger project initiation, endorsement, and construction based on 95% loading of transmission facilities.

Revised Cover Page Language

| Planning Guide Section Requiring Revision | 4.1, Introduction 4.1.1.2, Reliability Performance Criteria |
| --- | --- |

Revised Proposed Guide Language

4.1	Introduction

(1)	ERCOT employs both reliability criteria and economic criteria in evaluating the need for transmission system improvements.  The economic criteria are included in Protocol Section 3.11.2, Planning Criteria.  This Planning Guide provides the reliability criteria.

(2)	The ERCOT System consists of those generation and Transmission Facilities (60 kV and higher voltages) that are controlled by individual Market Participants and that function as part of an integrated and coordinated system.

(3)	To maintain reliable operation of the ERCOT System, it is necessary that all stakeholders observe and subscribe to certain minimum planning criteria.  The criteria set forth in this Section 4.1 constitute the aforementioned minimum planning criteria.  Tests outlined herein shall be performed to determine conformance to these minimum criteria; however, ERCOT recognizes that events more severe than those outlined in these criteria could cause grid separation and other tests may also be performed.

(4)	The complexity and uncertainty inherent in the planning and operation of the ERCOT System make exhaustive studies impracticable; therefore, to gain maximum benefit from the limited number of tests performed, the selection of the specific tests and the frequency of their performance will be made solely upon the basis of the expected value of the reliability information obtainable from the test.

(5)	ERCOT shall perform steady-state and dynamic analyses appropriate to ensure the reliability of the ERCOT System and identify appropriate solutions.

(6)	Each Transmission Service Provider (TSP) will perform steady-state, short circuit, and dynamic analyses appropriate to ensure the reliability of its portion of the ERCOT System and implement appropriate solutions to meet the reliability performance criteria in this Section 4.1.

(7)	The base cases created by the Steady-State Working Group (SSWG) and System Protection Working Group (SPWG) are available for use by Market Participants.

(8)	If a TSP has its own planning criteria in addition to those defined in this Planning Guide, the TSP shall provide documentation of those criteria to ERCOT.  ERCOT shall post the documentation on the Planning and Operations Information website.  The TSP shall notify ERCOT of any changes to their planning criteria and provide revised documentation within 30 days of such change.

4.1.1.2	Reliability Performance Criteria

(1)	The following performance criteria (summarized in Table 1, ERCOT-specific Reliability Performance Criteria, below) shall be applicable to planning analyses in the ERCOT Region:

(a)	With all Facilities in their normal state, following a common tower outage, or the contingency loss of a single generating unit, transmission circuit, transformer, shunt device, or FACTS device, all Facilities shall be within their applicable Ratings, the ERCOT System shall remain stable with no cascading or uncontrolled Islanding, and there shall be no non-consequential Load loss.

(b)	With any single generating unit unavailable, followed by Manual System Adjustments, followed by a common tower outage or the contingency loss of a transmission circuit or transformer, all Facilities shall be within their applicable Ratings, the ERCOT System shall remain stable with no cascading or uncontrolled Islanding, and there shall be no non-consequential Load loss.

(c)	With any single 345/138 kV transformer unavailable, followed by Manual System Adjustments, followed by a common tower outage, or the contingency loss of a single generating unit, transmission circuit, transformer, shunt device, or FACTS device, all Facilities shall be within their applicable Ratings, the ERCOT System shall remain stable with no cascading or uncontrolled Islanding, and there shall be no non-consequential Load loss.  An operational solution may be planned on a permanent basis to resolve a performance deficiency under this condition.

| Initial Condition | Event | Facilities within Applicable Ratings and System Stable with No Cascading or Uncontrolled Outages | Non-Consequential Load Loss Allowed |
| --- | --- | --- | --- |
| 1 | Normal System | Common tower outage; or Contingency loss of one of the following: 1. Generating unit; 2. Transmission circuit; 3. Transformer; 4. Shunt device; or 5. FACTS device | Yes | No |
| 2 | Unavailability of a generating unit, followed by Manual System Adjustments | Common tower outage; or Contingency loss of one of the following: 1. Transmission circuit; or 2. Transformer | Yes | No |
| 3 | Unavailability of a 345/138 kV transformer, followed by Manual System Adjustments | Common tower outage; or Contingency loss of one of the following: 1. Generating unit; 2. Transmission circuit; 3. Transformer; 4. Shunt device; or 5. FACTS device | Yes | No |

Table 1: ERCOT-specific Reliability Performance Criteria

(2)	The minimum performance criteria requires Transmission Facilities to remain less than or equal to 100% of their applicable Ratings.  TSPs and ERCOT, however, shall assess system performance and initiate and endorse projects for Facilities with loading greater than or equal to 95% of their applicable Ratings under normal system conditions and under the contingency events identified in paragraph (1) (a) above, and Line 1 of Table 1.

(a)	For normal system conditions and the conditions described in paragraph (1) (a) and Line 1 of Table 1, TSPs and ERCOT may elect not to initiate and endorse projects for Facilities loaded between 95% and 100% of their applicable Ratings if the loading on those Facilities is not expected to significantly change within the six-year planning horizon.  Examples of such Facilities may include, but are not limited to, transmission circuits that are radial to Generation Resources where the maximum output of the Generation Resources is not expected to increase within the six-year planning horizon and transmission circuits that are radial to Load that is not expected to significantly increase within the six-year planning horizon.

(3)	ERCOT and the TSPs shall endeavor to resolve any performance deficiencies as appropriate.  If a Transmission Facility improvement is required to meet the criteria in this Section 4.1.1.2, but the improvement cannot be implemented in time to resolve the performance deficiency, an interim solution may be used to resolve the deficiency until the improvement has been implemented.

(a)	Assessments, including proposed solutions, associated with criteria in paragraph (1)(c) and line 3 of Table 1 shall be completed by no later than May 1, 2015.

(b)	Assessments, including proposed solutions, associated with planning for Facilities loaded between 95% and 100% of their applicable Ratings, per the criteria in paragraph 2 shall be completed no later than [36 months after PGRR031 is Board of Director approved].

# Comments

Extracted ‘system reliability’ may be applicable to both versions.

Extracted ‘system reliability’ may be applicable to both versions.

Change applicable to both versions.