## Slide 1: PDCWG Report to ROS
David Kee Chair
CPS Energy
Sydney Niemeyer Vice Chair
NRG Energy

## Slide 2: October Meeting
Met Oct 22, 2013
  18 members representing 14 companies as well as ERCOT & TRE.
NPRR 486/ SCR 773 – update
NPRR 568 & 573
Event review
GREDP update
Frequency Control Report Oct 2013
  Significant Control Event

## Slide 3: NPRR 486/ SCR 773 update
Focus on development of metrics to track the regulation bias
Generator Startup process is likely next to be reviewed
Integral ACE was discussed as a candidate for control feedback to SCED
There was a consensus that the method recommended by NPRR 486 will not work. NPRR is likely to be withdrawn.

## Slide 4: NPRR 568 & 573
NPRR 568 was reviewed and it was determined that the proposed revisions do not impact reliability.
  Questions were raised
    “will the incentives align with ERCOT operator actions?”
    “what is an emergency condition based on?”
NPRR 573 was submitted by ERCOT to address issues indirectly raised by NPRR 568.
  PDCWG submitted comments to NPRR 573

## Slide 5: Event Review
PDCWG Reviewed 4 events
  Event resulted in good system frequency performance with few poor performers identified
  Non Frequency responsive RRS providers were noted and ERCOT will follow up with QSEs regarding their performance

## Slide 6: GREDP
All Conventional Generators passed metric
Increase in Wind Resource control performance
  With CREZ lines being energized there are less curtailments
  Scores have stayed consistent
  Signals better control of Wind Resources that are being curtailed

## Slide 7: Focus for 2013
Formal & documented review/report of frequency responsiveness for Power Augmentation on Combined Cycle Resources (train not individual unit)
Review regulation/GTBD deployment effectiveness (SCR 773)
  Study the impact of HSL/basepoint/generation deviation on compliance and reliability
  Develop metrics to track regulation deployment effectiveness
Pilot of fast frequency response – characterize & create evaluation process
Fast Responding Regulation – NPRR581 (new)
Ancillary Service Overhaul
  No performance required for nonpayment (freq. resp AS)
Responsive Reserve requirements, qualification vs. compliance. (10min vs. 16 second)
Standardized/consistent metrics for PFR analysis (BAL001-TRE).
  Work on realistic measurement of combined cycles
Standardized/reasonable expectations for extreme events (2750MW or larger lost) – driven by NERC.
ERS impact review with appropriate ERCOT group. Target Q1-2014
PMU data understanding of implications
Red = Work on going
Check = completed goal

## Slide 8: ERCOT Frequency Control Report October 2013
Sydney Niemeyer NRG Energy
November 11, 2013

## Slide 9: Notes
Time error values from NRG True Time device can be slightly different from ERCOT’s Time Error but the daily delta times should be accurate.

## Slide 10: Ercot frequency control
BAL-001 CPS 1 & 2 Performance, RMS 1 and Frequency Profile

## Slide 13
CPS1 12 Month Rolling Average = 166.79

## Slide 18
60.015 <= HZ < 60.020

## Slide 20: ERCOT Time error and time correction
Time Error History

## Slide 21: Time Error Corrections
Fourth consecutive month with no manual Time Error Correction.
Prior to July 2013 there have been 3 months with no manual Time Error Corrections. This is between Sept 2001 and June 2013, almost 12 years.
  One in 2004, 2009 and 2011.

## Slide 25
Time Correction History

## Slide 28: Ercot primary frequency response performance
BAL-003-1 Interconnection Frequency Response and Bias Measure.

## Slide 29
ERCOT Primary Frequency Response – BAL-003-1
2014 Bias and Frequency Response Measure Page 1

## Slide 30
ERCOT Primary Frequency Response – BAL-003-1
2014 Bias and Frequency Response Measure – Page 2

## Slide 31: Ercot total energy and wind production
October Total ERCOT Energy and Total Energy Production from Wind Resources.

## Slide 35
Questions?