## Slide 1: Annual TAC Review of the Market Impacts of Reliability Unit Commitments
ERCOT Market Analysis
Analysis of 1/1/13 through 12/31/13

## Slide 2: Summary of 2013 compared to 2012
Instructed Effective RUC Hours have increased
  267 hours in 2012 versus 653 hours in 2013
  Most of the increase has been from Congestion
    86 hours in 2012 to 448 hours in 2013
Hours with offer not at SWCAP has reduced significantly
  74.5% of RUC hours in 2012 to 16.9% of RUC hours in 2013
Possible increase in Peaker Net Margin after relaxing LSL of RUC Committed Resources has increased substantially
  $21.41/MW-year in 2012 to $5,825/MW-year in 2013
  RUC Generation for capacity reasons (insufficient HASL) on 1 day (10/1/2013) contributed to majority of this increase

## Slide 3: RUC Commitments and Offers
653 Instructed Effective RUC Unit Hours in 2013
  448 hours (68.6%) for Congestion
  116 hours (17.8%) for Voltage/Reactive Support
  89 hours (13.6%) for Capacity
Energy Offer Curve Compliance
  639 Instructed Effective RUC Unit Hours were required to have an Energy Offer Curve priced at SWCAP for MW above LSL
  531 hours (83.1%) properly priced at SWCAP above LSL
  82 hours (12.8%) not priced at SWCAP above LSL with less than an hours notice to update
  26 hours (4.1%) not priced at SWCAP above LSL with more than an hours notice to update

## Slide 4: RUC Effective MWh by Month

## Slide 5: RUC Type Units Hours by Month (2013)

## Slide 6: RUC Type Units Hours by Month (2012)

## Slide 7: RUC Committed Resources Dispatched for Capacity
40.4 hours (6.6%) were dispatched above LSL for capacity
    611.7 Effective RUC Unit Hours
      Difference between this number and the 653 is a result of Resources starting up, shutting down, or still being Off-Line for some portion of the RUC committed hours
  LMP<=System Lambda+2 and BP>=LDL+2 used to determine dispatch for capacity
    40.3 hours (6.6%) had prices below $100
    0.1 hours (0.01%) had prices between $100 & $500
    0 hours (0%) had prices greater than $500
Notes: RN LMP = System lambda & BP> LDL => Resource is moved up for capacity since there is no congestion
RN LMP > System lambda & BP> LDL => Resource can contribute to reducing congestion and hence could be moved up for transmission.

## Slide 8: 0 to LSL Energy from ONRUC Resources
611.7 Effective RUC Unit Hours
  Average ONRUC LDL is 121 MW, LSL is 118 MW, BP is 125 MW, HSL is 275 MW
  520.5 hours (85.1%) are at or below LDL (BP-LDL<2MW)
    Average ONRUC LDL is 112.5 MW, LSL is 111.7 MW
  91.3 hours (14.9%) are above LDL for transmission or capacity
    Average ONRUC LDL is 192.0 MW, LSL is 176.7 MW
471.7 Effective RUC hours with at least one ONRUC status
  Average system total ONRUC capacity for only these hours:
    LDL is 164 MW
    LSL is 160 MW
    HSL is 364 MW
    BP is 169 MW
‘Effective RUC Unit Hours’ is SCED duration, summed up to hour level, for each RUC committed Resource when it was On-Line. ‘Effective RUC Unit Hours’ considers multiple Resources committed for the same hour as different unit hours while ‘Effective RUC Hours’ considers it as single hour.

## Slide 9: Estimated PNM Impact of RUC Committed Resources
Month | Actual Incremental PNM | Incremental PNM Adder from Study
1 | 1,260 | 0
2 | 943 | 2
3 | 3,086 | 378
4 | 3,772 | 76
5 | 1,072 | 255
6 | 1,361 | 57
7 | 2,105 | 20
8 | 2,907 | 0
9 | 5,459 | 11
10 | 5,400 | 4,844
11 | 2,988 | 169
12 | 2,618 | 14
Total | 32,969 | 5,825
New PNM | 38,794 | 
  The monthly incremental Peaker Net Margin (PNM) was analyzed by relaxing the LSL to 0 for all RUC committed Resources and simulating the SCED solution
  The results indicate that the LSL of these Resources did not have a significant impact on the PNM for 2013 except for 1 day (10/1/2013)

## Slide 10: Conclusion
653 Instructed Effective RUC Hours
  of which only 89 hours were committed for capacity and
  Hours in which ONRUC resources were dispatched above LSL for capacity totaled 40.4 hours
EOC non compliance reduced considerably to 4.1%
Peaker Net Margin could increase by $5,825/MW-year if we remove the stranded 0-LSL energy from RUC Committed Resources

## Slide 11: Appendix

## Slide 12: Comparison of 2012 to 2013 (1 of 2)

## Slide 13: Comparison of 2012 to 2013 (2 of 2)

## Slide 14: RUC Committed Resources - Histogram of RUC BP

## Slide 15: RUC Committed Resources - Relationship to Real-time Prices
Chart: SCED System Lambda and Capacity Headroom
Notes: Offer floor could increase the system lambda for all intervals with Capacity Headroom <=0

## Slide 16: RUC Committed Resources - Relationship to Real-time Prices
Chart: SCED System Lambda and Capacity Headroom

## Slide 17: RUC Committed Resources - Relationship to Real-time Prices
Chart: SCED SYSTEM LAMBDA (< $500) vs RUC LSL MW

## Slide 18: RUC Committed Resources - Relationship to Real-time Prices
Chart: SCED SYSTEM LAMBDA (< $500) vs RUC Basepoint MW

## Slide 19: Estimated PNM Impact on 10/1/2013 (Total Impact of Day was $4,813/MW-year)

## Slide 20: HRUC Snapshot at 10AM on 10/1/2013 for Hours 1500 to 2200