| NPRR Number | 573 | NPRR Title | Alignment of PRC Calculation |
| --- | --- | --- | --- |
| Timeline | Normal | Action | Approved |
| Date of Decision | February 11, 2014 |
| Effective Date | March 1, 2014 for revisions to PRC1; upon system implementation for addition of new PRC2. |
| Priority and Rank Assigned | Priority – 2014; Rank – 1050 |
| Nodal Protocol Section Requiring Revision | 6.5.7.5, Ancillary Services Capacity Monitor |
| Market Guide Section(s) Requiring Revision | None. |
| Revision Description | This Nodal Protocol Revision Request (NPRR) aligns the Protocols with the current calculation used in the Energy Management System (EMS) to calculate Physical Responsive Capability (PRC), and adds capacity from Primary Frequency Response-capable Wind-powered Generation Resources (WGRs) to PRC. |
| Reason for Revision | This NPRR aligns the Protocol language with the current PRC calculation in the EMS, and modifies the PRC calculation to represent appropriate frequency-responsive WGRs. The original Nodal Market design documents required any capacity from WGRs and nuclear Generation Resources above their current output level to be excluded from the calculation of PRC in the EMS. NPRR076, Synchronization of Emergency Electric Curtailment Plan (EECP) Event Realignment, modified Section 6.5.7.5 to add an equation for the calculation of PRC. The equation that was added to the Protocols as a result of NPRR076 did not exclude unloaded WGR and nuclear Generation Resource capacity. However, no change was made to the EMS design calculation of PRC as a result of NPRR076. Therefore, this NPRR excludes WGRs and nuclear Generation Resources from the PRC calculation, with the exception of Primary Frequency Response-capable WGRs. |
| Credit Impacts | ERCOT Credit Staff and the Credit Work Group (Credit WG) have reviewed NPRR573 and do not believe that it requires changes to credit monitoring activity or the calculation of liability. |
| Procedural History | On 10/21/13, NPRR573 and an Impact Analysis were posted. On 11/5/13, Performance, Disturbance, Compliance Working Group (PDCWG) comments were posted. On 11/21/13, PRS considered NPRR573. On 12/18/13, a revised Impact Analysis was posted. On 12/19/13, PRS considered the 11/21/13 PRS Report and revised Impact Analysis for NPRR573. On 1/28/14, TAC considered NPRR573. On 2/11/14, the ERCOT Board considered NPRR573. |
| PRS Decision | On 11/21/13, PRS unanimously voted to recommend approval of NPRR573 as amended by the 11/5/13 PDCWG comments. All Market Segments were present for the vote. On 12/19/13, PRS unanimously voted to endorse and forward the 11/21/13 PRS Report and revised Impact Analysis for NPRR573 to TAC with a recommended priority of 2014 and rank of 1050. All Market Segments were present for the vote. |
| Summary of PRS Discussion | On 11/21/13, it was noted that the 11/5/13 PDCWG comments includes the capacity of frequency-responsive WGRs into the PRC calculation; that the conflict between the PRC calculation set forth in Section 6.5.7.5 and the EMS design calculation of PRC was discovered during the discussion of NPRR568, Real-Time Reserve Price Adder Based on Operating Reserve Demand Curve; and that further discussion regarding what should be included within the PRC calculation might be warranted outside consideration of NPRR573. On 12/19/13, there was no discussion. |
| TAC Decision | On 1/28/14, TAC unanimously voted to recommend approval of NPRR573 as recommended by PRS in the 12/19/13 PRS Report. All Market Segments were present for the vote. |
| Summary of TAC Discussion | On 1/28/14, there was no discussion. |
| ERCOT Opinion | ERCOT supports approval of NPRR573. |
| Board Decision | On 2/11/14, the ERCOT Board approved NPRR573 as recommended by TAC in the 1/28/14 TAC Report. |

| Business Case |
| --- |
| 1 | Alignment of Protocols and ERCOT systems. |

| Sponsor |
| --- |
| Name | Sandip Sharma |
| E-mail Address | Sandip.Sharma@ercot.com |
| Company | ERCOT |
| Phone Number | 512-248-4298 |
| Cell Number | 817-371-7773 |
| Market Segment | Not applicable |

| Market Rules Staff Contact |
| --- |
| Name | Jonathan Levine |
| E-Mail Address | Jonathan.Levine@ercot.com |
| Phone Number | 512-248-6464 |

| Comments Received |
| --- |
| Comment Author | Comment Summary |
| PDCWG 110513 | Proposed revisions to include in PRC the capacity from On-Line WGRs that are Primary Frequency Response-capable. |

Comments

Please note that NPRR576, Changing Non-Spin Service to an Off-Line Service, also proposes revisions to Section 6.5.7.5.

Proposed Protocol Language Revision

6.5.7.5	Ancillary Services Capacity Monitor

(1)	ERCOT shall calculate the following every ten seconds and provide Real-Time summaries to ERCOT Operators and all Market Participants using ICCP, giving updates of calculations every ten seconds, and posting on the MIS Public Area, giving updates of calculations every five minutes, which show the Real-Time total system amount of:

(a)	RRS capacity from Generation Resources;

(b)	RRS capacity from Load Resources excluding Controllable Load Resources;

(c)	RRS capacity from Controllable Load Resources;

(d)	Non-Spin available from On-Line Generation Resources with Energy Offer Curves;

(e)	Non-Spin available from undeployed Load Resources;

(f)	Non-Spin available from Off-Line Generation Resources;

(g)	Non-Spin available from Resources with Output Schedules;

(h)	Undeployed Reg-Up and undeployed Reg-Down;

(i)	Available capacity with Energy Offer Curves in the ERCOT System that can be used to increase Base Points in SCED;

(j)	Available capacity with Energy Offer Curves in the ERCOT System that can be used to decrease Base Points in SCED;

(k)	Available capacity without Energy Offer Curves in the ERCOT System that can be used to increase Base Points in SCED;

(l)	Available capacity without Energy Offer Curves in the ERCOT System that can be used to decrease Base Points in SCED; and

(m)	The ERCOT-wide Physical Responsive Capability (PRC) calculated as follows:

PRC1 =			Min(Max((RDF*HSL – Actual Net Telemetered Output)i , 0.0) , 0.2*RDF*HSLi),

where the included On-Line Generation Resources do not include WGRs and nuclear Generation Resources.

PRC2 =			Min(Max((RDFW*HSL – Actual Net Telemetered Output)i , 0.0) , 0.2*RDFW*HSLi),

where the included On-Line WGRs only include WGRs that are Primary Frequency Response-capable.

PRC3 =	((Hydro-synchronous condenser output)i as qualified by item (9) of Operating Guide Section 2.3.1.2, Additional Operational Details for Responsive Reserve Providers))

PRC4 =			(RRS MW supplied from Load Resources)i

PRC =	PRC1 + PRC2 + PRC3+ PRC4

The above variables are defined as follows:

| Variable | Unit | Description |
| --- | --- | --- |
| PRC1 | MW | Generation On-Line greater than 0 MW |
| PRC2 | MW | WGRs On-Line greater than 0 MW |
| PRC3 | MW | Hydro-synchronous condenser output |
| PRC4 | MW | RRS supplied from Load Resources |
| PRC | MW | Physical Responsive Capability |
| RDF |  | The currently approved Reserve Discount Factor |
| RDFW |  | The currently approved Reserve Discount Factor for WGRs |

[NPRR555: Replace paragraph (1) above with the following upon system implementation:] (1) ERCOT shall calculate the following every ten seconds and provide Real-Time summaries to ERCOT Operators and all Market Participants using ICCP, giving updates of calculations every ten seconds, and posting on the MIS Public Area, giving updates of calculations every five minutes, which show the Real-Time total system amount of: (a) RRS capacity from Generation Resources; (b) RRS capacity from Load Resources excluding Controllable Load Resources; (c) RRS capacity from Controllable Load Resources; (d) Non-Spin available from On-Line Generation Resources with Energy Offer Curves; (e) Non-Spin available from undeployed Load Resources; (f) Non-Spin available from Off-Line Generation Resources; (g) Non-Spin available from Resources with Output Schedules; (h) Undeployed Reg-Up and undeployed Reg-Down; (i) Available capacity from Controllable Load Resources in the ERCOT System that can be used to decrease Base Points (energy consumption) in SCED; (j) Available capacity from Controllable Load Resources in the ERCOT System that can be used to increase Base Points (energy consumption) in SCED; (k) Available capacity with Energy Offer Curves in the ERCOT System that can be used to increase Generation Resource Base Points in SCED; (l) Available capacity with Energy Offer Curves in the ERCOT System that can be used to decrease Generation Resource Base Points in SCED; (m) Available capacity without Energy Offer Curves in the ERCOT System that can be used to increase Generation Resource Base Points in SCED; (n) Available capacity without Energy Offer Curves in the ERCOT System that can be used to decrease Generation Resource Base Points in SCED; and (o) The ERCOT-wide Physical Responsive Capability (PRC) calculated as follows: PRC1 = Min(Max((RDF*HSL – Actual Net Telemetered Output)i , 0.0) , 0.2*RDF*HSLi), where the included On-Line Generation Resources do not include WGRs and nuclear Generation Resources. PRC2 = Min(Max((RDFW*HSL – Actual Net Telemetered Output)i , 0.0) , 0.2*RDFW*HSLi), where the included On-Line WGRs only include WGRs that are Primary Frequency Response-capable. PRC3 = ((Hydro-synchronous condenser output)i as qualified by item (9) of Operating Guide Section 2.3.1.2, Additional Operational Details for Responsive Reserve Providers)) PRC4 = (RRS MW supplied from Load Resources controlled by high-set under-frequency relay)i PRC5 = Min(Max((LRDF_1*Actual Net Telemetered Consumption – LPC)i, 0.0), (0.2 * LRDF_1 * Actual Net Telemetered Consumption)) from all Controllable Load Resources active in SCED and carrying Ancillary Service Resource Responsibility PRC6 = Min(Max((LRDF_2 * (Actual Net Telemetered Consumption – LPC)i, 0.0), (0.2 * LRDF_2 * Actual Net Telemetered Consumption)) from all Controllable Load Resources active in SCED and not carrying Ancillary Service Resource Responsibility PRC = PRC1 + PRC2 + PRC3 + PRC4 + PRC5 + PRC6 The above variables are defined as follows: Variable Unit Description PRC1 MW Generation On-Line greater than 0 MW PRC2 MW WGRs On-Line greater than 0 MW PRC3 MW Hydro-synchronous condenser output PRC4 MW RRS supplied from Load Resources controlled by high-set under-frequency relay PRC5 MW Capacity from Controllable Load Resources active in SCED and carrying Ancillary Service Resource Responsibility PRC6 MW Capacity from Controllable Load Resources active in SCED and not carrying Ancillary Service Resource Responsibility PRC MW Physical Responsive Capability RDF The currently approved Reserve Discount Factor RDFW The currently approved Reserve Discount Factor for WGRs LRDF_1 The currently approved Load Resource Reserve Discount Factor for Controllable Load Resources carrying Ancillary Service Resource Responsibility LRDF_2 The currently approved Load Resource Reserve Discount Factor for Controllable Load Resources not carrying Ancillary Service Resource Responsibility

[NPRR495 & NPRR555: Replace applicable portions of paragraph (1) above with the following upon system implementation:] (1) ERCOT shall calculate the following every ten seconds and provide Real-Time summaries to ERCOT Operators and all Market Participants using ICCP, giving updates of calculations every ten seconds, and posting on the MIS Public Area, giving updates of calculations every five minutes, which show the Real-Time total system amount of: (a) RRS capacity from: (i) Generation Resources; (ii) Load Resources excluding Controllable Load Resources; and (iii) Controllable Load Resources; (b) Ancillary Service Resource Responsibility for RRS from: (i) Generation Resources; (ii) Load Resources excluding Controllable Load Resources; and (iii) Controllable Load Resources; (c) RRS deployed to Generation and Controllable Load Resources; (d) Non-Spin available from: (i) On-Line Generation Resources with Energy Offer Curves; (ii) Undeployed Load Resources; (iii) Off-Line Generation Resources; and (iv) Resources with Output Schedules; (e) Ancillary Service Resource Responsibility for Non-Spin from: (i) On-Line Generation Resources with Energy Offer Curves; (ii) On-Line Generation Resources with Output Schedules; (iii) Load Resources; (iv) Off-Line Generation Resources excluding Quick Start Generation Resources (QSGRs); and (v) QSGRs; (f) Undeployed Reg-Up and Reg-Down; (g) Ancillary Service Resource Responsibility for Reg-Up and Reg-Down; (h) Deployed Reg-Up and Reg-Down; (i) Available capacity: (i) With Energy Offer Curves in the ERCOT System that can be used to increase Generation Resource Base Points in SCED; (ii) With Energy Offer Curves in the ERCOT System that can be used to decrease Generation Resource Base Points in SCED; (iii) Without Energy Offer Curves in the ERCOT System that can be used to increase Generation Resource Base Points in SCED; (iv) Without Energy Offer Curves in the ERCOT System that can be used to decrease Generation Resource Base Points in SCED; (v) With RTM Energy Bid curves from available Controllable Load Resources in the ERCOT System that can be used to decrease Base Points (energy consumption) in SCED; and (vi) With RTM Energy Bid curves from available Controllable Load Resources in the ERCOT System that can be used to increase Base Points (energy consumption) in SCED; (j) The ERCOT-wide Physical Responsive Capability (PRC) calculated as follows: PRC1 = Min(Max((RDF*HSL – Actual Net Telemetered Output)i , 0.0) , 0.2*RDF*HSLi), where the included On-Line Generation Resources do not include WGRs and nuclear Generation Resources. PRC2 = Min(Max((RDFW*HSL – Actual Net Telemetered Output)i , 0.0) , 0.2*RDFW*HSLi), where the included On-Line WGRs only include WGRs that are Primary Frequency Response-capable. PRC3 = ((Hydro-synchronous condenser output)i as qualified by item (9) of Operating Guide Section 2.3.1.2, Additional Operational Details for Responsive Reserve Providers)) PRC4 = (RRS MW supplied from Load Resources controlled by high-set under-frequency relay)i PRC5 = Min(Max((LRDF_1*Actual Net Telemetered Consumption – LPC)i, 0.0), (0.2 * LRDF_1 * Actual Net Telemetered Consumption)) from all Controllable Load Resources active in SCED and carrying Ancillary Service Resource Responsibility PRC6 = Min(Max((LRDF_2 * (Actual Net Telemetered Consumption – LPC)i, 0.0), (0.2 * LRDF_2 * Actual Net Telemetered Consumption)) from all Controllable Load Resources active in SCED and not carrying Ancillary Service Resource Responsibility PRC = PRC1 + PRC2 + PRC3+ PRC4 + PRC5 + PRC6 The above variables are defined as follows: Variable Unit Description PRC1 MW Generation On-Line greater than 0 MW PRC2 MW WGRs On-Line greater than 0 MW PRC3 MW Hydro-synchronous condenser output PRC4 MW RRS supplied from Load Resources controlled by high-set under-frequency relay PRC5 MW Capacity from Controllable Load Resources active in SCED and carrying Ancillary Service Resource Responsibility PRC6 MW Capacity from Controllable Load Resources active in SCED and not carrying Ancillary Service Resource Responsibility PRC MW Physical Responsive Capability RDF The currently approved Reserve Discount Factor RDFW The currently approved Reserve Discount Factor for WGRs LRDF_1 The currently approved Load Resource Reserve Discount Factor for Controllable Load Resources carrying Ancillary Service Resource Responsibility LRDF_2 The currently approved Load Resource Reserve Discount Factor for Controllable Load Resources not carrying Ancillary Service Resource Responsibility

# Comments

Please note that NPRR576 also proposes revisions to this section.

# Text boxes





resources

load

All

resource

load

online

i

online





resources

load

online

All

resource

load

online

i





resources

load

online

All

resource

load

online

i





resources

load

online

All

resource

load

online

i





resources

load

online

All

resource

load

online

i





resources

load

online

All

resource

load

online

i





resources

load

online

All

resource

load

online

i