## Slide 1
867_03 Meter Data Loading & Error Code Processing
Don Tucker/Kelly Brink
ERCOT
RMS
5/6/2014
Notes: <number>

## Slide 2: 867_03 Data Loading – Current Timeline
Timeframe for loading data initiated at 3am
Includes data submitted from 3am on Day 1 through 2:59 am on Day 2
  One activity report provided per meter type submitted (IDR, NIDR)
  867_03 Activity Reports provided via MIS to both the MRE and REP listed in N1SJ loop of transactions
May 6, 2014
Notes: <number>

## Slide 3: 867_03 Data Loading – Proposed Timeline
Timeframe for loading data initiated at 1 pm
Includes data submitted from 1pm on Day 1 through 12:59pm on Day 2
  One activity report provided per meter type submitted (IDR, NIDR)
  867_03 Activity Reports provided via MIS to both the MRE and REP listed in N1SJ loop of transactions
May 6, 2014

## Slide 4: 867_03 Data Loading Timeline Shift
3am Day 1 file pick up for data loading
2:59am Day 2
2:59am Day 3
3am Day 2
file pick up for data loading
5:30pm
Data Agg executes
1:00 pm Day 1
file pick up for data loading
12:59pm Day 2
12:59 pm
Day 3
1:00 pm Day 2
file pick up for
data loading
Day 1
Day 2
Day 3
5:30pm
Data Agg executes
May 6, 2014

## Slide 5: Reporting
867_03 IDR/NIDR Activity Report
  Posting time is tied to completion of data loading
  Posting time will move from early morning to late afternoon
  No change to delivery method (ERCOT MIS)
ESIID Service History and Usage Extract
  No change
Missing Consumption Report
  No change
May 6, 2014

## Slide 6: Moving the 867_03 data Loading Timeline
Why the discussion?
  Expand the time window for TDSP data submittals for inclusion in settlements
Proposed implementation
  Q4 2014
Question:
  Is RMS in agreement that ERCOT should proceed with moving the initiation of the 867_03 data loading process from 3:00 am to 1:00 pm, as described in this presentation?
May 6, 2014

## Slide 7: Error Code Processing Proposed Changes
Considering the retirement of a few error codes
  02 – Usage sent does not coincide with current ESIID/RESID history record
    Error code 01 - ESIID/RESID does not exist, would occur first and negate the need for this error
  12 – Incorrect Meter Role
    Meter level information is not considered for loading data.
  17 – TOU status unknown
    All ESIIDs in the ERCOT region must have a profile code assigned. This error is only triggered by a null profile code.
May 6, 2014

## Slide 8: Moving the 867_03 data Loading Timeline
Why the discussion?
  Remove unneeded error codes
Proposed implementation
  Q4 2014
Question:
  Is RMS in agreement with ERCOT proceeding with re-moving the 867_03 processing error codes as described in this presentation?
May 6, 2014