## Slide 1: Compromise Proposal to Adjust ORDC
Propose two adjustments to the calculation of ORDC adder:
  Subtract the quantity of ERS MWs from the reserve calculation upon deployment, even though those MWs were not counted pre-deployment.
  Adjust ORDC by taking out 25% of RUC MWs for the ORDCs calculated between December 1 and March 31, of every year. This correlates with the portion of RUC committed for capacity during cold-weather months, which we understand to be the primary concern.

## Slide 2: Compromise Proposal to Adjust ORDC
Both of these adjustments are compromises, as there are valid reasons that neither adjustment should be made:
  ERS. Available ERS MWs are not counted in the ORDC calculation. This inflates the ORDC relative to actual available reserves at all times when ERS is not deployed. The only reason the ORDC would reverse upon ERS deployment is because it was artificially high before deployment. While we do not agree with excluding ERS from the ORDC, this compromise corrects any potential reversal in the ORDC adder related to ERS.
  RUC. Reserves brought online through the RUC process are available to avoid firm load shed and should be included in the ORDC. RUC is used for two purposes, local and system-wide needs, and in each instance the RUC-committed resources would show up on the system as reserves at some price point. Ignoring these reserves altogether is unprincipled and results in excessive scarcity pricing in the ORDC. However, we understand that there have been concerns about excessive RUC commitments by ERCOT during winter months suppressing the ORDC. This proposal narrowly addresses that issue without further distorting the market.

## Slide 3: Compromise Proposal to Adjust ORDC
  Load Resources. Load Resources are included in the ORDC, and are properly reflected in the ORDC. When Load Resources are deployed, there is no ORDC reversal because those reserves are removed from the reserve calculation. Proposals to modify how Load Resources are treated in the ORDC are proxy approaches to requiring Loads to submit energy offers. Other efforts are under consideration to address those issues, and we do not believe any of the proposed adjustments are appropriate for the ORDC at this time.

## Slide 4: Additional Detail on the RUC Adjustment
The 25% value for the RUC adjustment is arrived at by trying to estimate the amount of RUC for Capacity and removing that from all intervals in the associated time frame.
  On January 28 ERCOT reported to TAC an estimate of the RUC breakdown: http://www.ercot.com/calendar/2014/01/20140128-TAC wherein it was reported for the 2013 that 13.6% of the RUC hours were for capacity.
  Compared to the smaller sample of January through March MWh the RUC for capacity is 25.8%.
Subtracting the RUC for the proposed months increases the ORDC to a much greater amount than a 0 to LSL adjustment as requested by the Commission.