## Slide 1
NPRR 617
Overview and Justifications

## Slide 2: Overview
Current protocols place restrictions on Day-Ahead Three-Part Supply Offers
  Part 1 (Startup Offer) – capped at generic or verifiable costs
  Part 2 (Minimum Energy Offer) – capped at generic or verifiable costs
  Part 3 (Offer Curve) – only limited by SWOC
Separately, generators are eligible for Day-Ahead and RUC make-whole payments, which are capped at generic or verified minimum energy values
NPRR 617 would eliminate the caps on Part 1 (Startup) and Part 2 (Minimum Energy), but keep in place the make-whole payments that are tied to generic or verifiable costs
2

## Slide 3: Acute Gas Supply Issues
Acute gas supply issues that increase fuel costs substantially above the index
<number>
Description | Baseline | Actual
Raw Average Fuel Consumption Rate per Start (MMBtu) - Cold | 6000 | 6000
Raw Verifiable Operation and Maintenance Expense per Start ($)- Cold | 6400 | 6400
Raw Verifiable Operation and Maintenance Expense at LSL ($/MWh) | 4.00 | 4.00
Raw Verified Fuel Consumption Rate at LSL (MMBtu/MWh) | 9.00 | 9.00
Assumed Gas Index | 4.50 | 7.00
Total Verified Start Cost | 36,400 | 51,400
Total Verified Minimum Energy | 49.00 | 71.50

## Slide 4: Invalid Index pricing
Day-over-day gas swings in HSC (as seen this past winter), or non-HSC pricing that varies wildly from the index (as seen this past winter)
<number>
Description | Baseline | Actual
Raw Average Fuel Consumption Rate per Start (MMBtu) - Cold | 6000 | 6000
Raw Verifiable Operation and Maintenance Expense per Start ($)- Cold | 6400 | 6400
Raw Verifiable Operation and Maintenance Expense at LSL ($/MWh) | 4.00 | 4.00
Raw Verified Fuel Consumption Rate at LSL (MMBtu/MWh) | 9.00 | 9.00
Assumed Gas Index | 4.50 | 25.00
Total Verified Start Cost | 36,400 | 159,000
Total Verified Minimum Energy | 49.00 | 233.50

## Slide 5: Acute Operational Issues
Acute operational/maintenance issues that increase the operational efficiency or reliability of generation
<number>
Description | Baseline | Actual
Raw Average Fuel Consumption Rate per Start (MMBtu) - Cold | 6000 | 6000
Raw Verifiable Operation and Maintenance Expense per Start ($)- Cold | 6400 | 6400
Raw Verifiable Operation and Maintenance Expense at LSL ($/MWh) | 4.00 | 4.00
Raw Verified Fuel Consumption Rate at LSL (MMBtu/MWh) | 9.00 | 12.00
Assumed Gas Index | 4.50 | 4.50
Total Verified Start Cost | 36,400 | 36,400
Total Verified Minimum Energy | 49.00 | 64.00

## Slide 6: Risk Associated with DAM commitments
During scarcity conditions, a generator could be willing to offer into the DAM only if there is a sufficient premium in the DAM to account for the risk of the financial commitment
<number>

## Slide 7: No Work-Arounds
There are no viable “work-arounds” for the problem
  Raising just one “part” of the offer (i.e., the offer curve) could result in a unit still being committed to run, but at LSL all day
  Submitting an “Energy-Only Offer” in lieu of a three-part supply offer will (i) preclude the DAM engine from optimizing generation assets, and (ii) ignore operational constraints of units (min off-line time, min run-time, etc.)
Generators are faced with option of either offering into the DAM at a price below what they should, or avoiding the DAM altogether. This tends to decrease generator participation in the DAM
<number>

## Slide 8: Protections for Load
NPRR 617 does not change the make-whole structure, as generators are only made whole to their generic or verified costs
There are already strong market-based incentives for Generators to make offers that do not significantly exceed true costs
  IMM oversight
  Economically-efficient offers
Loads are not required to purchase MW in the DAM, so if the price offered by generators exceeds what loads want to pay, they are free to not purchase the load in the DAM
<number>