## Slide 1: Seasonal Adjustment Factor Discussion
Technical Advisory Committee
6-26-14

## Slide 2: Background on CWG/MCWG Discussions
CWG/MCWG has been discussing how to best manage the credit exposure risk resulting from pricing excursions
  Recognition that existing methodology for determining Estimated Aggregate Liability and Minimum Current Exposure is backward looking and therefore insufficient
  Options for addressing price spike risk are currently being evaluated
CMW/MCWG has also been discussing credit exposure methodology changes which recognize differences in seasonal pricing outcomes
  Seasonal EAL NPRR
  Discussion of Seasonal Adjustment Factor increase at May CWG/MCWG meeting (no recommendation of magnitude or timing)

## Slide 3: Seasonal Adjustment Factor is a static multiplier applied to real-time prices on a 7x24 basis to calculate a daily Minimum Current Exposure (MCE). SAF has been set to 100% since implementation in 2012.
  MCE = Max[{ [[[Lo, i, d, k * T2 - G o, i, d, k * (1-NUCADJ o) * T3] * RTSPP i, d, k *SAF] + [RTQQNETES o, i, d, k * T1]]/n},
{ [G o, i, d, k * NUCADJ o * T1 * RTSPPidk*SAF]/n},
{ DARTNET o, i, d, k * T4/n}]
  RTQQNETES o, i, d, k = Max [0, [[RTQQES o, i, d, k, c * RTSPP i, d, k*SAF] - [RTQQEP o, i, d, k, c * RTSPP i, d, k *SAF]]]
16.11.4.1 Determination of Total Potential Exposure for a Counter-Party
Background on SAF
The Seasonal Adjustment Factor (SAF) is a component of the Minimum Current Exposure (MCE) calculation that serves as a price multiplier.

## Slide 4: Seasonal Adjustment Factor is not a Price Spike Adjustment Factor.
The Seasonal Adjustment Factor (SAF) is intended to adjust for seasonal price increases based on historical trends.
  SAF = Seasonal Adjustment Factor—Used to provide for the potential for Seasonal price increases based on historical trends. ERCOT shall initially set this factor equal to 100%. This factor will not go below 100%. ERCOT will provide Notice to Market Participants of any change at least 14 days prior to effective date along with the analysis supporting the change.
16.11.4.1 Determination of Total Potential Exposure for a Counter-Party
Background on SAF

## Slide 5: June 18th CWG Action
ERCOT staff recommends increasing the Seasonal Adjustment Factor to a value of 400% from the effective date through the end of July, 500% for the month of August, and 400% for the month of September. This will approximate the impact of the high price events in March 2014.

## Slide 6: MCE vs. Pricing Events
Since the MCE calculation is backward looking, increasing the Seasonal Adjustment Factor does not mitigate price spike risk.
A price spike event does not get picked up in MCE until 11 days later.

## Slide 7: Historical Price Trends
* ERCOT North Hub RT Settlement Point Prices

## Slide 8: Recommendations
Increase the Seasonal Adjustment Factor consistent with its intended use: to adjust for seasonal price increases based on historical pricing trends.
  SAF is not a price spike mitigation tool
  150% for July and September, 200% for August
    Given relevant historical data (on previous slide) this still seems high
Endorse CWG/MCWG’s pursuit of credit exposure reforms which actually mitigate price spike risks to the market.
  Evaluate Credit Insurance products
  Other?