## Slide 1: RCWG Update to WMS
August 6, 2014
<number>

## Slide 2: Draft NPRR for Resource Specific Fuel Price
Background - Some Resources were mitigated in real-time to below their actual cost due to large differences between FIP and their actual gas price on certain days in February and March 2014.
WMS directed RCWG to develop an NPRR for a resource specific fuel price equal to one of the following:
  FIP (Houston Ship Channel)
  Waha
  Maximum of FIP or Waha
Also discussed need for a make-whole mechanism for fuel events not covered by a Resource-specific fuel price (i.e. intraday gas purchases).
<number>

## Slide 3: Concept of Draft NPRR for Resource Specific Fuel Price
Provides a Resource-specific Fuel Price (RFP) equal to either FIP (HSC), Waha, or Maximum of FIP or Waha.
Includes a dispute process for Resources mitigated below their cost due to exceptional fuel costs.
  Similar language to RUC make-whole.
  Uplift allocated by LRS.
  Exceptional Event: Actual price paid for delivered gas must be greater than RFP plus a threshold fuel price.
    Threshold Fuel Price to be defined in the VCM.
    RCWG discussed a Threshold Fuel Price of at least $2/MMBtu or greater.
  Make-whole cost calculated as follows:
    Calculate an adjusted Mitigated Offer Curve for the Resource utilizing its approved Verifiable Costs and the verified actual fuel cost.
    Make-whole calculated as the positive difference between the minimum of the price from the adjusted Mitigated Offer Curve or the Energy Offer Curve, and the real-time Settlement Point Price (i.e. price from original MOC), times the minimum of the aggregated base point or metered generation.
  Must have verifiable costs on file to qualify.
<number>

## Slide 4: Make-Whole Calculation for Exceptional Fuel Events
Make-Whole = [Min(EOC, Adjusted MOC) – Original MOC] x Min(Agg. Base Point, Metered Generation)

## Slide 5: Next Steps
Continue discussion of the NPRR at the August 16th RCWG meeting.
<number>