## Slide 1: RCWG Update to WMS September 3, 2014
Draft NPRR for Resource Specific Fuel Price
ICE Indices for Real-Time MOC’s
1

## Slide 2: APPENDIX
<number>

## Slide 3: Overview of Draft NPRR for Resource Specific Fuel Price
Provides a Resource-specific Fuel Price (RFP) equal to either FIP (HSC), Waha, or Maximum of FIP or Waha.
Includes a dispute process for Resources mitigated below their cost due to exceptional fuel costs.
  Similar language to RUC make-whole.
  Uplift allocated by LRS.
  Exceptional Event: Actual price paid for delivered gas must be greater than RFP plus a threshold fuel price.
    Threshold Fuel Price to be defined in the VCM.
    RCWG discussed a Threshold Fuel Price of at least $2/MMBtu or greater.
  Make-whole cost calculated as follows:
    Calculate an adjusted Mitigated Offer Curve for the Resource utilizing its approved Verifiable Costs and the verified actual fuel cost.
    Make-whole calculated as the positive difference between the minimum of the price from the adjusted Mitigated Offer Curve or the Energy Offer Curve, and the real-time Settlement Point Price (i.e. price from original MOC), times the minimum of the aggregated base point or metered generation.
<number>

## Slide 4: Make-Whole Calculation for Exceptional Fuel Events
MOC = [ IHR x (RFP + fuel adder) + VOM] x CF Multiplier
Adjusted MOC = [ IHR x (verified actual fuel cost + 0) +VOM] x 1
Make-Whole = [Min(EOC, Adjusted MOC) – Original MOC] x Min(Agg. Base Point, Metered Generation)