## Slide 1: Annual TAC Review of the Market Impacts of Reliability Unit Commitments
ERCOT Market Analysis
Analysis of 1/1/14 through 12/31/14

## Slide 2: RUC Commitments Hours
1,698 Instructed Effective RUC Unit Hours in 2014
    881 hours (51.9%) for Voltage/Reactive Support
    468 hours (27.6%) for Congestion
    349 hours (20.5%) for Capacity
117 hours were successfully bought back though ONOPTOUT

## Slide 3: RUC Type Unit Hours by Month
2013
2014

## Slide 4: RUC Committed Resources Dispatched for Capacity
114 hours (6.8%) were dispatched above LSL for capacity out of 1,667 Effective RUC Unit Hours
  Only 1 five minute SCED interval out of 114 hrs was dispatched at a price above the RUC offer floor
    112hrs were dispatched for capacity due to incorrect EOC
    2hrs were dispatched for capacity due to mitigation of EOC
Considering all RUC commitments, the average Base Point was not much higher than the average LSL
Note: Difference between 1,667 and the 1,698 is a result of Resources starting up, shutting down, still being Off-Line for some portion of the RUC committed hours, or Resources not following RUC instructions
Notes: RN LMP = System lambda & BP> LDL => Resource is moved up for capacity since there is no congestion
RN LMP > System lambda & BP> LDL => Resource can contribute to reducing congestion and hence could be moved up for transmission.

## Slide 5: Energy Offer Curve Compliance
  1,667 Instructed Effective RUC Unit Hours were required to have an Energy Offer Curve priced above the floor from LSL to HSL
  1,471 hours (88.2%) properly priced above LSL
  23 hours (1.4%) incorrectly priced above LSL with less than one hour notice to update
  174 hours (10.4%) incorrectly priced above LSL in SCED with more than one hour notice to update
    Majority of the 174 hours were due to differences between LSL in COP and LSL via telemetry
    75 of the 174 hours (4.5%) had submitted EOCs below the RUC offer floor
With NPRR626, EOC will be automatically floored at RUC offer floor

## Slide 6: Estimated PNM Impact of RUC Committed Resources
  The impact of 0-LSL based on NPRR 626 is about $4k increase in PNM.
  Nearly $2k of the $4k increase in PNM was from 1/6 and 3/3
  Applying RUC offer floor of $1500/MWh, removing offer floors for AS and not releasing HASL showed that the impact reduced to approximately $1500 for these days.
  Applying RUC offer floor of $1500/MWh, removing offer floors for AS and implementing HASL release showed that the impact on energy prices is minimal (approximately $20) for these days. It could be expected that the impact of the remaining 363 days would be similar.
  Effects on RUC HSL on ORDC adder was not included in this analysis

## Slide 7: Conclusion
1,698 Instructed Effective RUC Hours
  52% of hours are for Voltage/Reactive Support
EOC non-compliance was only 4.5% (75 out of 1,667 hours)
  After implementation of NPRR 626, EOC will be automatically floored at $1,500
Impact of 0-LSL on energy prices is minimal after applying recent operational and market design changes. Impact on ORDC is not accounted in this analysis.

## Slide 8: Appendix

## Slide 9: Comparison of 2012, 2013 and 2014 (1 of 2)

## Slide 10: Comparison of 2012, 2013 and 2014 (2 of 2)