## Slide 1
NPRR680 background concept
Carrie Bivens
Manager, Day-Ahead Market
PRS
February 12, 2015

## Slide 2: Day-Ahead Market AS Procurement
DAM does not directly consider trades
QSEs can submit self-arrangement in DAM for their AS obligation (AS plan X load ratio share) to be covered by resources or trades
Ancillary Services Plan
Sum of QSE self-arrangement
Ancillary Services Procurement

## Slide 3: AS Responsibility Check
AS Responsibility Check starts at 1430 and checks for missing AS on a QSE-level
  If your QSE AS Responsibility>0, ERCOT checks that the Sum of AS capacity in COPs for all QSE’s Resources = QSE AS Responsibility
AS Bought in Trades
Total AS Offer awards
QSE AS Responsibility
Self-Arranged AS
AS Sold in Trades
COP AS capacity

## Slide 4: Current implementation - example
QSE A (Load, No Resources):
AS Obligation 40 MW
Trade 50 MW with QSE B
Enters self-arrangement of
40 MW
QSE B either:
Puts 50 MW of capacity in COP
Enters negative self-
arrangement of 50 MW
Scenario 1
Scenario 2
Result (assume no other self-arrangement):
QSE A receives nothing for the extra 10 MWs
Scenario 1 – DAM procures 80 MWs and 130 MW of AS is provided in Real-Time (10 MW more than needed).
Scenario 2 – DAM procures 130 MW (10 MW more than the AS Plan)
AS Plan = 120 MW

## Slide 5: Current implementation - example
QSE A (Load, No Resources):
AS Obligation 40 MW
Trade 50 MW with QSE B
Enters self-arrangement of
50 MW
QSE B either:
Puts 50 MW of capacity in COP
Enters negative self-
arrangement of 50 MW
Scenario 1
Scenario 2
Result (assume no other self-arrangement):
QSE A is paid MCPC for 10 MW of AS.
Scenario 1 – DAM procures 70 MWs and 120 MW of AS is provided in Real-Time (the amount needed).
Scenario 2 – DAM procures 120 MW (the exact AS Plan).
AS Plan = 120 MW