## Slide 1: OpenADR: The Standard for Automated Demand Response
Barry Haaser
Managing Director

## Slide 2: OpenADR Progression
2002 to 2006 2007 2008 2009 2010 2011 2012 2013 2014
Research initiated by LBNL/ CEC
Pilots and field trials
Developments, tests (Utilities)
OpenADR 1.0 Commercialization
(PG&E, SCE, and SDG&E)
Official OpenADR specification (v1.0) by LBNL/CEC*
1. OpenADR Standards Development
- OASIS (EI TC), UCA, IEC
2. NIST Smart Grid, PAP 09
1. DR 2.0 Pilots and field trials
- Wholesale markets, ancillary services
- Dynamic pricing, renewable, EVs
- International demonstrations
2. All end-uses and sectors
1. Foster Adoption
2. Test/Certify (v2.0)
* OpenADR v1.0: http://openadr.lbl.gov/
** OASIS EI 1.0 standards: http://www.oasis-open.org/committees/download.php/45425/energyinterop-v1.0-cs01.zip
*** Publication: http://drrc.lbl.gov/sites/drrc.lbl.gov/files/LBNL-5273E.pdf
Standards Interoperability Lifecycle Process: An iterative development process for a standard to be deployed In markets.***
Research and development
Pilots and field trials
Interoperability standards development
Deployment and market facilitation
EI 1.0 standards
- OpenADR profiles**
1. OpenADR 2.0 specifications
- International standards (IEC)
- OpenADR 2.0 products/deployments.
2. USGBC national pilots
3. Codes (CA T24)

## Slide 3: Understanding OpenADR
Open Automated Demand Response (OpenADR) provides a non-proprietary, open standardized DR interface that allows electricity providers to communicate DR signals directly to existing customers using a common language and existing communications such as the Internet.
Source: LBNL
Price Signal
$/kWh
Data Model
Comm
Internet
OpenADR
Pricing
Data Models
Physical Communications
Auto-DR
Client Server
End-Use Controls
Building
Action
Control Strategies

## Slide 4: ADR Market Forecast
(Source: Navigant Research)
ADR Sites by Region World Markets: 2014-2023

## Slide 5: Introducing VENs and VTNs
OpenADR is a message exchange protocol with two primary actors:
  Virtual End Nodes (VEN)
    Receive events and respond
    to them
    Generate reports
    Control demand side
    resources
  Virtual Top Nodes (VTN)
    Transmit events other
    nodes
    Request Reports
VTN
VTN/VEN
VEN
VEN
VEN

## Slide 6: OpenADR 2.0 Profiles
Energy Interoperation 1.0
B Profile
EiEvent
EiOpt
EiReport
EiRegistrerParty
A Profile
Simple EiEvent
“A” profile is targeted at limited resource devices and simple DR applications
“B” profile is targeted at robust devices and sophisticated DR applications
Excerpted from QualityLogic’s OpenADR Training Workshop © QualityLogic

## Slide 7: Profile Architecture
Transport Protocols
  Simple HTTP: Using standard http command. Ideal for pull clients, possible for push but firewall issues need to be taken into account
  XMPP: Used in messengers and many other social communication tools. Excels for push applications and fast DR. Pull also possible
Simple HTTP or XMPP for VEN, both mandatory for VTN

## Slide 8: Profile Architecture
Security
  Standard Security: TLS with server and client side certificates
  High Security: Standard Security + XML signatures to increase non-repudiation
Standard Security mandatory, High Security optional

## Slide 9: Event Intervals
Intervals carry the actionable information in a DR Event. Example:
 | Signal Name Start Time: 10am | Interval 1 20 mins | Interval 2 30 mins | Interval 3 15 mins
Signal 1 | SIMPLE (Level) | 1 (moderate) | 3 (Special) | 2 (High)
Signal 2 | ELECTRICITY_PRICE (price) CurrencyPerKWh | 1.05 (USD) | 1.30 (USD) | 1.15 (USD)
Excerpted from QualityLogic’s OpenADR Training Workshop © QualityLogic

## Slide 10: Event Resources
Target a VEN
Target a Group
Target a device class
Target a service area
Target a Resource
Pool Pump
Resource 2
Water Heater
Resource 4
Thermostat
Resource 1
VEN 1
Pool Pump
Resource 3
VEN 2
Water Heater
Resource 6
Lighting
Resource 5
VEN 3
DRMS can target available resources.
Excerpted from QualityLogic’s OpenADR Training Workshop © QualityLogic

## Slide 11: Supports Multiple DR Applications
ISO/Utility/Operator
C&I, SMB
Residential
Aggregator
C&I, SMB
Residential
OpenADR 2.0 link
EV Chargers / Battery
© greenlots
Renewables

## Slide 12: Cloud Interface
VTN
VEN
VEN
Internet
OpenADR 2.0 a or b enabled
Retail or Operator provided or bring your own thermostat
Cloud interface
No resource constraints
Feedback supported
GUI in Cloud

## Slide 13: Direct Connect
VTN
VEN
VEN
Internet
OpenADR 2.0a or b enabled
Retail or Operator provided
Easy config in cloud interface
Connection from cloud to device up to vendor
No resource constraints
Feedback possible
GUI in Cloud or LAN
ZigBee
Wi-Fi
etc.

## Slide 14: Commercial & Industrial
VTN
VEN
Internet
BACnet
LonMark
OpenADR
ZigBee
Wi-Fi
etc.

## Slide 15: Aggregators
VTN
VEN
Internet
Internet
VEN/VTN
Aggregator

## Slide 16: OpenADR . . .
Standardizes customer DR interface
Delivers interoperability/interchangeability
Eliminates stranded assets
Backed by industry leaders
Over 65 certified products
  Demand Response Management Servers (DRMS)
  Building automation controllers
  Energy management interfaces
  Lighting controllers
  Thermostats
  Water heaters
  Gateways

## Slide 17: What is the OpenADR Alliance?
Vision: Facilitate the global deployment of OpenADR to reduce the cost of supplying and consuming electricity, while improving energy reliability and reducing environmental impact.
California based nonprofit 501(c)(6) corporation
Member based organization comprised of over 130 industry stakeholders
Leverages Smart Grid related standards from OASIS, IEC, UCA and NAESB
Supports development, testing, and deployment of commercial OpenADR
Enables stakeholders to participate in automated DR, dynamic pricing, and electricity grid reliability
Notes: M

## Slide 18: Key Players

## Slide 19: OpenADR Resources

## Slide 20: OpenADR Program Guide
Defines ADR program templates modeled after most popular DR programs
Defines deployment scenarios with actors and roles clearly defined
Defines best practices recommendations for OpenADR characteristics
Provides a decision tree to aide utilities in selecting templates and deployment scenarios
Draft available upon request

## Slide 21: DR Program Templates
Critical Peak Pricing
Capacity Bidding Program
Residential Thermostat Program
Fast DR Dispatch (Ancillary Services)
Future Templates
  Real Time Pricing Program
  Direct Load Control Program

## Slide 22: Certification & Testing
Alliance created
  Profile Specification
  PICS documents
  Test plan and testing
  Certification documents
  Certification test tool
Test tool built by QualityLogic
Third party testing performed by Intertek
Members can obtain test tool for pretesting and do final certification testing at the test lab

## Slide 23: OpenADR 2.0 Documentation
OpenADR 2.0 Profile Specification
  Draft for Alliance members, final version public
  Overview section
  Definition of feature sets
  Conformance statements
  Transport Mechanism
  Security
  UMLs
  Mapping to other SG standards
Over 5000 Downloads
Available at www.openadr.org

## Slide 24: Product Database
Dynamic searchable database
66 certified VTNs and VENs
Simplifies product search process
Over 500 unique visitors search for certified products each month
www.openadr.org/certified-products

## Slide 25: EPRI Open Source Code
VTN: http://sourceforge.net/projects/openadr2vtn/
VEN: http://sourceforge.net/projects/openadr2bven-pull/
Over 1500 Downloads

## Slide 26: OpenADR Cloud Test Server
OpenADR Cloud Server for testing VENs
Subscription Service offered by QualityLogic
Ideal for small scale pilots
Verifies interoperability of VENs with a certified VTN
Good learning tool for understanding OpenADR
Available at www.qualitylogic.com

## Slide 27: OpenADR International Standard
The OpenADR Alliance is active in several IEC working groups
  IEC PC118 published the OpenADR 2.0b Profile Specification as IEC/PAS 62746-10-1
  IEC/PAS 62746-10-1 proposed as IEC standard
  IEC PC118 and TC57 WG 21 are working on CIM integration
  IEC TC65 WG17 (Industrial Automation) is adopting on OpenADR functionality

## Slide 28: OpenADR Implementers Workshop
1-2 day workshop
Periodic public workshops or private, on-site workshops
Led by Jim Zuber, QualityLogic’s Chief Test Architect and co-founder
  Authored the OpenADR Test Specification and PICS
  Designed the certification test harness,
  Major contributor to the Implementation Working Group

## Slide 29: OpenADR Developers Workshop
1-2 day workshop
Periodic public workshops or private, on-site workshops
Led by Jim Zuber, QualityLogic’s Chief Test Architect and co-founder
  Authored the OpenADR Test Specification and PICS
  Designed the certification test harness,
  Major contributor to the profile specification itself

## Slide 30: Rolf Bienert Barry Haaser Technical Director Managing Director rolf@openadr.org barry@openadr.org +1 925 336 0239 +1 408 310 9213
www.openadr.org
Thank You!
Q&A