## Slide 1
ORDC Phase 2 Analysis Summary
Wholesale Market Subcommittee
March 4, 2015
David Thompson

## Slide 2: Analysis Overview
Objective is to look at potential impacts for ORDC Phase 2 using historic data
Analysis was done to look at what additional capacity would be made available in Phase 2, or capacity that is upgraded from 30 minute payment to online payment and the effect it would have had on ORDC from June 1, 2014
  Combined Cycle configuration change
  Combined Cycle head room containing Non-Frequency Responsive Capacity (NFRC)
  Cold Start Time Peakers <30 min that are currently not available to SCED

## Slide 3: Phase 2 ORDC Analysis
CC Analysis
Assumptions
  Analysis looks at dates from 6/1/2014 to 12/31/2014
  Analysis looks at intervals when the Price Adder >= $1
  MW available for OFF10 or OFF30 would be on configuration change or on headroom not in HSL
  Evaluated intervals where Resource was in an online, ON or ONREG, status and not in outage that restricts unit from max configuration
Results Summary
  < 1% of CC capacity are not in their respective max configuration
Observation
  CCs are in max configuration when not in an outage and the economics are favorable

## Slide 4: Phase 2 ORDC Analysis
Peaker Analysis
Assumptions
  Analysis looks at dates from 6/1/2014 to 12/31/2014
  Analysis looks at all intervals
  MW available for OFF10 are qualified QSGRs and Resources with a start time <=10 minutes in the RARF
  Evaluated intervals where Resources were in an offline status and not in outage
Observation
  Total capacity available In <= 10 minutes is about 2800 MW
  NPRR 272 allows this capacity to submit offers to SCED
    1050 already in SCED
    1750 not currently in SCED
  Phase 2 could potentially move approximately maximum of 1750 MWs of existing MWs from RTOFFCAP to RTOLCAP
    Average is ~ 1,000 MW

## Slide 5: Phase 1 vs Phase 2 ORDC
Current metrics on Phase 1 ORDC vs. Phase 2 Analysis (By SCED interval)
Phase 2
Phase 1
Peaker Net Margin reduced by ~ 3.25%

## Slide 6: Phase 2 ORDC Summary
Overall Observations
  Phase 2 ORDC CC capacity is already in the ORDC payment because it is online when ORDC curve is in the range for payment
  Any MWs that can move from offline payments to online payments (i.e. QSGRs) already have an online mechanism through SCED
  Estimated Project cost savings of 65k and annual O&M savings of 1.1 FTE