## Slide 1
Outage Cost Study
Market Analysis and Design
Outage Coordination Improvement Task Force
3/23/2015

## Slide 2: Study Objective
Evaluate factors affecting predictability of congestion rent associated with hypothetical outages
Congestion Rent: Marginal cost of the constraint times the flow across the element.
  Congestion rent could be used as a metric to get relative value of transmission constraint since it is based on the marginal cost of resolving the constraint and the extent of violation
  CRRs/PTPs could be purchased to hedge against congestion in DAM/RT
  Congestion payout associated with outages not modeled in CRR could result in CRR payout shortfall and affect the effectiveness of the hedging in DAM and the convergence of CRR/DAM/SCED

## Slide 3: Study Methodology
Calculated congestion rent using modified Reliability Unit Commitment engine
  Penalty costs matching SCED shadow price caps
  COP and 3-Part Offers as submitted by 1400 of prior day
Studied 10 outages x 4 actual OD cases representing a range of system conditions
  For each outage and case, calculated difference in congestion rent with and without outage
  Analyzed additional sensitivities to multiple outages (N-1-1) and generation + transmission outages (N-1, G-1)

## Slide 4: Observations - Outage Type I
A few outages result in congestion irrespective of the variation in overall system conditions. Congestion is mainly dependent on local generation/load.
Outage | Summer 1 - 59000MW High Wind | Summer 2 - 63000MW Low Wind | Fall 1 - 42000MW Low Wind | Fall 2 - 37000MW Moderate Wind
La Palma to Rio Hondo 345kV circuit | ($8,217,002) | ($6,446,971) | $0 | $0
La Palma to Rio Hondo 345kV circuit + Silas Ray generation | ($10,170,363) | ($13,720,339) | ($2,489,595) | $0
Caddo Switch to Apache Tnp 138kv circuit | ($13,723,500) | ($13,265,000) | $0 | ($7,913,500)
Odessa Southwest to Moss Switch 138kV circuit | ($3,992,394) | ($6,523,320) | ($6,658,597) | $0

## Slide 5: Observations - Outage Type II
Majority of the outages do not independently cause congestion. However the pancaking effect when other outages are taken in the area can cause significant congestion.
Outage | Summer 1 - 59000MW High Wind | Summer 2 - 63000MW Low Wind | Fall 1 - 42000MW Low Wind | Fall 2 - 37000MW Moderate Wind
Moss Switch to Odessa EHV 345kV circuit | ($24) | $0 | $0 | $0
Midland East to Moss Switch 345kV circuit | $0 | $0 | $0 | $0
Moss Switch to Odessa EHV 345kV circuit + Midland East to Moss Switch 345kV circuit | ($3,197,198) | ($7,805,306) | ($7,142,003) | $0
Moss Switch to Odessa EHV 345kV circuit + Odessa Southwest to Moss Switch 138kV circuit | ($9,347,401) | ($14,110,224) | ($13,238,512) | $0

## Slide 6: Observations - Outage Type III
For some outages, the extent of congestion is highly dependent on several factors like system load level/ wind level/ forced outages
Outage | Summer 1 - 59000MW High Wind | Summer 2 - 63000MW Low Wind | Fall 1 - 42000MW Low Wind | Fall 2 - 37000MW Moderate Wind
Kuykendahl to Rothwood 345kV circuit | $0 | $0 | $0 | $0
Hays Energy to Kendal 345 kV circuit | $0 | ($72,597) | $0 | $0
Jewett 345 kV bus 1Bb1 | ($523,386) | ($99,484) | ($15,122) | ($55,074)
Lufkin to Nacogdoches South Tap 138kV circuit | $0 | ($32,777) | $0 | $0
Pawnee to Choate to Four Corners Sub 138kV circuits | $0 | $0 | $0 | $0

## Slide 7: Observations
Only few outages consistently cause congestion under all system conditions
Majority of outages cause congestion only under specific scenarios
  Pancaking of outages
    Could be addressed by approval priority based on submission timeline
  Forced outage
    Is it worthwhile to study N-2 based on significant ODF?
  Extreme load level or wind level
    Probabilistic analysis could capture the effects from both normal study case and conservative study case

## Slide 8: Further Discussion
How to effectively estimate the impact of variations of load and wind when predicting possible congestion due to an outage?
  Optimism of average case vs. over conservatism of extreme case
Construct a cost metric based on different possible system conditions weighted based on the possibility of materialization of that system condition
Probabilistic approach
  Expected Congestion Rent = Sum of (Congestion Rent in Scenario * Probability of Scenario)