## Slide 1
Design Your Screens for Situation Awareness
Mike Legatt, Ph.D.
Principal Human Factors Engineer
Electric Reliability Council of Texas, Inc.
Michael.Legatt@ercot.com
Source: Design Directions

## Slide 2
Introduction
This presentation is cover how humans perceive visual information and control visual attention, so that you can optimize your displays and control room environment to maximize situation awareness.

## Slide 3
Objectives
You will:
  Comprehend and report key components of how people process visual information
  Comprehend and report the role of working memory on human performance
  Comprehend and report the levels and characteristics of situation awareness
  Evaluate the layout of operator workstations, maximizing information processing
  Formulate UI design improvements to reduce working memory loading

## Slide 4
Definitions
Color Discriminability/Deficiency/Blindness
Signal Detection Theory (SDT)
Situation Awareness
Visual pathways
  Magnocellular
  Parvocellular
  Koniocellular
  Non-linear contrast gain
Working memory

## Slide 5
Question 1
Which text can you read most quickly, due to the nonlinear contrast gain control system and pathway speed?
Gray text against a white background
Black text against a white background
Yellow text against a blue background
Green text against a red background

## Slide 6
Starting Small…
Eye to LGN to several areas of brain:
  “What” system
  “Where / how” system
  Both involved in visual attention

## Slide 7
Starting Small…
Magnocellular (large cells):
  Edges, motion, low contrast
  “Low resolution”
  Black/Gray/White
  Fast processing
  Strongly linked to attention
  Nonlinear contrast gain control system – speeds up visual processing to high contrast
Source: Legatt, 2005

## Slide 8
Starting Small…
Parvocellular (small cells):
  Red/green color, form, high contrast, slower processing
  “High resolution”
  80% of LGN area
Koniocellular (“sand” cells)
  Yellow/blue color, slowest processing
  Recently discovered, hidden between layers
Source: Legatt, 2005

## Slide 9
Signal Detection Theory
Green & Swets (1966)
  Ability to correctly identify stimuli on a radar screen
How accurately can you detect stimuli?
  Hit / False Alarm Proportion
  Accuracy (% correct)
  Sensitivity (accuracy)
  Response criterion (bias in ambiguous situations)
 | Target | Noise
Response | Hit | False Alarm
No Response | Miss | Correct Rejection
Source: Legatt, 2005

## Slide 10
Measuring Visual Attention: VC-CPT
Source: Legatt, 2005

## Slide 11
Question 1
Which text can you read most quickly, due to the nonlinear contrast gain control system and pathway speed?
Gray text against a white background
Black text against a white background
Yellow text against a blue background
Green text against a red background

## Slide 12: Situation Awareness

## Slide 13
Question 2
Which of the following indicates the highest level of situation awareness when looking at a screen?
Being able to locate important information
Understanding the status of the equipment
Being able to predict the status of the equipment one minute from now
Seeing a flashing alarm when there’s a problem

## Slide 14
Situation Awareness
“The perception of elements in the environment within a volume of time and space, the comprehension of their meaning, and the projection of their status into the near future” (Endsley, 1995).
Level 1: Perception (What?)
Level 2: Comprehension (So what?)
Level 3: Projection (Now what?)
Both individual and team SA
Source: Endsley, 2011

## Slide 15
Question 2
Which of the following indicates the highest level of situation awareness when looking at a screen?
Being able to locate important information
Understanding the status of the equipment
Being able to predict the status of the equipment one minute from now
Seeing a flashing alarm when there’s a problem

## Slide 16
Question 3
Which designing your workstation, how should your content be laid out, if you’re facing forward?
 | User Interfaces (Left to Right) | Desk Materials
A) | Within 60° | To sides
B) | Within 30° | Forward
C) | Within 15° | Forward
D) | Within 15° | To sides

## Slide 17
Field of Vision
Resolution on retina highest at center, lower towards periphery.
  Farther out, you can only detect motion & vague shapes.
  Motion in the periphery can be distracting
  Try to keep content within
  FOV A(-15 to +15).
Source: Lean Valley

## Slide 18
Area of Reach
Lay out your workspace, and user interfaces so the most commonly-used interfaces and materials are in front of you, and less frequently used materials/interfaces are on the periphery.
Source: UN Enable

## Slide 19
Blind Spot
Close one eye and stare at the cross (if right eye open) or dot (if left eye open). Move your head back or forward
Source: Serendip Studio

## Slide 20
Question 3
Which designing your workstation, how should your content be laid out, if you’re facing forward?
 | User Interfaces (Left to Right) | Desk Materials
A) | Within 60° | To sides
B) | Within 30° | Forward
C) | Within 30° | To Sides
D) | Within 15° | To sides

## Slide 21
Question 4
What is absolutely necessary for good information organization and consolidation in a UI?
Operator trust in the system
Showing only warning/error information
Avoiding colors at all costs
Preventing redundant data across screens

## Slide 22
Ambient Lighting
Source: Lean Valley
High contrast differences between environment and your screen/UI can cause stress. For example,
  Full brightness in the middle of the night
  Low brightness screen in direct sunlight
  Transitioning between the screen and other factors of the environment can be frustrating.

## Slide 23
Colors
Color is a fascinating subject
  Cultural values associated with colors
  Evolutionary issues
    Favorite color blue (60% of men, 35% of women)
Source: Color Blindness Simulator
    Processing speed increases when large red objects seen
  In the eye, three types of cones process color

## Slide 24
Issues with color
Color discriminability decreases both with age and nicotine use
Color deficiency / blindness
Source: Chroma: A wearable augmented reality…

## Slide 25
Targeting our visual system
Based on knowledge on the visual system:
  If colors are being used, critical information should have strong red/green components (but check users for color blindness)
  Motion captures attention – only use when you want to capture attention
  Critical information should not have low contrast differentials
Source: UN Enable

## Slide 26
Information Organization
Try to group UIs based on task, frequency of use, and/or how critical its information
Try to minimize redundant data across multiple screens
If possible, integrate information from multiple sources to support operations
If possible, stay involved in development/vendor efforts; make sure the screens you receive work for you.

## Slide 27
Information Organization
When possible, show as little “all good” information – especially in complex systems
Provide straightforward paths to navigating to detail and searching
Whenever possible, test screens in simulations under a variety of conditions before deploying.

## Slide 28
Processing under stress
Source: Hancock & Warm (1989)
It’s most difficult to process information under extreme stress
Working memory decreases under stress
  7±2 items => 3-5 long term damage

## Slide 29
Trust is key!
A low trust in system is a major source of stress and forces changes in processing

## Slide 30
Question 4
What is absolutely necessary for good information organization and consolidation in a UI?
Operator trust in the system
Showing only warning/error information
Avoiding colors at all costs
Preventing redundant data across screens

## Slide 31
User-Centered Design
Organize around:
  User procedures and abilities
  The way we process information and make decisions
Source: Bernardo Malfitano
  Users understanding the state of the system (e.g., avoid early auto-pilot failures)

## Slide 32
Focus on the message
“This system is powerful”
Source: StackExchange

## Slide 33
Focus on the message
“This system is powerful”
Source: Rudy Vessup

## Slide 34
Focus on the message
“This system is powerful”
Source: Gizmodo

## Slide 35
Focus on the message
“This system is powerful”
Source: YouTube

## Slide 36
Focus on the message
“This system is powerful”
Source: Design Directions

## Slide 37
Focus on the message
“This system is powerful”
vs.
“This system is optimized so you can quickly understand what is going on”
Source: UN Enable

## Slide 38
Focus on the message
“This system is trying to optimize SA”
Sources: SA Tech, DHS,

## Slide 39
Question 5
Which of these statements is always true?
“Powerful system” user interfaces should never be used
Operator error risk can be mitigated, even with increased data complexity
User interface design can completely compensate for operator fatigue
An operator in a dark, quiet room will perform best

## Slide 40
Focus on the message
Why “this system is powerful?”
  Dignitaries and others visiting control rooms
  “cool” / “wow” factor
Why “Optimizing SA?”
  Important, mission critical systems
  Data that may be changing rapidly, and is of importance
  Trust in core systems – show primarily the exceptions, not all information
Both messages have their place!
Source: UN Enable

## Slide 41
Avoid Pitfalls
Attentional narrowing – attention grabbed, drawing focus away from critical information
Data overload – More/faster information presented than a human can process
Misplaced salience – Avoid the wrong things standing and catching your attention
Source: Endsley, 2011

## Slide 42
Avoid Pitfalls
Complexity Creep – Additions to a UI or procedure may affect far more than one screen
Alarm screens
  “Alarm storms” – critical information scrolling off the screen due to other important alarms
  “Dust storms” – critical information scrolling off the screen due to unimportant alarms
Source: Endsley, 2011

## Slide 43
Avoid Pitfalls
Human factors still matter
  User Interfaces can’t compensate fully for fatigue, stress, etc.
  People’s personality types influence how they perform in different environments
  Low operator confidence in systems
  Uncertainty in data not represented to users
Source: Endsley, 2011

## Slide 44
Question 5
Which of these statements is always true?
“Powerful system” user interfaces should never be used
Operator error risk can be mitigated, even with increased data complexity
User interface design can completely compensate for operator fatigue
An operator in a dark, quiet room will perform best

## Slide 45
Watch for Data Context & Misinterpretation Risk
Source: J. Merlo

## Slide 46
Watch for Data Context & Misinterpretation Risk
Source: J. Merlo

## Slide 47
Focus On What’s Important
Source: J. Merlo

## Slide 48
Focus On What’s Important
Source: J. Merlo

## Slide 49
Blind Spot
Close one eye and stare at the cross (if right eye open) or dot (if left eye open). Move your head back or forward
Source: Serendip Studio

## Slide 50
Questions
?
?

## Slide 51
Question 1
Which text can you read most quickly, due to the nonlinear contrast gain control system and pathway speed?
Gray text against a white background
Black text against a white background
Yellow text against a blue background
Green text against a red background

## Slide 52
Question 2
Which of the following indicates the highest level of situation awareness when looking at a screen?
Being able to locate important information
Understanding the status of the equipment
Being able to predict the status of the equipment one minute from now
Seeing a flashing alarm when there’s a problem

## Slide 53
Question 3
Which designing your workstation, how should your content be laid out, if you’re facing forward?
 | User Interfaces (Left to Right) | Desk Materials
A) | Within 60° | To sides
B) | Within 30° | Forward
C) | Within 30° | To Sides
D) | Within 15° | To sides

## Slide 54
Question 4
What is absolutely necessary for good information organization and consolidation in a UI?
Operator trust in the system
Showing only warning/error information
Avoiding colors at all costs
Preventing redundant data across screens

## Slide 55
Question 5
Which of these statements is always true?
“Powerful system” user interfaces should never be used
Operator error risk can be mitigated, even with increased data complexity
User interface design can completely compensate for operator fatigue
An operator in a dark, quiet room will perform best