## Slide 1
Multi-Interval Real-Time Market
Plan for Proposed Study Process

## Slide 2: MIRTM – Plan for Proposed Study Process
Stakeholders requested ERCOT to conduct studies to assess the proposed MIRTM with regard to the following:
  Forecast accuracy
  Commitment accuracy i.e. compare magnitude of make-whole payments for unnecessary commitment of Demand Resources versus benefit of correct commitment of Demand Resources
The plan to accomplish this has the following components:
  New model/algorithm for short term load forecasting
  Prototype MIRTM tool based on software changes to current Indicative Pricing Tool that will allow capability to commit Demand Resources
  Demand Resource bids used in study compiled from survey results
  ERCOT staff conducting studies, analyzing results and compiling reports to be presented to stakeholders
Notes: Slide #5

## Slide 3: MIRTM – Plan for Proposed Study Process
New model/algorithm for short term load forecasting
  New model/algorithm moved into production environment for 8 weather zones
  Begin tuning the models to optimize performance over the next 4-6 weeks
  Report accuracy of the new models versus current Short Term Load Forecast (ERCOT wide basis) – after models tuned
Software changes to current Indicative Pricing Tool
  Set Study Period to be 30 minutes
  Use telemetered ramp rates for entire study period (30 minutes)
  Add functionality to enable commitment of Demand Resources based on bids that contain
    Single Part Offer/Bid – no startup or minimum energy costs modeled
    Ramp Period or Notification time
    Minimum Curtailment time
    Maximum Curtailment time
    Return to service time
Notes: Slide #5

## Slide 4: MIRTM – Plan for Proposed Study Process
Demand Resource bids from survey
  ERCOT has received numerous examples of Demand Resource bids
ERCOT staff conducting studies, analyzing results and compiling reports
  Periodically review recent history of Real-Time prices and select periods of interest
    e.g. operating near the knee or the steep part of the aggregated EOC
  Retrieve Production Indicative Pricing Tool savecases for the period of interest
  Run the prototype MIRTM tool in offline environment using the Indicative Pricing Tool savecases
    In the savecase, swap out Short Term Load Forecast with the output from the new model
    Include Demand Resource bids
  Evaluate/analyze results and determine cost/benefit
Notes: Slide #5