## Slide 1
AS Demand Curves for
Real-Time Co-optimization of Energy & Ancillary Services

## Slide 2: Constructing AS Demand Curves – Concept paper
From the ORDC for Spinning Reserves:
Regulation Up Service (RegUp) Demand Curve
  Carve out RegUp Demand Curve from the first part of ORDC for Spinning Reserves
    The width of the carve out is the required MW for RegUp
Regulation Down Service (RegDn) Demand Curve
  RegDn Demand Curve is the same as the RegUp Demand Curve in terms of price but the MW width of the RegDn Demand Curve is equal to the RegDn MW requirement
Responsive Reserve Service (RRS) Demand Curve
  Carve out RRS Demand Curve from the remaining part of ORDC for Spinning Reserves after removing the RegUp requirement
    The width of the carve out is the required MW for RRS
From the ORDC for the combined Spinning and Non-Spinning Reserves:
Non-Spin Service (Non-Spin) Demand Curve
  Carve out Non-Spin Demand Curve from the ORDC for the combined Spinning and Non-Spinning Reserves starting from the MW point equal to the sum of the RegUp and RRS MW requirement
Notes: Slide #5

## Slide 3: Constructing AS Demand Curves – Other Ideas ?
Another approach would be to modify the carve out of the individual AS demand curves from the ORDC, but allow the carve outs of the ORDC to OVERLAP
Notes: Slide #5

## Slide 4: Constructing AS Demand Curves – Concept paper
ORDC – Spinning Reserves
ORDC – Combined Spinning & Non-Spinning
Reserves
Non-Spin Demand Curve
MW
MW
$/MW
$/MW
RegUp
Demand Curve
RRS
Demand Curve
Notes: Slide #5

## Slide 5: Example AS Demand Curve for 2015 Summer
Attached are 12 separate proposed demand curves based on the following:
Summer 2015 ORDC curves for spinning and non spinning reserves based
on the mean and standard deviation (mu and sigma).
Overlay the estimated Regulation and Responsive Reserve quantities to
the spinning reserve ORDC.
All remaining reserves considered Non-Spinning.
Examples use a SWOC of 3,000 $/MWh, VOLL 9,000 $MWh, with a
maximum demand curve price of 6,000 $/MWh
Notes: Slide #5

## Slide 6: Example AS Demand Curve for 2015 Summer
Summer 2015
Hour Block 23-24
and 1-2
Regulation
755 MW
(HE23)
Responsive Reserve
2702 MW
(HE23)
Notes: Slide #5

## Slide 7: Example AS Demand Curve for 2015 Summer
Non-Spin
Summer 2015
Hour Block 23-24
and 1-2
Notes: Slide #5

## Slide 8: Example AS Demand Curve for 2015 Summer
Summer 2015
Hour Block 3-6
Regulation
412 MW
(HE6)
Responsive Reserve
2702 MW
(HE6)
Notes: Slide #5

## Slide 9: Example AS Demand Curve for 2015 Summer
Non-Spin
Summer 2015
Hour Block 3-6
Notes: Slide #5

## Slide 10: Example AS Demand Curve for 2015 Summer
Summer 2015
Hour Block 7-10
Regulation
634 MW
(HE7)
Responsive Reserve
2702 MW
(HE7)
Notes: Slide #5

## Slide 11: Example AS Demand Curve for 2015 Summer
Non-Spin
Summer 2015
Hour Block 7-10
Notes: Slide #5

## Slide 12: Example AS Demand Curve for 2015 Summer
Summer 2015
Hour Block 11-14
Regulation
557 MW
(HE11)
Responsive Reserve
2538 MW
(HE11)
Notes: Slide #5

## Slide 13: Example AS Demand Curve for 2015 Summer
Non-Spin
Summer 2015
Hour Block 11-14
Notes: Slide #5

## Slide 14: Example AS Demand Curve for 2015 Summer
Summer 2015
Hour Block 15-18
Regulation
474 MW
(HE17)
Responsive Reserve
2300 MW
(HE17)
Max price on the Demand Curve
= VOLL – SWOC
=$9,000 - $3,000
= $6,000
$6,000
Notes: Slide #5

## Slide 15: Example AS Demand Curve for 2015 Summer
Non-Spin
Summer 2015
Hour Block 15-18
Notes: Slide #5

## Slide 16: Example AS Demand Curve for 2015 Summer
Summer 2015
Hour Block 19-22
Regulation
561 MW
(HE20)
Responsive Reserve
2300 MW
(HE20)
Notes: Slide #5

## Slide 17: Example AS Demand Curve for 2015 Summer
Non-Spin
Summer 2015
Hour Block 19-22
Notes: Slide #5