## Slide 1: Load Resource Inputs for MIRTM Simulation
ERCOT Staff
SAWG
April 29, 2015

## Slide 2: Background
Load Resource qualification in SCED today is limited to Controllable Load Resources (CLRs)
A Multi-Interval Real-Time Market (MIRTM) could enable different types of LRs to become SCED-qualified
  ‘Blocky’ Loads that can’t respond incrementally
  Loads with temporal constraints such as:
    Ramp periods longer than 5 minutes
    Minimum/maximum curtailment periods
    Return-to-service times
Under MIRTM, only the first 5-minute interval would produce a binding LMP
Prices further into the future would be non-binding, but MIRTM commitments would be binding

## Slide 3: Background (2)
If MIRTM commits a Resource further out than 5 minutes, and the Resource’s bid/offer price fails to materialize, Resource would need to be made whole
The question is: would the make-whole payments exceed the net benefits to the market?
  i.e., would it cost the market more or less to commit/dispatch the next Resource up the aggregated energy offer curve?
In an effort to answer the question, SAWG asked ERCOT to collect input data from LRs and their QSEs to enable simulated MIRTM runs
  The idea is to simulate real-world bid/offer prices and MW values
Discussed at DSWG, followed by ERCOT request for input data via emails to the DSWG exploder list

## Slide 4: LR inputs requested
DESCRIPTION | VALUE | INPUT
Energy curtailment price -- minimum real-time energy price that the LR would curtail consumption Assume, per market rules, LR can be made whole only for a single 15-minute Settlement interval and may need to incorporate this into curtailment price (see example page 6) | $/MWh | 
DR Quantity (Curtailable MWs available now [2015]) | MW | 
Ramp period (duration needed to reach full curtailment – a.k.a. “notification period”) | minutes | 
Minimum curtailment duration (a.k.a., “minimum down time”) | minutes | 
Maximum curtailment duration (a.k.a., “maximum down time”) | minutes | 
Post recall unavailability duration (a.k.a., “return to service time”) | minutes | 
Future DR Quantity (Curtailable MW expected to be available in 2018) | MW | 
And for future consideration….

## Slide 5: LR inputs received
QSE-RESOURCE | Offer/Bid Price ($/MWh) | Offer/Bid (MW) | Ramp Period (min.) | Min Run Time (min.) | Max Run Time (min.) | Return to Service Time (min.) | Ramp + Min Run Time
A-3 | $ 200 | 40 | 10 | 15 | 2880 | 1440 | 25
B-1 | $ 250 | 50 | 10 | 15 | 240 | 0 | 25
B-2 | $ 250 | 100 | 10 | 15 | 30 | 30 | 25
A-2 | $ 300 | 1 | 10 | 15 | 60 | 90 | 25
D-1 | $ 498 | 30 | 15 | 15 | 75 | 120 | 30
A-6 | $ 500 | 5 | 15 | 15 | 120 | 1 | 30
D-2 | $ 665 | 30 | 15 | 15 | 180 | 1200 | 30
A-7 | $ 800 | 30 | 15 | 15 | 120 | 4 | 30
D-4 | $1,431 | 25 | 15 | 15 | 75 | 60 | 30
D-3 | $ 2,008 | 20 | 15 | 15 | 360 | 1200 | 30
D-5 | $2,008 | 20 | 15 | 15 | 180 | 1200 | 30
D-6 | $ 3,365 | 15 | 15 | 15 | 360 | 1200 | 30

## Slide 6: Notes, Disclaimers
ERCOT will not use data submissions in which the Ramp Period + Minimum Run Time (curtailment period) exceeds 30 minutes
  At least initially, MIRTM window is expected to be ≤30 minutes due to short-term load forecast uncertainty
MIRTM simulations using this data have not been run yet
Stay tuned…

## Slide 7: Questions?
ON
OFF