## Slide 1
FAST Procurement and Pricing
May 28, 2015 TAC Meeting

## Slide 2: Introduction
The following slides describe the pricing and replacement costs associated with the different proposals:
  FAST proposal,
  IMM proposal (modification to NPRR 018 with introduction of linked energy bids from FFR providers),
  Enhanced 2015-2018 Alternative Proposal
Note that the purpose of these slides is to explain the concepts and therefore, as a simplification, do not differentiate between FFR1 and FFR2.

## Slide 3: Introduction
The PFRS and FFRS procurement constraints are the same in the FAST and IMM proposals, i.e. equivalency ratio is incorporated into the optimization process for procuring PFR and FFR
The Enhanced 2015-2018 alternative proposal considers the equivalency ratio in determining the initial estimate for AS requirements, but the optimization process assumes that the equivalency ratio is one for all hours (similar to current approach for RRS from Load Resources and Generation Resources)
  After DAM submission window closes, ERCOT operator may choose to modify PFR (and/or FFR) requirements based on expectation of PFR MCPC.

## Slide 4: FAST Proposal (PFRS & FFRS)
Stays with the current approach of pricing equivalent FFR MW awards the same as equivalent PFR awards
For example, FFR1, FFR2, awards are valued the same as the corresponding equivalent PFRS awards
In the case of FFRS, the ratio (R) determines the equivalence of R MW of PFRS to 1 MW of FFRS
If the PFRS MCPC reflect opportunity costs, then the corresponding equivalent FFR1, FFR2 MCPCs will also reflect opportunity costs

## Slide 5: FAST Proposal (PFRS & FFRS)
ERCOT is planning to submit comments on NPRR 667 to REMOVE the VOLL cap on FFR MCPC.
  If this is accepted, then the FAST proposal ensures that PFR and FFR providers have the same risks in terms of replacement

## Slide 6: FAST Proposal (PFRS & FFRS)
Replacement Risks
Provider Risk
Provider of FFR (FFR1, FFR2 MW) responsibility has the same risk as a provider of PFR responsibility in terms of replacement.
    Purchaser Risk
    If a provider of FFR needs to replace FFR1, FFR2 MW responsibility there is no risk that any of that cost will be uplifted to other market participants.

## Slide 7: IMM Proposal (PFRS & FFRS)
The core economic principle in this proposal is that marginal offers should be paid their cost (including their opportunity cost)
If the maximum FFR limit is reached, highest cleared FFRS offer sets the FFRS MCPC
Includes the concept of a resource specific energy bid from FFRS provider to incorporate opportunity costs for energy into FFRS pricing
For Resources offering to sell FFRS and other AS products(CRS, SRS for “blocky” Load Resources and FRRS-Up and PFRS for storage), this proposal will lead to MCPC and awards that are consistent with respect to the offered price.
  In the FAST proposal, the MCPC formulation for FFRS is such that there is an incentive to only offer to sell FFRS

## Slide 8: IMM Proposal (PFRS & FFRS)
MCPC Price Formation Process:
  Procure PFRS and FFRS identically to FAST Proposal
  Calculate prices of PFRS and FFRS based on the shadow prices of the constraints used to procure PFR and FFR
  The end result is that FFR1 and FFR2 MCPC will incorporate the opportunity cost for energy if it exists.
    Note that in the case where MCPC for FFR1 and/or FFR2 incorporates the opportunity cost, the marginal resource specific linked energy bid will be charged a energy price for cleared amount that is higher than the submitted not-to-exceed bid price for energy consumption
The above pricing philosophy also needs to be applied to other AS products (CR2, SR2, FRRS-Up, FRRS-Down)

## Slide 9: IMM Proposal (PFRS & FFRS)
Replacement Risks
Provider Risk
If a provider of FFRS needs to replace FFR1, FFR2 MW responsibility, the original provider of the FFR will be responsible for the cost of all the AS bought to replace their responsibility, even if higher priced PFRS MWs need to be purchased.
    Purchaser Risk
    If a provider of FFRS needs to replace FFR1, FFR2 MW responsibility there is no risk that any of that cost will be uplifted to other market participants.

## Slide 10: Enhanced 2015-2018 Proposal (PFRS & FFRS)
Stays with the current approach of pricing FFRS MW awards the same as PFRS awards and uses the equivalency ratio in determining the quantity of PFR/FFR to procure
If the PFRS MCPC reflect opportunity costs, then the corresponding equivalent FFR1, FFR2 MCPCs will also reflect opportunity costs
Replacement is 1 MW of PFRS for 1 MW of FFRS at all times – simplifies FFRS participation and reduces exposure of having to replace R MW (as high as 2.2) of PFRS for each FFRS in SASM
To meet new reliability standards, loads already required to pay for greater quantity of PFR/FFR in most of the year
With “FAST” implementation, loads not only pay for a greater quantity of PFR/FFR but also FFRS is paid “R” times PFRS prices – as high as $19,800/MW-h (more than twice the SWOC) – a significant increase in costs for loads over 2018 costs for the same MWs being procured
This proposal results in a lower PFR/FFR cost for loads while providing for simpler FFRS participation rules and lower exposure for FFRS replacement

## Slide 11: Enhanced 2015-2018 Proposal (PFRS & FFRS)
Description
@6:00 AM ERCOT posts PFRS and FFRS requirements taking into account the equivalency ratio. For example, hour ending X:
  PFR_requirement = 1240 MW
  FFR_requirement = 1060 MW
  Equivalency Ratio (R) = 2.0
  Total PFR+FFR requirement in PFRS MW is = 1240 + 2.0*1060 = 3360 MW

## Slide 12: Enhanced 2015-2018 Proposal (PFRS & FFRS)
Description (continued)
@10:00 AM, DAM submission window close,
  Determine expected FFRS MW amounts to be awarded equal to FFRS MW offered below previous day’s MCPC for PFR/FFR for the corresponding hour.
  Determine total requirements in PFRS MW for the DAM engine as:
    New_Total_PFR_FFR_Req =
    Original_total_PFR_FFR_req – (R-1)*Expected_FFR_cleared_amount
  DAM Procurement constraints are:
      Sum(PFR)+Sum(FFR) >=New_Total_PFR_FFR_Req
      Sum(FFR) <= FFR_requirement
  The MCPC for PFRS and FFRS is the same and is the shadow price of constraint 3.a) above

## Slide 13: Enhanced 2015-2018 Proposal (PFRS & FFRS)
Description (continued)
For example, at 10:00 AM DAM submission window close, the following offers are in the system (assume R=2 for this hour):
  3000 MW of PFRS @10 $/MW
  800 MW of FFRS @3 $/MW
  500 MW of FFRS @11 $/MW
  ERCOT guesstimates the MCPC for PFR/FFR to be $10/MW (based on some adjustment of previous day’s MCPC)
  If prior day’s MCPC was $10/MW, then FFRS MW expected to clear is 800
  New Total PFR+FFR requirement = 3360 - (2-1)*800 = 2560 MW
  DAM Procurement constraints are:
      Sum(PFR)+Sum(FFR) >=2560
      Sum(FFR) <= 1060
  The MCPC for PFRS and FFRS is the same and is the shadow price of constraint 4.a) above, i.e. $10/MW (800 MW of FFRS and 1760 MW of PFRS awarded)

## Slide 14: Enhanced 2015-2018 Proposal (PFRS & FFRS)
Replacement Risks
Provider Risk
If a provider of FFRS needs to replace FFR1, FFR2 MW responsibility, the original provider of the FFR will be responsible for only the cost of replacing the same MW amount of either FFRS or PFRS. Thus, the risk to the provider of FFRS is the same as the risk to the provider of PFRS.
    Purchaser Risk
    If a provider of FFRS needs to replace FFR1, FFR2 MW responsibility there is risk that some of that cost will be uplifted to other market participants.

## Slide 15: PFR & FFR MCPC Formulas
Note that FFRS is of two types - FFR1 and FFR2
The details of the procurement constraints (in NPRR 667) are:
  Sum(PFR) + R*Sum(FFR1+FFR2) >= Total Requirement in PFR MW terms (shadow price SP1 >=0)
  Sum(FFR1+FFR2) <= FFR_Total_Requirement (shadow price SP2<=0)
  Sum(FFR1) <= FFR1_Requirement (shadow price SP3<= 0)
  PFR MCPC = SP1
AS | FAST | IMM Proposal | Enhanced 2015-2018 Alternative
FFR | R * PFR MCPC | Ratio * PFR MCPC + SP of FFRmax constraints1 | PFR MCPC
1 Opportunity costs, if present, will be included in the shadow prices
SP = Shadow Price of Constraint