## Slide 1
Market Update
ERCOT Market Analysis
QSE Managers Working Group
6/5/2015

## Slide 2: Supplemental Ancillary Services Market (SASM) Update
  3/5 SASM insufficient; large AS requirement
  HRUC determined AS was undeliverable due to unit isolation from outage scheduler which led to 3/5 SASM
  Over-procurement of 5/25 SASM due to rounding of awards to nearest 0.1MW
Notes: Non-reconfiguration SASMs

## Slide 3: Manual Overrides
  One SCED interval 3/25 22:10:13 had an HDL override on one Resource due to an unsolved contingency
  Contingency was immediately solved after override
  Constraint was then activated for congestion management and override was removed

## Slide 4: Manual Overrides
  4/29 8:34-9:00 (six SCED intervals) two Resources had HDL overrides due to loss of VAR control system at Resources causing voltage spikes
  Override removed once VAR control system rebooted at Resources

## Slide 5
QUESTIONS / COMMENTS???