## Slide 1
AS Demand Curves for
Real-Time Co-optimization of Energy & Ancillary Services

## Slide 2: ISO AS Demand Curves
Review Matrix to compare basic market functionality across all ISO’s
  Reviewed California ISO (CAISO), Pennsylvania-New Jersey-Maryland Interconnection (PJM), Midwest ISO (MISO), New York ISO NYISO), and Southwest Power Pool (SPP)
  All have Co-optimization of Energy and Reserves in Day Ahead and Real Time
  Each ISO utilizes the same AS demand curve (MW and $MW) In their Day Ahead market and RT Market. Across ISO’s the AS demand curves vary
  All have same basic reserve products Spinning reserve, 10 minute reserves, and 30 minute reserves; even though product names vary quite a bit.
Review Market differences
Review AS demand curve differences
Review scarcity action plans
FERC findings
Appendix: Details regarding individual ISO AS demand curves
Notes: Slide #5

## Slide 3: ISO Demand Curves - Matrix
Notes: Slide #5

## Slide 4: ISO AS Demand Curves – Day Ahead Requirements
CAISO
Backstop resources must provide capacity into Day Ahead.
Load serving entities must schedule a percentage of the Load Forecast
PJM
PJM capacity resources obligated to offer everyday into Day Ahead
NYISO
Resources that are Capacity providers must offer in Day Ahead
MISO
Must offer in Day Ahead based on installed Capacity of the generator
SPP
Firm contracts or generation assets must offer in DA based on next day obligation to cover Load & Reserve Requirement
Notes: Slide #5

## Slide 5: ISO AS Demand Curves – AS Demand Curves
CAISO
Requirements for sub-region must be met by resources in the sub-region
Real Time requirement may change from Day Ahead based on Load Forecast
Max energy bid price = $1000
Demand curve based on percentage of max bid price and the amount of shortage
PJM
Max Spinning $1700, Max Non Spinning $850, Max Energy $2700 (without congestion)
Penalty price based on highest out of market payment to maintain reserves
No curve single step regardless of shortage
NYISO
Requirements set for sub regions to facilitate distribution of reserves throughout state and for post contingency voltage concerns.
Scarcity price could go to $8000 without congestion
Demand curve price determined by most expensive unit of supply curve multiplied by estimated future price ($750/MWh)
MISO
Operating Reserve Demand Curve determined by probability of loss of generation applied to a Value of Lost Load (VOLL) of $3500 (less regulating reserve price)
Regulating and Spinning reserve prices based on percentage of shortage in two steps
VOLL set by class that valued the interruption the least (residential class) via surveys
Price capped at $3500 ex-post. Offer caps $100 Spinning and Supplemental, $500 Regulation
SPP
Shortage price as follows: $1100 Operating reserve, $600 Regulation, $200 spinning. Priority to energy which accounts for each Shortage Price with a max $50,000
Reserve zones ensure deliverability. Optimization tries to maintain the minimum amount to carry and the maximum to export. Load in each zone pays for those reserves.
Notes: Slide #5

## Slide 6: ISO AS Demand Curves – Scarcity Action plan
CAISO
RUC is an economical bid in market and will commit to meet demand if not enough scheduled in Day Ahead
Reserves can be deployed when Operators do a contingency run which will release the reserves to be dispatched as energy.
PJM
Would not shed load to maintain reserves but would shed load as a type of reserve
Will take a voltage reduction to maintain reserves
NYISO
If short in Day Ahead, the operator would commit a resource and/or schedule across the interchange
Spinning and Non Spinning reserves are deployed manually
MISO
Never had a Day Ahead Insufficiency
If insufficient in Real Time, then they would release emergency energy logic (No out of market commitment)
SPP
If short in Day Ahead, will commit a resource out of market
In case of Real Time scarcity, they will commit, then release emergency limits, then curtail exports
Notes: Slide #5

## Slide 7: ISO AS Demand Curves - FERC Summary
FERC Observations:
RTOs and ISOs all tend to define a shortage in the same way, but shortage pricing triggers differ.
Shortage events are rare, sometimes not occurring at all in a year. But the frequency at which these events occur varies by RTO or ISO.
Oftentimes, shortage events only last for a matter of a few 5-minute dispatch intervals.
Because shortage events are rare and short-lived, potential revenue to be earned from shortage pricing could be minimal.
Some operator actions taken to avert a shortage are not reflected in market clearing prices
Taken from Price Formation in Organized Wholesale Electricity Markets docket: https://www.ferc.gov/legal/staff-reports/2014/AD14-14-pricing-rto-iso-markets.pdf
Notes: https://www.ferc.gov/legal/staff-reports/2014/AD14-14-pricing-rto-iso-markets.pdf
We did not look at ISO-NE but they were covered in the FERC document

## Slide 8: ISO AS Demand Curves – FERC Summary
…competing interests likely explain the different price levels for similar products…
For instance, Synchronous Reserve in PJM, Spinning Reserve in SPP, Ten-Minute Spinning Reserve in ISO-NE, and MISO’s Spinning and Regulating Reserves constraint all apply to roughly the same product.
In PJM, during a shortage of Synchronous Reserve, Synchronous Reserve would be priced at $550/MWh and energy would be $550/MWh plus the relevant locational marginal energy price.
In SPP, during a Spinning Reserve deficiency, Spinning Reserve would be priced at $200/MW, plus the clearing price for Supplemental Reserve, plus the zonal Regulation-Up plus Contingency Reserve shadow price.
In ISO-NE, during a shortage of Ten-Minute Spinning Reserve, Ten-Minute Spinning Reserve would be priced at $50/MWh plus the price of Ten-Minute Non-Spinning Reserve, plus the price of Thirty-Minute Operating Reserve.
And in MISO, if there is a deficiency in the Spinning and Regulating Reserves requirement, the market-clearing price for Spinning Reserve will be set at a level dependent upon the degree of shortage (between $65/MWh and $98/MWh) plus the price of Supplemental Reserve (derived from the Operating Reserve requirement). Depending on the levels of the prices for the other products, these price levels may be quite different.
Taken from Price Formation in Organized Wholesale Electricity Markets docket: https://www.ferc.gov/legal/staff-reports/2014/AD14-14-pricing-rto-iso-markets.pdf
Notes: https://www.ferc.gov/legal/staff-reports/2014/AD14-14-pricing-rto-iso-markets.pdf
We did not look at ISO-NE but they were covered in the FERC document

## Slide 9: ISO AS Demand Curves: Appendix
Notes: https://www.ferc.gov/legal/staff-reports/2014/AD14-14-pricing-rto-iso-markets.pdf
We did not look at ISO-NE but they were covered in the FERC document

## Slide 10: ISO AS Demand Curves – California ISO
Higher quality reserve can satisfy the requirements of lower quality reserves (substitution)
Reg Up = 20% of Max Energy Bid = $1000 x .2 = $200
Spinning = 10 % = $100
Non-Spinning = shortage > 210MW = 70% = $700, shortage >70 & < 210 = 60% = $600, shortage < 70 = 50% = $500
Table 4 From https://www.ferc.gov/legal/staff-reports/2014/AD14-14-pricing-rto-iso-markets.pdf

## Slide 11: ISO AS Demand Curves – Midwest ISO
The Probability of Load shed (LOLP) is based on the probability of load shed given a single forced outage will occur based on how many units will be online > 100 MW (which is determined by a quarterly network model)
VOLL based on surveys and set by the class that valued load interruption the least (Residential)
Not much Demand Response - ~150MW blocky spinning and ~75MW regulation (based on DR types that can provide)
Table 5 from https://www.ferc.gov/legal/staff-reports/2014/AD14-14-pricing-rto-iso-markets.pdf
Notes: Zonal requirements are determined 2 days before OP day by an offline study. Zonal requirements may change but not System wide.
Offer caps: $100 Spinning, $100 Supplemental, $500 Regulation
For cleared Market-Wide Regulating Reserve levels less than the Market-Wide Regulating Reserve Requirement, the Market-Wide Regulating Reserve Demand Curve price is set equal to the average cost per MW of committing and running a peaking unit for an hour ($175)
For cleared Market-Wide Regulating and Spinning Reserve levels greater than ninety percent (90%) but less than one hundred percent (100%) of the
Market-Wide Regulating and Spinning Reserve, the Market-Wide Regulating and Spinning Reserve Demand Curve price is $65 per MWh. For cleared Market-Wide Regulating and Spinning Reserve levels less than ninety percent (90%), of the Market-Wide regulating and Spinning Reserve,the Market Wide Regulating and Spinning Reserve Demand Curve price is $98 per MWh.
The MCP calculations, including Shadow Price descriptions, are described below.
Regulation MCPREG = gOR(z) + gRS(z) + gRR(z) + gRPOR(z) + gRPRS(z) + gRPRR(z) + gGOR + gGRS
SER Regulation MCPREGSER = gOR + gMSERR + gRS + gRR + gGOR
Spinnning MCPSPING = gOR(z) + gRS(z) + gRPOR(z) + gRPRS(z) + gGOR + gGRS
DR Spinning MCPSPIND = gOR(z) + gRS(z) + gRPOR(z) + gRPRS(z)
Supplm RSV gen based MCPSUPPG = gOR(z) + gRPOR(z) + gGOR
Supplm RSV dr based MCPSUPPD = gOR(z) + gRPOR(z)

## Slide 12: ISO AS Demand Curves – New York ISO
30 Minute Reserve = 30 Min Rsv price = $750
10 Minute Rsv = 30 Min Rsv price + 10 Min Rsv price = $1500
Spin Rsv = 30 Min Rsv price + 10 Min Rsv price + Spin price = $2275
DC determined by most expensive unit on supply curve (SU and ME) multiplied by estimated forward fuel price
Utilize shortage pricing for statewide and locational reserves
Demand response limited to 5 minute dispatchable Steel Mill

## Slide 13: ISO AS Demand Curves – New York ISO Regional pricing
Notes: https://www.ferc.gov/legal/staff-reports/2014/AD14-14-pricing-rto-iso-markets.pdf
We did not look at ISO-NE but they were covered in the FERC document

## Slide 14: ISO AS Demand Curves - PJM
PJM does not have a Regulation reserve shortage price.
$850 penalty factor based on the highest Out of Market payment to maintain reserves
Demand Response provides ~200 MW reserves and ~8-9000 MW deployable energy (recovery and response time ~10 minutes).
Notes: Under most conditions, the increased Synchronized Reserve Requirement will be 75% of the larger single contingency during the off-peak period (0000 –0459) and 100% of the larger single contingency during the on-peak period (0500 – 2359). This value may be further adjusted by PJM to meet the system reliability needs

## Slide 15: ISO AS Demand Curves – Southwest Power Pool
The product substitution logic ensures that, within each reserve zone, the MCP for Regulation-Up is always greater than or equal to the Spinning Reserve MCP and that the Spinning Reserve MCP is always greater than or equal to the Supplemental Reserve MCP.
If an OR shortage is caused by insufficient ramping ability, no shortage price is instituted
No Demand Response resource carrying Ancillary Service
Firm contracts or generation assets must offer in Day Ahead based on next day obligation to cover Load and Reserve requirement.
Notes: Capacity is required by Energy, Regulation-Up Service, Spinning Reserve and Supplemental Reserve and Operating Reserve product pricing rules (“price cascading”) require that the Regulation-Up Service MCP be greater than or equal to Spinning Reserve MCP and that the Spinning Reserve MCP be greater than or equal to the Supplemental Reserve MCP on both a system-wide basis and Reserve Zone basis. Therefore, any shortage in capacity to meet Energy, Regulation-Up and Contingency Reserve (both spinning and supplemental) requirements will be reflected in the pricing of all of these products.
(a) For example, if we assume that there is a 50 MW shortage of Supplemental Reserve, the Supplemental Reserve MCP would be set to $1100/MW and the Spinning Reserve MCP, Regulation-Up Service MCP and the Energy LMP would also reflect the impacts of this $1100/MW price. The Energy LMP is increased by the Operating Reserve shortage price of $1100/MW if the cost of serving an incremental MW of energy worsens the Operating Reserve capacity shortage condition (i.e. Operating Reserve Demand Curve is included in the LMP calculation), otherwise it is not.
Table 3 from the FERC Shortage pricing document