## Slide 1
Constraint Management Plans (CMPs) An Ops Planning Perspective
Nitika Mago
Operations Planning, ERCOT

## Slide 2
An Introduction to Constraint Management Plans
  What/Why, Types
Overview of the Annual CMP Review Process
  What/Why, When, Who’s involved
  Study Case, Contingency Definitions
  Criteria Used in Studies
2015 Review Summary
  Initial Details – kick off, case used, case changes
  Highlights of the Review
  A Pick-list of plans
Agenda

## Slide 3
Set of pre-defined actions executed in response to system conditions
To prevent or to resolve one or more thermal or non-thermal transmission security violations or to optimize transmission.
Typically developed in cases where studies indicate economic dispatch alone may be unable to resolve a transmission security violation
What are CMPs? Why are CMPs needed?

## Slide 4
Remedial Action Plans (RAPs)
  may be relied upon for allowing additional use of transmission system in SCED
  are modeled in CIM.
  constrained element must have a 15-minute rating >= its normal & emergency rating
  must not include load shed.
Mitigation Plans (MPs)
  shall not be used to manage constraints in SCED
  must be implemented in a timeframe that will not result in loss of the constrained element/facility
  may include load shed.
Pre-Contingency Action Plans (PCAPs)
  may be implemented in anticipation of a contingency
  must not include load shed.
Temporary Outage Action Plans (TOAPs)
  Temporary CMP, live & die with an outage.
  shall not be used to manage constraints in SCED
  must be implemented in a timeframe that will not result in loss of the constrained element/facility
  may include load shed.
Common Types of CMPs

## Slide 5
An Introduction to Constraint Management Plans
  What/Why, Types
Overview of the Annual CMP Review Process
  What/Why, When, Who’s involved
  Study Case, Contingency Definitions
  Criteria Used for selection
2015 Review Summary
  Initial Details – kick off, case used, case changes
  Highlights of the Review
  A Pick-list of plans
Agenda

## Slide 6
Objective
  Generate a set of CMPs to address anticipated reliability issues in the upcoming year.
Scope
  Existing CMPs
  CMPs proposals (may include plans emanating from system planning studies)
Time Frame for Review
  March to May
Participants
  All Market Participants
Study Case
  SSWG Planning Cases are relied upon (Summer Peak)
  Load & Generation in this case are analyzed and may be altered as necessary to build a scenario that is reflective of (extreme) peak conditions anticipated in the upcoming Summer season.
Overview of Annual CMP Review Process

## Slide 7
Contingency
  For CMP replication purposes
    Operations Contingency (Breaker-to-Breaker) are overlaid on the planning case.
  For CMP viability (i.e. N-1 studies post CTG & CMP action; to ensure no new violation is created)
    A blend of contingencies posted by SSWG are used.
Criteria for CMP Selection
Approval Process (applicable for CMPs that meet the Activate criteria)
  Coordinated process involves soliciting review & approval from all involved TSPs and REs as applicable.
Overview of Annual CMP Review Process

## Slide 8
An Introduction to Constraint Management Plans
  What/Why, Types
Overview of the Annual CMP Review Process
  What/Why, When, Who’s involved
  Study Case, Contingency Definitions
  Criteria Used in Studies
2015 Review Summary
  Initial Details – kick off, case used, case changes
  Highlights of the Review
  A Pick-list of plans
Agenda

## Slide 9
Kick Off
  March 11, 2015
2015 Review Highlights

## Slide 10
Submittals
  Reviewed 196 Proposals
  Submitters included
2015 Review Highlights

## Slide 11
Approvals
  Approved 55 CMPs
    (21 Existing, 11 New)
  Removed 25 CMP
  On-Shelf 40 CMPs
    9 N-1 (3 Existing, 8 New)
  31 N-i related CMPs
2015 Review Highlights

## Slide 12
Type | ID | Document | Contingency | TSP/MP | Note
MPs | MP_2013_29 | Alice (ALICE) 138-69 kV transformer.doc | XALI89 | AEP | Maintain
MPs | MP_2014_49 | Edison_Orsted_SSR_.doc | Multiple | ETT/AEP | Maintain
MPs | MP_2013_07 | Eskota Sw 138-69 kV Autotransformer.docx | XESK89 | ONCOR | Maintain
MPs | MP_2012_07 | FormosaAuto 21 and 22_hi EXPORT.docx | XFO2R89 or XFO3R89 | N/A | Maintain
MPs | MP_2012_08 | FormosaAuto 21and22_hi-IMPORT.docx | XFO2R89 or XFO3R89 | N/A | Maintain
MPs | MP_2014_01 | Lon Hill - Smith 69kV line (LON_HI_SMITH1) rev 2.doc | SORNLON8, DLONOR58 | AEP | Maintain
MPs | MP_2010_22 | Minerva 138,69 kV Autotransformer.doc | XMNR89T1 | ONCOR | Maintain
MPs | MP_2013_27 | Monticello Area.doc | MNSES gen OFFLINE | AEP, ONCOR | Maintain
MPs | MP_2014_25 | MP_BigLakeAuto_XBGL89_XBG2L89.docx | XBGL89 or XBG2L89 | AEP | Maintain
MPs | MP_2014_53 | MP_Bruni_Auto_138kV_69_XF.docx | SLAQLOB8 | STEC, AEP | Maintain
MPs | MP_2015_08 | MP_Forest_Hill_138_69_kV_XF.docx | XFHL89 | ONCOR | New
MPs | MP_2015_02 | MP_Fort_Lancaster_-_Mesa_View_Switch_138kV_line.docx | SFTLMES8 | AEP | New
MPs | MP_2015_05 | MP_Hillsboro_138_69_kV_XF.docx | XHL2S89 | ONCOR | New
MPs | MP_2015_08 | MP_Hutto_-_Rnd_Rck_Gabriel_138kV_Double_Circuit_Line_rev.docx | DHUTGAB8 | ONCOR | New
MPs | MP_2015_07 | MP_Permian_Basin_138_69_kV_Autotransformer.docx | XPB2S89 or XPB1S89 | ONCOR | New
MPs | MP_2014_22 | MP_Turtle_Creek_to_Uvalde_OR_Crystal_City_69kV.doc | SLA_UVA9 or SCRYTUR9 | AEP | Maintain
MPs | MP_2014_30 | MP_WillsPoint_XTRL89.docx | XTRL89 | ONCOR | Maintain
MPs | MP_2015_09 | MP_Wink_138_69_kV_XF_OR_Wink_TNMP_Wink_138kV_LN.docx | XWI2N89 or SWINWIN8 | TNMP | New
MPs | MP_2015_02 | SLIVGIL9_MP.doc | SLIVGIL9 & DGILFR89 | LCRA | New
MPs | MP_2014_52 | SRULASP9_MP.doc | SRULASP9, SHSKRUL9, SGILROC9 | AEP, BEPC | Maintain
MPs | MP080214-0 | SSIGSAN8_MP.doc | SSIGSAN8 | AEP | Maintain
MPs | MP_2011_08 | Valley Import.doc | Multiple | AEP, STEC, BPUB, SHARYLAND | Maintain
MPs | MP_2015_01 | XAND189_MP_rev2.doc | XAND189 | ONCOR | New
PCAPs | PCAP_2010_02 | DBIGKEN5_PCAP.doc | DBIGKEN5 | AEP | Maintain
PCAPs | PCAP_2013_03 | Elgin Switch (ELGSW) 138 69 kV Autotransformer.doc | XELG89 | ONCOR | Maintain
PCAPs | PCAP_2014_01 | FREER to LOBO 69kV.doc | SSANALI9 | ONCOR | Maintain
PCAPs | PCAP_2010_01 | LCRA Fort Mason - Yellow Jacket 138 kV Circuit.doc | SFORYLJ8 | AEP | Maintain
PCAPs | PCAP_2013_01 | LOBO to San Miguel 345kV Line or Lobo 345,138 kV Autotransformer.doc | SLOBSAN5 or XLOB58 | AEP | Maintain
RAPs | RAP_2012_01 | Allen Sw. - RoyseMonticello Double-Circuit 345 kV Line.docx | DALNRYS5 | ONCOR | Maintain
RAPs | RAP_2012_05 | Baytown Autotransformers AT1 and AT2.doc | SBTECH25 or SBTECHB5 | CALPINE | Maintain
RAPs | RAP_2012_04 | Lewisville Switch -Autotransformer 2.doc | XLWS58 | BEPC | Maintain
RAPs | RAP_2015_07 | RAP_Navarro_Limestone_Plant_345_kV_Double_Circuit_Lines.docx | DNAVLEG5 | ONCOR | New
RAPs | RAP_2015_06 | RAP_Salem_-_Fayette_Power_Plant_345kV_line.docx | SSALFPP5 | LCRA | New
RAPs | RAP_2015_08 | RAP_Salem_-_Fayette_Power_Plant_345kV.docx | DSALFA58 | LCRA | New
A Pick-list of Approved CMPs

## Slide 13
Completion
  June 1, 2015
2015 Review Highlights

## Slide 14
An Introduction to Constraint Management Plans
  What/Why, Types
Overview of the Annual CMP Review Process
  What/Why, When, Who’s involved
  Study Case, Contingency Definitions
  Criteria Used in Studies
2015 Review Summary
  Initial Details – kick off, case used, case changes
  Highlights of the Review
  A Pick-list of plans
Agenda

## Slide 15
Questions?
Nitika Mago nmago@ercot.com 512-248-6600