## Slide 1
Real-Time Co-optimization of Energy & Ancillary Services
Co-ordination of Power Balance Penalty Curve, VOLL, SWOC for AS Demand Curves

## Slide 2: RT Energy + Ancillary Service Co-Optimization
Objective is to maximize bid base revenues while minimizing offer-based costs
Constraints (some of the important ones):
  Power Balance:
    Energy MWh Awards on Supply Side = Energy Demand (GTBD)
    Supply Side Awards includes MWh from Power Balance Penalty Curve (PBPC) if any
  AS :
    AS MW/h Awards on Supply Side = AS Demand MW/h Awards on AS Demand Curve
  For each Resource (Supply Side):
    Sum of Energy MWh Award and AS MW/h Award cannot exceed its High Sustainable Limit (HSL)
    AS MW/h Award cannot exceed the AS Offer MW/h
Notes: Slide #5

## Slide 3: RT Energy + Ancillary Service Co-Optimization
Supply side energy MWh awards determined by the intersection of supply side energy offer curve and the vertical demand (GTBD) line
Supply side and demand side AS MW/h awards determined by the intersection of the supply side AS offer curve and the AS demand curve
VOLL+1
PBPC
GTBD
MWh
$/MWh
AS Demand Curve
MW/h
$/MW/h
CeneOffer
Energy Supply/Demand
intersection
AS Supply/Demand
intersection
CASOffer
CASDemand
LMP
Offer Based Costs
Bid Based Revenue
Notes: Slide #5

## Slide 4: RT Energy + Ancillary Service Co-Optimization
Points to note :
  Without congestion the maximum energy price (LMP) is set by the Power Balance Penalty Curve = VOLL+1 $/MWh
    Occurs when there is insufficient real supply to meet demand (GTBD)
  The maximum AS price (MCPC) is the highest price (bid to buy) on the AS Demand Curve
    Occurs when there is insufficient supply to meet AS demand and the AS Demand Curve sets the price (MCPC)
  Optimization maximizes the area between the supply and demand curves for energy and AS as long as constraints are satisfied
Notes: Slide #5

## Slide 5: RT Energy + Ancillary Service Co-Optimization
Points to note (continued):
  The result of the energy and AS co-optimization should be such that:
    Procurement of energy and AS from supply side must be at least cost
    Given the prices (LMP, MCPC) and the respective awards (energy, AS) to each supply side resource, the resource has the maximum revenue
    For example, if the energy price (LMP) = 60 $/MWh and AS price (MCPC) = 8 $/MW/h and the resource submitted a energy offer for 59$/MWh and AS offer for 6 $/MW/h, then the awards to this resource should be for AS as much as possible (limited by the AS Offer MW/h) and then energy (MWh)
Notes: Slide #5

## Slide 6: RT Energy + Ancillary Service Co-Optimization
Points to note (continued):
  In Real-Time, the results should be such that meeting the energy demand (GTBD) is given higher priority than meeting the AS demand
    This requires co-ordination between the maximum price (bid to buy) on the AS demand curve, System Wide Offer Cap (SWOC), Power Balance Penalty Curve and VOLL
Notes: Slide #5

## Slide 7: Example 1:
VOLL $/MWh | PBPC $/MWh | SWOC $/MWh or $/MW/h | AS Demand Curve | GTBD $/MWh | Generator Parameters |  | 
 |  |  |  |  | HSL MW | EOC | AS Offer
9000 | 9001 | 9000 | 9000 $/MW/h for 10 MW | 111 | 120 | 50 $/MWh for 120 MW | 8$/MW/h for 20 MW
9001
PBPC
GTBD=111
MWh
$/MWh
50
HSL=120
Energy Supply/Demand
MW/h
9000
8
10
20
AS Supply/Demand
Notes: Slide #5

## Slide 8: Example 1:
Generator Net Revenue per MW capacity
  Energy: LMP-EOC = 9001-50 = 8951 $/MWh
  AS: AS_MCPC-ASOffer = 8959-8 = 8951 $/MW/h
Generator indifferent to whether its capacity is procured for energy or AS
However, Power Balance is NOT met and will have to rely on deploying AS or perform load shed to achieve power balance
Desired Awards to Generator |  | Power Balance
Energy Award | AS Award | Energy Award
111 MWh | 9 MW/h | 0 MWh
Actual Award to Generator |  | Power Balance | Prices | 
Energy Award | AS Award | Energy Award | Energy LMP | AS MCPC
110 MWh | 10 MW/h | 1 MWh | 9001 | 8959
Notes: Slide #5

## Slide 9: Co Ordination of the SWOC, Power Balance Penalty Curve, VOLL and AS Demand Curve prices
If under all possible scenarios, the net revenue per MW capacity for energy is higher than the net revenue per MW capacity for AS, then, one can satisfy the requirement of giving priority to meeting energy demand (GTBD) over meeting AS demand
  LMP-EOC > AS_MCPC – ASOffer
In the extreme case:
  LMP = Power Balance Penalty = VOLL+1
  EOC = SWOC
  ASOffer = 0 $/MW/h
The upper limit on AS_MCPC (AS_MCPCmax) under these extreme conditions needs to satisfy:
  VOLL+1-SWOC > AS_MCPCmax – 0
  AS_MCPCmax = VOLL – SWOC
  This AS_MCPCmax is the maximum price on the AS Demand Curve
Notes: Slide #5

## Slide 10: Example 2:
VOLL $/MWh | PBPC $/MWh | SWOC $/MWh or $/MW/h | AS Demand Curve | GTBD $/MWh | Generator Parameters |  | 
 |  |  |  |  | HSL MW | EOC | AS Offer
9000 | 9001 | 2000 | 7000 $/MW/h for 10 MW | 111 | 120 | 50 $/MWh for 120 MW | 8$/MW/h for 20 MW
9001
PBPC
GTBD=111
MWh
$/MWh
50
HSL=120
Energy Supply/Demand
MW/h
7000
8
10
20
AS Supply/Demand
Notes: Slide #5

## Slide 11: Example 2:
Generator Net Revenue per MW capacity
  Energy: LMP-EOC = 7042-50 = 6992 $/MWh
  AS: AS_MCPC-ASOffer = 7000-8 = 6992 $/MW/h
Generator indifferent to whether its capacity is procured for energy or AS
Power Balance is met
Desired Awards to Generator |  | Power Balance
Energy Award | AS Award | Energy Award
111 MWh | 9 MW/h | 0 MWh
Actual Award to Generator |  | Power Balance | Prices | 
Energy Award | AS Award | Energy Award | Energy LMP | AS MCPC
111 MWh | 9 MW/h | 0 MWh | 7042 | 7000
Notes: Slide #5

## Slide 12: Example 3:
VOLL $/MWh | PBPC $/MWh | SWOC $/MWh or $/MW/h | AS Demand Curve | GTBD $/MWh | Generator Parameters |  | 
 |  |  |  |  | HSL MW | EOC | AS Offer
9000 | 9001 | 2000 | 7000 $/MW/h for 10 MW | 111 | 120 | 2000 $/MWh for 120 MW | 8$/MW/h for 20 MW
9001
PBPC
GTBD=111
MWh
$/MWh
2000
HSL=120
Energy Supply/Demand
MW/h
7000
8
10
20
AS Supply/Demand
Notes: Slide #5

## Slide 13: Example 3:
Generator Net Revenue per MW capacity
  Energy: LMP-EOC = 8992-2000 = 6992 $/MWh
  AS: AS_MCPC-ASOffer = 7000-8 = 6992 $/MW/h
Generator indifferent to whether its capacity is procured for energy or AS
Power Balance is met
Desired Awards to Generator |  | Power Balance
Energy Award | AS Award | Energy Award
111 MWh | 9 MW/h | 0 MWh
Actual Award to Generator |  | Power Balance | Prices | 
Energy Award | AS Award | Energy Award | Energy LMP | AS MCPC
111 MWh | 9 MW/h | 0 MWh | 8992 | 7000
Notes: Slide #5