## Slide 1
Distributed Energy Resources
Future Market Options
ERCOT Staff
DER Workshop
June 18, 2015

## Slide 2: DER Concept Paper
ERCOT Staff is committed to publishing a concept paper on Distributed Energy Resources (DERs) by third quarter of 2015
  Draft is under development
  Preliminary outline was released to ETWG in April and is posted to today’s meeting page
Today’s workshop is part of an ongoing effort by ERCOT to engage with Market Participants and solicit input
Concept paper will include:
  Potential market options for DERs
  Data Requirements
    DER mapping to ERCOT CIM from TDSPs
    Real-time or near-Real Time Resource-specific (single site or aggregations) operational data from QSEs
  Registration / Interconnection Requirements
    ERCOT
    TDSP
  Metering issues
  Settlement Mechanisms
  Forecasting tools
  Compliance metrics

## Slide 3: Defining DER
ERCOT definition of Distributed Generation (DG):
  An electrical generating facility located at a Customer’s point of delivery (point of common coupling) ten megawatts (MW) or less and connected at a voltage less than or equal to 60 kilovolts (kV) which may be connected in parallel operation to the utility system.
ERCOT definition of Distributed Renewable Generation (DRG)
  Electric generation with a capacity of not more than 2,000 kW provided by a renewable energy technology that is installed on a retail electric Customer’s side of the meter.
DER (currently undefined in ERCOT) may include:
  Technologies such as solar photovoltaic (PV), combined heat and power (CHP) or cogeneration systems, microgrids, wind turbines, microturbines, back-up generators, energy storage or any combination of such.
  Demand Response?

## Slide 4: Examples of DER definitions
EPRI:
  ….smaller power sources that can be aggregated to provide power necessary to meet regular demand.
New York ISO (from DNV GL report):
  ….behind-the-meter” power generation and storage resources typically located on an end-use customer’s premises and operated for the purpose of supplying all or a portion of the customer’s electric load.
NREL:
  ….as used in this report, refers to a variety of small, modular electricity-generating or storage technologies that are located close to the load they serve.

## Slide 5: Current ERCOT DG Rules
Registration with ERCOT
  DG greater than the 1 MW DG registration requirement
    Registration with ERCOT is required
    The resource production will be accounted for in wholesale generation settlements
  DG equal to or below the 1 MW DG registration threshold
    Registration with ERCOT is permitted, but not required
    Unregistered DG outflow is accounted for in the load aggregation process for settlements
Notes: Walk audience to ERCOT.com

## Slide 6: DG Metering - Data Collection & Data Submittal
Registered DG
  Resource Entity and TDSP agree on metering
    ERCOT Polled Settlement (EPS) Meter
      EPS Meter data will be included in initial settlements
    TDSP-Read Generation Meter
      TDSP-Read meter data will be included in settlement when data is received from the TDSP
        Typically submitted on a monthly basis
        867 Transaction (IDR Meter)
Notes: Walk audience to ERCOT.com

## Slide 7: DG Metering - Data Collection & Data Submittal
Unregistered DG
  In NOIE Territories
    Unregistered DG outflows are not submitted to ERCOT
  In Competitive areas
    Unregistered DG outflows are submitted to ERCOT by the TDSP through the Texas SET retail transaction process
      ESI ID must be assigned a DG load profile type
      AMS interval data (LSE File) or
      NIDR 867 transaction
Notes: Walk audience to ERCOT.com

## Slide 8: DG Settlement
Registered DG Settlement
  Compensated at the Load Zone Settlement Point Price (LZ SPP)
    LZ SPP is a Load-weighted average of all Locational Marginal Prices (LMPs) in a Load Zone for a given 15-minute Settlement Interval.
Unregistered DG Settlement
  NOIE Territories
    Unregistered DG outflows are accounted for by a load reduction at the NOIE boundary metering points
  Competitive areas
    Outflows are treated as negative load in the ERCOT data aggregation process (effectively compensated at LZ SPP)
    The load of the Competitive Retailer associated with the ESI ID is reduced by the amount of the outflow energy
Notes: Walk audience to ERCOT.com

## Slide 9: Metering Types
Type |  | Notes
Unidirectional | Measures consumption only | Load only (no DG)
‘Traditional’ Net metering | Single-channel non-directional. Single data point representing net Load minus net on-site generation over a billing period (could be a negative number). | Mostly disallowed by PUC Rule 25.213.
Bi-directional | Two data points for each 15-minute interval: measures net in-flow to the point of delivery (i.e., may be reduced by on-site DG), and net exports to the grid from the point of delivery. | Required by PUC Rule for investor-owned TDSPs
Dual metering | Two meters, two data points for each 15-minute interval: measures gross Load and gross generation. | Allows DSP to bill customer based on gross consumption; allows LSE to pay customer for gross generation.

## Slide 10: DERs on the horizon
More PV is coming – we just don’t know how much or how fast
30% federal solar investment tax credit:
  Residential credit expires completely 12/31/16
  Commercial credit reduces to 10% after 12/31/16
But PV prices keep plummeting….
Meanwhile, efficiency keeps improving and costs are coming down for:
  Firm backup/emergency DG
  Distribution-level storage devices
eere.doe.gov

## Slide 11: DER Energy Pricing
DERs today are settled on the applicable LZ SPP if the energy meter records a net injection into the grid (at meter location)
Applies to both:
  Injections to the grid by registered DG with QSE representation
  Negative load treatment for an unregistered DG’s Load Serving Entity
In other words, DERs today are ‘passive’ participants to prices:
  Controlled passive response – e.g. fossil fuel, PV + storage, or storage – may chase LZ SPPs
  Uncontrolled passive response – e.g., pure PV – they produce when the sun is shining

## Slide 12: Optional LMPs for DERs
If DERs were eligible to be settled on more granular pricing, then passive response could better align with grid conditions
  Higher local prices indicate local scarcity – signaling DERs to chase these prices if they are capable of doing so
DERs would need to be mapped to appropriate electrical bus(es), and settled at that electrical bus (or average of multiple buses) price
Proposed to be optional: Entity representing the DER could choose whether to get LZ SPP pricing or the locational price
If it’s the locational price, then the DER should meet further requirements:
  Telemetry or some other type of real-time or near-real-time communication to the ISO (active power, status, etc.)
  Revenue quality metering (AMI/IDR/EPS) that measures DER gross output separate from the gross load behind common service delivery point
  This is necessary to ensure compliance with PUC Rules 25.501 which requires all load in the ERCOT region to be settled at the applicable Load Zone Price

## Slide 13: DER Market Options
Type | DER Minimal | DER Light | DER Heavy
Energy Settled at: | Load Zone SPP | Price at Local electrical bus(es) | Logical Resource Node (price at Local electrical bus(es))
Energy Market Participation | Self-responding | Self-responding | SCED-dispatched
Ancillary Service Market Participation | Not eligible | Not eligible | Eligible
Aggregation Allowed? | N/A | Yes | Yes
Metering Required | Single meter OK (15-minute revenue quality) at POI | Separate (dual) metering for Generation and native Load | Separate (dual) metering for Generation and native Load
Telemetry or telemetry-light to and from ERCOT | Not required | Real-time or near real-time with multiple attributes | Real-time or near real-time with multiple attributes
COP, Outage Schedule, Offers/Bids, etc. | N/A | N/A | Required
CRR Implications | None | None | None/?

## Slide 14: Ancillary Services from DERs
DER participation in the AS markets would require new sets of market rules
  Registration
  Qualification
  Validation
  Aggregation issues – i.e., similar challenges to enabling Aggregated Load Resources (for Load Participation in SCED)
Expected growth of dispatchable DERs featuring integrated PV + storage creates challenges AND opportunities

## Slide 15: DER interconnections
Regions that have experienced high DER penetration have found it necessary to adopt a common set of interconnection requirements
  Germany, Hawaii, and California have either adopted or are in the process of adopting common set of requirements for distributed PV (smart inverter).
  As an example, the requirements for a DER installation could include:
    Two-way communication/control between DER and remote entity
    Anti-Islanding Protection
    Low and High Voltage Ride-Through
    Low and High Frequency Ride-Through
    Dynamic Volt-Var Operation
    Ramp Rates
    Fixed Power Factor
    Soft Start Reconnection
Should there be a common set of DER interconnection requirements in the ERCOT Region?

## Slide 16: DER Operational Issues
ERCOT Demand/Load Forecasting
  What should ERCOT be forecasting?
    Net load forecast only -- i.e., net load forecast would incorporate DER impacts
    Net load forecast and DER forecast separately -- provide information on both for planners, developers, grid operators and markets
    Impact of storage on forecasting both net load and DER – this is a challenge that needs to be addressed if there is significant adoption of this technology
  Currently ERCOT has a project to forecast Solar PV for utility scale (transmission connected) installations, but not distributed solar

## Slide 17: DER Operational Issues
Should ERCOT’s Capacity, Demand & Reserve reports account for DERs and also include forecasted DER growth?
  CDR provides important information on expected reserves, reserve margins, and is closely monitored by market participants
How should ERCOT take into account impact of DER on Operations planning (Outage coordination, Resource availability planning, etc.) ?
  Should transmission outage approval process include potential impact of expected DERs? Is net load forecast sufficient?
  What other operational procedures need to include potential impact of expected DERs?
    Reliability Unit Commitment (RUC) process?
    Others?

## Slide 18: Next Steps
ERCOT recommends that stakeholders provide written comments on today’s presentation and discussion
  Please provide by Friday, July 10 to paul.wattles@ercot.com and sainath.moorty@ercot.com
ERCOT will ask TAC for guidance on the appropriate forum for future DER discussions
Concept paper to be posted in September

## Slide 19: Questions?

## Slide 20
APPENDIX
Notes: Walk audience to ERCOT.com

## Slide 21: Topics
Nomenclature
DG Registration Requirements
Metering, Data Collection and Data Submittal
DG Settlements
Unregistered DG Report
Interconnection Issues
Impacts on ISO Operations
Notes: During this presentation I will cover the following:

## Slide 22: Nomenclature
ERCOT Protocol Terms
Customer
  An Entity that purchases electricity for its consumption.
Service Delivery Point
  The specific point on the system where electricity flows from the TSP or DSP to a Customer.
Electric Service Identifier (ESI ID)
  The basic identifier assigned to each Service Delivery Point used in the registration and settlement systems managed by ERCOT or another Independent Organization.
Premise
  A Service Delivery Point or combination of Service Delivery Points that is assigned a single ESI ID for Settlement and registration.

## Slide 23: Nomenclature
ERCOT Protocol Terms (continued)
Distributed Generation (DG)
  An electrical generating facility located at a Customer’s point of delivery (point of common coupling) ten megawatts (MW) or less and connected at a voltage less than or equal to 60 kilovolts (kV) which may be connected in parallel operation to the utility system.
Distributed Renewable Generation (DRG)
  Electric generation with a capacity of not more than 2,000 kW provided by a renewable energy technology that is installed on a retail electric Customer’s side of the meter.
Telemetry for typical ISO requirements
  Real-Time information of active, reactive power, voltage, current, frequency, switch status, etc. Typically data refreshed in a 2 second cycle

## Slide 24: Unregistered DG Report
2015 1st Quarter Un-Registered DG Report - LZ Summary |  |  | 
Load Zone | Aggregate MW | kWh exported to the grid during the prior 12 months | 
LZ_AEN | 4.64 | 1,109,442 | 
LZ_CPS | 0.226 | 13,889 | 
LZ_HOUSTON | 1.15289 | 594,966 | 
LZ_NORTH | 6.855145 | 1,806,961 | 
LZ_SOUTH | 3.22531 | 889,070 | 
LZ_WEST | 0.94248 | 554,103 | 
NOTE1: Current DG registration threshold = 1MW |  |  | 
NOTE2: Report includes un-registered DG above 50kW and equal to or below ________the DG threshold |  |  | 
NOTE3: Installed capacity limit per load zone = 10 MW |  |  | 
Notes: Walk audience to ERCOT.com