## Slide 1: PLWG Report to ROS
July 9, 2014

## Slide 2: PGRRs needing vote
PGRR043 – FIS Scoping Amendment
  PGRR043 moves the Subsynchronous Resonance (SSR) Study out of the Full Interconnect Study (FIS) and makes it a requirement for initial synchronization
  Aligns FIS procedures with IEs business practices and lowers the probability of SSR restudies
  PLWG has agreed on current language as in the 6/22/2015 PLWG report
  IA is no impact
  Recommended action is to approve PGRR043

## Slide 3: PGRRs needing vote
PGRR044 – MIS Classification of GINR Study Information
  PGRR044 changes the MIS classification of certain studies in the GINR process. Requires ERCOT to post the security screening study and the steady state, system protection and facility studies out of the TSP FIS studies
  FIS Dynamic Studies will be posted to the Certified area of the MIS for TSPs only
  PLWG has agreed on current language as in the 6/22/2015 PLWG report
  IA of less than $5k and will be absorbed in O&M
  Recommended action is to approve PGRR040

## Slide 4: CDR/Planning Model White Paper
Assigned to PLWG in July 2014
Describe the load and generation assumption methodologies utilized in the CDR and transmission planning models
Explain why different assumption methodologies may be appropriate for certain assumptions
Identify assumptions where it may be appropriate to eliminate the differences

## Slide 5: CDR/Planning Model White Paper - Purpose
 | CDR Report | Transmission Planning Models |  | 
 |  | SSWG Models | RTP Reliability Models | RTP Economic Models
Purpose | Provide an estimate of the planning reserve margin during summer and winter peak load seasons | Provide a range of power flow cases with a common reference point for ERCOT and Market Participants | Provide power flow cases for use in developing the reliability portion of the ERCOT Regional Transmission Plan (RTP) | Provide a power flow case for use in developing the economic assessment portion of the ERCOT Regional Transmission Plan (RTP)

## Slide 6: CDR/Planning Model White Paper – Load Assumptions
 | CDR Report | Transmission Planning Models |  | 
 |  | SSWG Models | RTP Reliability Models | RTP Economic Models
Preparer | ERCOT | TSPs | ERCOT and TSPs | ERCOT
Season | Summer and Winter | Four seasons for current year Summer peak for next 6 years Minimum load and high wind for a future year | Summer peak for future Years 1, 3, 5, and 6 | Full year hourly analysis for Future Years 3 and 6
Weather Assumptions | Average weather (expect actual load to exceed forecast one out of two years) | Varies by TSP, see Appendix A | Higher of: Summed TSP SSWG case loads in each weather zone; or ERCOT 90th percentile forecast by weather zone (expect actual load to exceed forecast one out of ten years) | “Average” weather in each weather zone (expect actual load to exceed forecast one out of two years)
Load Coincidence | Coincident (single peak load hour for ERCOT Region) | Based on ALDR forecast, TSPs use varied methods for populating loads by individual substation (see Appendix A for description by TSP) | Peak load by individual substation for each weather zone (non-coincident), with exceptions made depending on the case | Non-Coincident by weather zone
Load Resource and other Demand Response Programs | Included (shown as separate line item) | Not Included | Not included | Not Included
Self-Serve Load | Net to the grid (self-serve load minus self-serve generation) | Gross (no reduction for self-serve generation) | Gross (no reduction for self-serve generation) | Gross (no reduction for self-serve generation)
Load Adjustments | None | No adjustments from TSP provided loads are made | Within a region of study the higher of: SSWG load in each weather zone or ERCOT 90th percentile load forecast by weather zone Adjustments may be made outside of study region | None

## Slide 7: CDR/Planning Model White Paper – Generation Assumptions
 | CDR Report | Transmission Planning Models |  | 
 |  | SSWG Models | RTP Reliability Models | RTP Economic Models
Preparer | ERCOT | TSPs | ERCOT and TSPs | ERCOT
Extraordinary Dispatch Methods – a method of adding capacity to a model | Not applicable | As needed, see Appendix B of SSWG manual. Has been used for years 4, 5, and 6 in recent years | Yes, a combination of extraordinary dispatch and load scaling outside of the region being studied may occur | Not applicable
Thermal Generation | Seasonal Net Maximum Sustainable MW Rating from RARF | Seasonal Net Maximum Sustainable MW Rating from RARF and Reactive curve gross MVAR less auxiliary Load MVAR Ratings from RARF | Seasonal Net Maximum Sustainable MW Rating from RARF and Reactive curve gross MVAR less auxiliary Load MVAR Ratings from RARF | Seasonal Net Maximum Sustainable MW Rating from RARF
Wind Generation | Capacity contribution based on average of recent peak-season output (top 20 load hours) | 100% of capacity modeled. Units dispatched according to CDR Report unless needed in extraordinary dispatch | 100% of capacity modeled. Units dispatched at varying levels, depending on the case | Units dispatched based on representative hourly patterns appropriate for weather assumptions
Solar Generation | 100% of capacity reported | 100% of capacity modeled. Units dispatched based on review of historic seasonal output | 100% of capacity modeled. Units dispatched at 70% of capacity | Units dispatched based on representative hourly patterns appropriate for weather assumptions; using vendor profiles
DC-Ties | Output levels based on average of recent peak-season output (top 20 load hours) | 100% of capacity modeled. Units dispatched based on review of historic seasonal operating levels | 100% of capacity modeled. Units dispatched based on review of historic seasonal operating levels | Units dispatched based on historical hourly patterns

## Slide 8: CDR/Planning Model White Paper – Generation Assumptions Cont.
 | CDR Report | Transmission Planning Models |  | 
 |  | SSWG Models | RTP Reliability Models | RTP Economic Models
Preparer | ERCOT | TSPs | ERCOT and TSPs | ERCOT
Hydro Generation | Output levels based on average of recent peak-season output (top 20 load hours) | 100% of capacity modeled. Units modeled offline | 100% of capacity modeled. Units modeled offline | Units dispatched based on historical hourly patterns
Requirements for Including Planned Generation | Signed interconnection agreement; Air permits (if needed); and Cooling water attestation | Planning Guide 6.9. Signed interconnection agreement; Air permits (if needed); Cooling water attestation; and Full financial commitment and notice to proceed given to TSP | Planning Guide 6.9. Signed interconnection agreement; Air permits (if needed); Cooling water attestation; and Full financial commitment and notice to proceed given to TSP | Planning Guide 6.9. Signed interconnection agreement; Air permits (if needed); Cooling water attestation; and Full financial commitment and notice to proceed given to TSP
Self-Serve Generation | Net to grid during peak hours of recent peak season | Full capacity available | Full capacity available | Full capacity available
Switchable Units | Capacity contracted to other region is not included | Capacity contracted to other region is considered unavailable | Capacity contracted to other region is considered unavailable | Capacity contracted to other region is considered unavailable
Mothball Generation | Capacity is included if unit owner states likelihood of return is greater than 50% | Designated as a mothball unit and status set to “out-of-service” unless needed for extraordinary dispatch | Mothball units not available (new for 2015 as a result of TPL-001-4) | Mothball units not available

## Slide 9: CDR/Planning Model White Paper - Recommendations
In the CDR, make a clear delineation which resources have met Planning Guide 6.9 requirements and which have not and lack only financial commitment
RTP Reliability Models should match CDR for calculating hydro-electric unit dispatch
SSWG base case models and RTP Reliability Models should adopt the methodology for DC tie import/export levels utilized in the CDR

## Slide 10: CDR/Planning Model White Paper – Recommendations Cont.
For extraordinary dispatch for SSWG base case models and RTP Reliability Models, wind generation output level should be consistent with the CDR
As more solar is developed, consistency between the CDR and Planning Models should be reviewed and modified, if necessary

## Slide 11: CDR/Planning Model White Paper
Vote accepting the White Paper?
Vote to rectify the inconsistencies between the CDR and Planning Models?

## Slide 12: PGRRs under review
PGRR042 – Regional Transmission Plan Model Reserve Requirement and Load-Generation Imbalance Methodology
PGRR045 – Alignment with NPRR705, Provides Consistency for References to the End Date of the Generation Interconnection Process

## Slide 13: Assignments to PLWG
Generation Deliverability Criteria
  ERCOT staff is working on draft PGRR language for consideration.