## Slide 1
Long-Term Load Forecasting
Calvin Opheim
ERCOT
Manager, Forecasting & Analysis
LTSA Scenario Development Workshop
July 14, 2015

## Slide 2: Outline of Today’s Presentation
Forecasting Framework
Model Data Input
LTSA Load Forecasting Scenarios

## Slide 3: Weather Zones

## Slide 4: Forecasting Framework
Premise Models
  Forecasted premise counts are used as the driver of future demand/energy growth
Daily Energy Models
Hourly Models
  Allocate daily energy forecast into a hourly forecast
Ensemble Approach
  Developing a suite of forecast methods for further study

## Slide 5: Model Data Input
Load Values
  ERCOT uses hourly load values
  Result is an 8,760 hour load forecast for each year

## Slide 6: Model Data Input
Weather Data
  Cooling Degree Days
  Heating Degree Days
  Calculated for the entire day, part of a day (like morning, afternoon, evening, and night)
  May also include values from a previous day(s)
Two or three weather stations located in each weather zone

## Slide 7: Model Data Input
Calendar
  Month
  Season
  Day of the week
  Holidays
  Daylight minutes

## Slide 8: Model Data Input
Monthly Economic Measures
  Non-farm employment
  Population
  Housing stock
  Households
  Other measures (GDP, GSP, etc)
Data Availability
  County level
  Counties are mapped into a weather zone
Growth Driver in Demand and Energy Models

## Slide 9: Model Data Input
Monthly Premise Count by Customer Class
  Instead of using economic measures, use the actual number of premises for each customer class
  Customer class is determined by the load profile assignment
  Three classes
    Residential (includes lighting)
    Commercial
    Industrial
Requires a Premise Forecast
Requires Average Use per Premise per Customer Class

## Slide 10: Model Data Input – Premise forecast
Monthly Economic Measures
  Non-farm employment
  Population
  Housing stock
  Households
  Other measures (GDP, GSP, etc)
Premise Forecast
  ERCOT also uses the monthly economic data to forecast the number of premises within a customer class

## Slide 11: Model Data Input
The number of premises is used as an input in the Demand and Energy forecast model(s)
The average use per premise is also included as input
Both of the above are combined into a weighted premise index variable which is used in the Demand and Energy forecast model(s)

## Slide 12
LTSA - Load Forecast Scenarios

## Slide 13: Scenarios
Created by post forecast adjustments
  ERCOT’s official Long-Term Load Forecast output is adjusted outside of the model to reflect the load as defined by the scenario
Base scenario is referred to as Current Trends
Current Trends scenario would include the following adjustments to ERCOT’s official Long-Term Load Forecast
  Increased load in the Coast weather zone for LNG of ~ 700 MW
  Adjustments for Energy Efficiency and Demand Response
  Possible load reduction in North Central weather zone

## Slide 14: Scenarios
Variables available in scenario development
  Premise growth rate
  Economic variables growth rate (Economic vendor developed scenarios)
  Energy Efficiency, Demand Response, Price Responsive Load MW
  Roof-top PV MW
  LNG or other large industrial MW
  etc ..
Goal is to capture a wide range of possible future load levels

## Slide 15: Questions