## Slide 1
Cost-Benefit Analysis of ERCOT’s Future Ancillary Services
Draft Study Assumptions
ERCOT Technical Advisory Committee
Sam Newell
Pablo Ruiz
Rebecca Carrol
Will Gorman
July 30, 2015
PRESENTED TO
PRESENTED BY

## Slide 2: Study Design
  Objective: evaluate the net benefits of ERCOT’s FAS proposal
  Tools: PLEXOS, modeling DA market as a single zone
  Evaluation metrics: total resource cost savings (TRC), where
    TRC = production cost savings - incremental capital costs - implementation cost, and
    Production cost savings includes avoided fuel, VOM, startup and capacity bid costs
*Current Trends and Stringent Environmental scenarios based on 2024 Long Term System Assessment (LTSA) – see slides 5 and 6 for details

## Slide 3: Supply and Demand Assumptions
Notes:
1) Hourly shapes for Load, Wind, and Solar profiles are taken from 2010 actual profiles
2) Peak Load and Capacities include PUN Load and Pun Capacities

## Slide 4: Thermal Unit Characteristics
*CCs modeled as single trains, with duct burners modeled separately (with operations tied to parent CC) and not able to provide AS
Online non-spin capabilities not shown here because capabilities vary with each unit’s hourly output vs. HSL (and ramp rates)

## Slide 5: Provision of FAS Products
Product | Resources that Can Provide It
Regulation—4 products | Same as under CAS
FFR1 (59.8 Hz, limited duration) | Batteries, flywheels, loads with short duration
FFR2 (59.7 Hz, longer duration) | Existing Load Resources + new ones
PFR | Same as those providing Gen RRS under CAS; potentially wind
CRS1 (dispatchable 10-min) | Any online/offline gen, dispatchable load
CRS2 (manual 10-min) | Existing and new Load Resources, DG
SRS1 (dispatchable 30-min) | Any online/offline gen, dispatchable load
SRS2 (manual 30-min) | Existing and new Load Resources, DG

## Slide 6: Current Trends Scenario
Assumptions are Consistent with the LTSA Scenario
  Conditions existing today will generally continue into the future
  ERCOT’s base case load forecast with the addition of small amounts LNG
  Natural gas prices increase slowly to $5.93/mmBtu by 2024
  No changes to environmental regulations
  Trends in capital cost for new resources are increasing at GDP with the exception of Solar PV which is declining thru the planning period
  Modest increase in penetration of demand response
  No specified reserve margin; generator additions for conventional and renewable resources based on economics only
  No PTC

## Slide 7: Stringent Environmental Scenario
Assumptions are Consistent with the LTSA Scenario
  Current Trends load forecast adjusted for 1,200 MW Solar DG by 2024
  Current Trends NG forecast increased $1.50/mmBtu each year
  Costs for SO2, NOx, and CO2 added
  PTC and ITC added to Wind and Solar expansion
  Demand response increased 3% per year over Current Trends
  DC Ties increased 3,000 MW to represent new connections to external ERCOT markets