## Slide 1
Environmental Regulations Overview
Dana Lazarus
Planning Analyst, ERCOT
July 29, 2015

## Slide 2: Environmental Regulations
Mercury and Air Toxics Standards (MATS)
Regional Haze Federal Plan
Clean Water Act Section 316(b)
Ash Disposal Rule
Clean Power Plan
Cross-State Air Pollution Rule (CSAPR)
April 2015
January 2015
2018-2020**
2018-2022
2015-2018*
2020-2029; 2030
Compliance Date:
Addresses cross-state air pollution through a cap and trade program
Sets limits on hazardous air pollutant emissions at power plants
Requires controls on air emissions to improve visibility in national parks
Requires controls to limit impacts to aquatic life at cooling water intake structures
Sets carbon dioxide emissions limits for existing units
Places requirements on disposal of coal ash
*Longer timeframes for facilities required to close. Does not include the proposed Steam Electric Effluent Limitation Guidelines (ELG) rule.
**Subject to timing of final rule
Coal units
Natural gas units
Costs to:
Color key:
No or low costs
Moderate costs
High Costs
There are several proposed and recently finalized environmental regulations that could impact grid reliability in ERCOT:

## Slide 3: Cross-State Air Pollution Rule
Mercury and Air Toxics Standards (MATS)
Regional Haze Federal Plan
Clean Water Act Section 316(b)
Ash Disposal Rule
Clean Power Plan
Cross-State Air Pollution Rule (CSAPR)
April 2015
2018-2020**
2018-2022
2015-2018*
2020-2029; 2030
Compliance Date:
*Longer timeframes for facilities required to close. Does not include the proposed Steam Electric Effluent Limitation Guidelines (ELG) rule.
**Subject to timing of final rule
Coal units
Natural gas units
Costs to:
Addresses cross-state air pollution through a cap and trade program
January 2015
Status | Compliance Requirements | Next Milestone
Final rule | Purchase allowances, upgrade controls, or reduce production to comply | Litigation pending at U.S. Court of Appeals
Color key:
No or low costs
Moderate costs
High Costs

## Slide 4: Mercury and Air Toxics Standards
Mercury and Air Toxics Standards (MATS)
Regional Haze Federal Plan
Clean Water Act Section 316(b)
Ash Disposal Rule
Clean Power Plan
Cross-State Air Pollution Rule (CSAPR)
April 2015
2018-2020**
2018-2022
2015-2018*
2020-2029; 2030
Compliance Date:
*Longer timeframes for facilities required to close. Does not include the proposed Steam Electric Effluent Limitation Guidelines (ELG) rule.
**Subject to timing of final rule
Coal units
Natural gas units
Costs to:
Sets limits on hazardous air pollutant emissions at power plants
Several units in ERCOT have compliance extensions to April 2016
January 2015
Status | Compliance Requirements | Next Milestone
Final rule | Install control technologies to comply (e.g., activated carbon injection) | Case sent back to U.S. Court of Appeals
Color key:
No or low costs
Moderate costs
High Costs

## Slide 5: Ash Disposal Rule
Mercury and Air Toxics Standards (MATS)
Regional Haze Federal Plan
Clean Water Act Section 316(b)
Ash Disposal Rule
Clean Power Plan
Cross-State Air Pollution Rule (CSAPR)
April 2015
2018-2020**
2018-2022
2015-2018*
2020-2029; 2030
Compliance Date:
*Longer timeframes for facilities required to close. Does not include the proposed Steam Electric Effluent Limitation Guidelines (ELG) rule.
**Subject to timing of final rule
Coal units
Natural gas units
Costs to:
Regulates disposal of coal ash in impoundments and landfills
Steam-Electric Effluent Limitation Guidelines is related rulemaking
January 2015
Status | Compliance Requirements | Next Milestone
Final rule | Requirements for siting, design, post-closure care, groundwater monitoring, etc. | Compliance
Color key:
No or low costs
Moderate costs
High Costs

## Slide 6: Regional Haze
Mercury and Air Toxics Standards (MATS)
Regional Haze Federal Plan
Clean Water Act Section 316(b)
Ash Disposal Rule
Clean Power Plan
Cross-State Air Pollution Rule (CSAPR)
April 2015
2018-2020**
2018-2022
2015-2018*
2020-2029; 2030
Compliance Date:
*Longer timeframes for facilities required to close. Does not include the proposed Steam Electric Effluent Limitation Guidelines (ELG) rule.
**Subject to timing of final rule
Coal units
Natural gas units
Costs to:
Requires controls on air emissions to improve visibility in national parks
January 2015
Status | Compliance Requirements | Next Milestone
Proposed rule | Certain coal-fired units would be required to upgrade or install scrubbers | Final rule (projected Dec. 2015)
Color key:
No or low costs
Moderate costs
High Costs

## Slide 7: Regional Haze Affected Units in ERCOT
Big Brown 1, 2
Sandow 4
Limestone 1, 2
Coleto Creek
San Miguel
Martin Lake 1, 2, 3
Monticello 1, 2
Monticello 3

## Slide 8: Cooling Water Intake Structures Rule
Mercury and Air Toxics Standards (MATS)
Regional Haze Federal Plan
Clean Water Act Section 316(b)
Ash Disposal Rule
Clean Power Plan
Cross-State Air Pollution Rule (CSAPR)
April 2015
2018-2020**
2018-2022
2015-2018*
2020-2029; 2030
Compliance Date:
*Longer timeframes for facilities required to close. Does not include the proposed Steam Electric Effluent Limitation Guidelines (ELG) rule.
**Subject to timing of final rule
Coal units
Natural gas units
Costs to:
Requires controls to limit impacts to aquatic life at cooling water intake structures
January 2015
Status | Compliance Requirements | Next Milestone
Final rule | Install or upgrade modified traveling screens and fish return systems | Compliance
Color key:
No or low costs
Moderate costs
High Costs

## Slide 9: Clean Power Plan
Mercury and Air Toxics Standards (MATS)
Regional Haze Federal Plan
Clean Water Act Section 316(b)
Ash Disposal Rule
Clean Power Plan
Cross-State Air Pollution Rule (CSAPR)
April 2015
2018-2020**
2018-2022
2015-2018*
2020-2029; 2030
Compliance Date:
*Longer timeframes for facilities required to close. Does not include the proposed Steam Electric Effluent Limitation Guidelines (ELG) rule.
**Subject to timing of final rule
Coal units
Natural gas units
Costs to:
Sets carbon dioxide emissions limits for existing sources
EPA separately proposed emissions limits for new/modified sources
January 2015
Status | Compliance Requirements | Next Milestone
Proposed rule | Uncertain, but likely to result in significant reductions in output from coal units | Final rule (projected summer 2015)
Color key:
No or low costs
Moderate costs
High Costs

## Slide 10: Ozone National Ambient Air Quality Standards
Mercury and Air Toxics Standards (MATS)
Regional Haze Federal Plan
Clean Water Act Section 316(b)
Ash Disposal Rule
Clean Power Plan
Cross-State Air Pollution Rule (CSAPR)
April 2015
2018-2020**
2018-2022
2015-2018*
2020-2029; 2030
Compliance Date:
*Longer timeframes for facilities required to close. Does not include the proposed Steam Electric Effluent Limitation Guidelines (ELG) rule.
**Subject to timing of final rule
Coal units
Natural gas units
Costs to:
Would tighten the national ozone standard
Not shown in timeline; potential impacts would begin in early/mid 2020s
January 2015
Status | Compliance Requirements | Next Milestone
Proposed rule | Potential requirements for additional emissions controls; tightening of CSAPR | Final rule (projected Oct. 2015)
Color key:
No or low costs
Moderate costs
High Costs

## Slide 11: Current ERCOT Fleet
SCR = Selective catalytic reduction
SNCR = Selective non-catalytic reduction

## Slide 12: Capacity at Risk from CSAPR and Regional Haze

## Slide 13
CREZ Reactive Study
Questions?