## Slide 1
ORDC Curve Discussion
ERCOT
QSE Managers Working Group
9/4/2015

## Slide 2: Discussion Outline
Review of Loss of Load Probability
  Review of years used for the Mu and Sigma calculation
  Review of hourly blocks and seasons
  Data used for Mu and Sigma calculation
6.5.7.3 Security Constrained Economic Dispatch
  (14) At the end of each season, ERCOT shall determine the ORDC for the same season in the upcoming year, based on historic data using the ERCOT Board-approved methodology for implementing the ORDC. Annually, ERCOT shall verify that the ORDC is adequately representative of the loss of Load probability for varying levels of reserves. Twenty days after the end of the Season, ERCOT shall post the ORDC for the same season of the upcoming year on the MIS Public Area.

## Slide 3: Years used in Mu and Sigma calculations
If the methodology to calculate the Mu and Sigma stays the same then over time the curve change year over year will be very small

## Slide 4: Seasons and Hour Blocks used for Mu and Sigma
Anytime blocks of data are used
  The high intervals will be lowered
  The low intervals will be raised
  Block to block, Identical system conditions can have different ORDC price
    Same with season to season and the combination of the two
    This will happen inherently no matter how small or large the blocks are
    Potential Hour to Hour difference can be reduced the smaller the time blocks
    The smaller the time blocks the more data is required for representative results
    Would a blended value give more stable results?
Hour Ending | Hour_block
1 | 1
2 | 1
3 | 2
4 | 2
5 | 2
6 | 2
7 | 3
8 | 3
9 | 3
10 | 3
11 | 4
12 | 4
13 | 4
14 | 4
15 | 5
16 | 5
17 | 5
18 | 5
19 | 6
20 | 6
21 | 6
22 | 6
23 | 1
24 | 1
25 | 1
Month | Season
1 | WINTER
2 | WINTER
3 | SPRING
4 | SPRING
5 | SPRING
6 | SUMMER
7 | SUMMER
8 | SUMMER
9 | FALL
10 | FALL
11 | FALL
12 | WINTER

## Slide 5: Seasons and Hour Blocks used for Mu and Sigma
LOLP Distribution as of March |  |  | 
season | hour_block | mean | sd
WINTER | 1 | -166.75 | 1283.26
WINTER | 2 | 76.97 | 1194.47
WINTER | 3 | -158.03 | 1555.81
WINTER | 4 | -705.62 | 1535.97
WINTER | 5 | -417.76 | 1402.66
WINTER | 6 | -287.31 | 1138.72
97 Hourly Curves; smoothed within the seasons LOLP Distribution as of March |  |  |  |  |  | 
season | hour_block | mean | sd | Hour Block | Factor | Block Hour
WINTER | 1 | -105.82 | 1261.06 | 1 | 0.75 | 3
WINTER | 2 | -44.89 | 1238.87 | 1 | 0.5 | 4
WINTER | 3 | -44.89 | 1238.87 | 2 | 0.5 | 1
WINTER | 4 | 16.04 | 1216.67 | 2 | 0.75 | 2
WINTER | 5 | 18.22 | 1284.81 | 2 | 0.75 | 3
WINTER | 6 | -40.53 | 1375.14 | 2 | 0.5 | 4
WINTER | 7 | -40.53 | 1375.14 | 3 | 0.5 | 1
WINTER | 8 | -99.28 | 1465.48 | 3 | 0.75 | 2
WINTER | 9 | -294.93 | 1550.85 | 3 | 0.75 | 3
WINTER | 10 | -431.83 | 1545.89 | 3 | 0.5 | 4
WINTER | 11 | -431.83 | 1545.89 | 4 | 0.5 | 1
WINTER | 12 | -568.72 | 1540.93 | 4 | 0.75 | 2
WINTER | 13 | -633.66 | 1502.64 | 4 | 0.75 | 3
WINTER | 14 | -561.69 | 1469.32 | 4 | 0.5 | 4
WINTER | 15 | -561.69 | 1469.32 | 5 | 0.5 | 1
WINTER | 16 | -489.73 | 1435.99 | 5 | 0.75 | 2
WINTER | 17 | -385.15 | 1336.68 | 5 | 0.75 | 3
WINTER | 18 | -352.54 | 1270.69 | 5 | 0.5 | 4
WINTER | 19 | -352.54 | 1270.69 | 6 | 0.5 | 1
WINTER | 20 | -319.92 | 1204.71 | 6 | 0.75 | 2
WINTER | 21 | -257.17 | 1174.86 | 6 | 0.75 | 3
WINTER | 22 | -227.03 | 1210.99 | 6 | 0.5 | 4
WINTER | 23 | -227.03 | 1210.99 | 1 | 0.5 | 1
WINTER | 24 | -257.17 | 1174.86 | 1 | 0.75 | 2
In this example Hour Block 4 values would become 4 separate hourly values with
  Hours 1 and 2 of the block smoothing with the previous hour block
  Hours 3 and 4 of the block smoothing with the next hour block

## Slide 6
QUESTIONS / COMMENTS???

## Slide 7: Appendix

## Slide 8: Mu and Sigma Posting
The Summer 2016 (effective 6/1/2016) values will be posted in September
    http://www.ercot.com/mktinfo/rtm/index.html
The Mu and Sigma values will be recomputed using most recently approved methodology; NPRR 710 Approved on August 11, 2015

## Slide 9: Mu and Sigma Posting Calendar
6.5.7.3 Security Constrained Economic Dispatch
  (14) At the end of each season, ERCOT shall determine the ORDC for the same season in the upcoming year, based on historic data using the ERCOT Board-approved methodology for implementing the ORDC. Annually, ERCOT shall verify that the ORDC is adequately representative of the loss of Load probability for varying levels of reserves. Twenty days after the end of the Season, ERCOT shall post the ORDC for the same season of the upcoming year on the MIS Public Area.
The historical data will be recomputed using most recently approved methodology
  This means if there are to be changes they need to be made >=9 months before change is to take effect
Values are posted 9 months prior to being used by SCED (e.g. Summer 2016 posted Sep-2015 and used on Jun-2016)