## Slide 1: RUC for AS If the Resource “opts out” of the RUC does it impact the obligation to provide AS?
It shouldn’t, but Protocols are not clear

## Slide 2: Definitions
Reliability Unit Commitment (RUC)
A process to ensure that there is adequate Resource capacity and Ancillary Service capacity committed in the proper locations to serve ERCOT forecasted Load.
Reliability Unit Commitment (RUC) Buy-Back Hour
An Operating Hour for which a QSE with a Resource that is not an RMR Unit that has been committed to come On-Line by a RUC process or Verbal Dispatch Instruction (VDI) may choose, at its sole discretion, to self-commit that Resource in lieu of the RUC instruction or VDI.
Reliability Unit Commitment (RUC)-Committed Hour
An Operating Hour for which a RUC has committed a Resource to be On-Line and the QSE has not designated a RUC Buy-Back Hour.
Reliability Unit Commitment (RUC)-Committed Interval
A Settlement Interval for which there is a RUC instruction to commit a Resource.

## Slide 3: 5.5.2 (10)
  A QSE that has one or more of its Resources RUC-committed to provide Ancillary Services must increase its Ancillary Service Supply Responsibility by the total amount of RUC-committed Ancillary Service quantities. The QSE may only use a RUC-committed Resource to meet its Ancillary Service Supply Responsibility during that Resource’s RUC-Committed Interval if the Resource has been committed by the RUC process to provide Ancillary Service. The QSE shall indicate the exact amount and type of Ancillary Service for which it was committed as the Resource’s Ancillary Service Resource Responsibility and Ancillary Services Schedule for the RUC-Committed Intervals for both telemetry and COP information provided to ERCOT. Upon deployment of the Ancillary Services, the QSE shall adjust its Ancillary Services Schedule to reflect the amounts requested in the deployment.
  If a Resource opts out of its RUC instruction is it still a “RUC-committed Resource”? Does it have “RUC-Committed Intervals”?

## Slide 4: Related Issues
Clarify instructions from ERCOT – specify AS details in RUC? Separate AS and RUC instructions? Seems there is room for improvement here.
Other thoughts to improve this process:
  SASM after RUC?
  Min(DAM MCPC, SASM MCPC) -> RUC for AS?