## Slide 1
Settlement Changes
R5 (SEP 2015) and R5.5 (OCT 2015)
Blake Holt
ERCOT
COPS
9/14/2015

## Slide 2: R5 - NPRR 701- As-Built Clarification of NPRR589, Ancillary Service Offers in the Supplemental Ancillary Services Market
6.7.2 Charges for Ancillary Service Capacity Replaced Due to Failure to Provide
(1)
(a-d) The total charge of failure on Ancillary Service Supply Responsibility for xx by QSE, if applicable:
xxFQAMTQSETOT q = xxFQAMT q + RxxFQAMT q
Where:
xxFQAMT q = ( Max m (MCPCxxm) * xxFQ q)
RxxFQAMT q = MCPCxx rs * RxxFQ q, rs
6.7.3 Adjustments to Cost Allocations for Ancillary Services Procurement
(2-5)
(a) xxCOSTTOT = (-1) *( ( RTPCxxAMTTOT m) + PCxxAMTTOT + xxFQAMTTOT)
Where:
Total payment of SASM and RSASM-procured capacity for xx by market
RTPCxxAMTTOT m = RTPCxxAMT q, m
Total payment of DAM-procured capacity for xx
PCxxAMTTOT = PCxxAMT q
Total charge of failure on Ancillary Service Supply Responsibility for xx
xxFQAMTTOT = xxFQAMTQSETOT q
Total payment of SASM- and RSASM-procured capacity for xx by QSE
RTPCxxAMTQSETOT q = RTPCxxAMT q, m
Max of all markets, including RSASM

## Slide 3: R5 - NPRR 701- As-Built Clarification of NPRR589, Ancillary Service Offers in the Supplemental Ancillary Services Market
6.7.3 Adjustments to Cost Allocations for Ancillary Services Procurement
(2-5)
(b) Each QSE’s share of the net total costs for Reg-Up for the Operating Hour is calculated as follows:
xxCOST q = xxPR * xxQ q
Where:
    xxPR = xxCOSTTOT / xxQTOT
    xxQTOT = RUQ q
    xxQ q = RUO q – SARUQ q
    xxO q = (SAxxQ q + (RTPCxx q, m) + PCxx q – xxRP q – xxFQ q – RxxFQ q) * HLRS q + xxRP q
    SAxxQ q = DASxxQ q + RTSAxxQ q

## Slide 4: R5.5 – NPRR 706- Restore the ability to use Physical Responsive Reserve Capability as an Indicator of Available Frequency-Responsive Capacity
“The improvement will be to use available Non-Frequency Responsive Capacity (NFRC) telemetry to adjust the PRC and remove the non-responsive reserves from the PRC calculation. The proposed changes will allow ERCOT to accurately count the available PRC reserves during all conditions and especially during EEAs when Responsive Reserve (RRS) capacity is released to SCED.”
  PRC1 = Min(Max((RDF*(HSL-NFRC) – Actual Net Telemetered Output)i , 0.0) , 0.2*RDF*(HSL –NFRC)i)
This NPRR does not affect the settlement system.

## Slide 5: R5.5 - NPRR 710- Removal of ORDC Phase 2 Language and Modification to HASL Calculation
“This Nodal Protocol Revision Request (NPRR) removes ORDC Phase 2; changes the High Ancillary Service Limit (HASL) calculation to remove Non-Frequency Responsive Capacity (NFRC) included in a Generation Resource’s High Sustained Limit (HSL), thereby creating the opportunity for an ORDC payment for the NFRC capacity through Ancillary Service imbalance Settlement; and clarifies the HASL definition between use in the Resource limit calculator, Reliability Unit Commitment (RUC) optimization, and the capacity shortfall ratio share.”
[NPRR568: Replace the above equation RTRDASIAMT q with the following upon Phase 2 system implementation:] RTRDASIAMT q= (-1) * ((RTASOLIMB q - RTOFF10 q )* RTRDP)
[NPRR568 and NPRR698: Replace applicable portions of the above equation RTOLCAP q with the following upon system implementation (upon or following the implementation of NPRR568):] RTOLCAP q = (RTOLHSL q –RTMGQ q – SYS_GEN_DISCFACTOR * ( UGENA q, r, p)) + RTCLRCAP q + RTOFF10 q RTOFF10 q = SYS_GEN_DISCFACTOR * RTOFF10R q, r, p
[NPRR568: Replace the above equation RTOFFCAP q with the following upon Phase 2 system implementation:] RTOFFCAP q = RTOFF30 q + RTOFFNSHSL q + RTCLRNS q RTOFF30 q = SYS_GEN_DISCFACTOR * RTOFF30R q, r, p RTOFFNSHSL q = SYS_GEN_DISCFACTOR * RTOFFNSHSLR q, r, p

## Slide 6: R5.5 - NPRR 698- Clarifications to NPRR595, RRS Load Resource Treatment In ORDC
“This Nodal Protocol Revision Request (NPRR) clarifies ERCOT’s intended implementation of NPRR595, RRS Load Resource Treatment In ORDC, and allows the use of currently telemetered values to provide the intent of NPRR595 at a lower project cost.”
RTOLCAP q = (RTOLHSL q – RTMGQ q – SYS_GEN_DISCFACTOR * ( UGENA q, r, p)) + RTCLRCAP q + RTNCLRCAP q + RTNCLRRRSq
RTNCLRRRS q = SYS_GEN_DISCFACTOR * RTNCLRRRSR q, r, p
RTNCLRCAP q = RTNCLRNPC q – RTNCLRLPC q
RTNCLRNPC q = SYS_GEN_DISCFACTOR * RTNCLRNPCR q, r, p
RTNCLRLPC q = SYS_GEN_DISCFACTOR * RTNCLRLPCR q, r, p
RTCLRCAP q= RTCLRNPCF q – RTCLRLPCSL q – RTCLRNS q + RTCLRREG q
Where:
RTCLRNPCF q= SYS_GEN_DISCFACTOR * RTCLRNPCFR q, r, p
RTCLRLPCSL q = SYS_GEN_DISCFACTOR * RTCLRLPCSLR q, r, p

## Slide 7: R5.5 – NPRR 615- PVGR Forecasting
5.7.4.1.1 Capacity Shortfall Ratio Share
In calculating the amount short for each QSE, the QSE must be given a capacity credit for its WGR IRRs based on the HSL values entered into the COP by the QSE just prior to the RUC execution. For IRRs, ERCOT shall use for Settlement purposes the COP and Trades Snapshot prior to the RUC regardless of Real-Time capacity or actual generation. Therefore, the HASLSNAP and HASLADJ variables used below shall be equal to the HSL values entered into the QSE’s COP submitted prior to the RUC for WGR IRRs.
(2) In calculating the amount short for each QSE, the QSE must be given a capacity credit for non- wind resources IRRs that were given notice of decommitment within the two hours before the Operating Hour as a result of the RUC process by setting the HASLSNAP and HASLADJ variables used below equal to the HASLSNAP value for the Resource immediately before the decommitment instruction was given.
(10) The RUC Shortfall in MW for one QSE for one 15-minute Settlement Interval, as measured at Real-Time, but including capacity from WGRs IRRs as seen in the RUC snapshot, is:
RUCSFADJ ruc,q,i = Max (0, (( RTAMLq,p,i) *4) + RTDCEXP q, p, i – ( HASLSNAP ruc, q, r, h + RUCCAPADJq,i))
11) The amount of capacity that a QSE had in Real-Time for a 15-minute Settlement Interval, excluding capacity from WGRs IRRs, is:
RUCCAPADJq,i = HASLADJq,r,h + (RUCCPADJq,h – RUCCSADJq,h) + ( DAEPq,p,h – DAESq,p,h) + ( RTQQEPADJq,p,i – RTQQESADJq,p,i) + DCIMPADJ q, p, i

## Slide 8: R5.5 – NPRR 588- Clarifications for PV Generation Resources
4.4.9.2.3 Startup Offer and Minimum-Energy Offer Generic Caps
Resource Category | O&M Costs ($)
Nuclear, coal, lignite and hydro | 7,200
Combined Cycle Generation Resource with a combustion turbine ≥ 90 MW, as determined by the largest combustion turbine in the Combined Cycle Generation Resource and for each combustion turbine in the Combined Cycle Generation Resource | 6,810
Combined Cycle Generation Resource with a combustion turbine < 90 MW, as determined by the largest combustion turbine in the Combined Cycle Generation Resource and for each combustion turbine in the Combined Cycle Generation Resource | 6,810
Gas steam supercritical boiler | 4,800
Gas steam reheat boiler | 3,000
Gas steam non-reheat or boiler w/o air-preheater | 2,310
Simple cycle greater than 90 MW | 5,000
Simple cycle less than or equal to 90 MW | 2,300
Reciprocating Engines | $58 /MW * the average of the seasonal net max sustainable ratings
RMR Resource | Not Applicable
Wind generation Resources | 0
PhotoVoltaic Generation Resources (PVGRs) | 0
Any Resources not defined above | 0
(1) The Resource Category Startup Offer Generic Cap, by applicable Resource category, is determined by the following Operations and Maintenance (O&M) costs by Resource category:

## Slide 9: R5.5 – NPRR 588- Clarifications for PV Generation Resources
4.4.9.2.3 Startup Offer and Minimum-Energy Offer Generic Caps
(2) The Resource Category Minimum-Energy Generic Cap is the cost per MWh of energy for a Resource to produce energy at the Resource’s LSL and is as follows:
(n) PVGRs = $0; and
4.4.9.4.2 Mitigated Offer Floor
Energy Offer Curves may be subject to mitigation in the Real-Time market under Section 6.5.7.3, Security Constrained Economic Dispatch, using a Mitigated Offer Floor. The “Mitigated Offer Floor” is:
Resource Category | Mitigated Offer Floor
Nuclear and Hydro | -$250/MWh
Coal and Lignite | -$20/MWh
Combined Cycle | 1 MMBtu/MWh * FIP
Gas/Oil Steam and Combustion Turbine | 6 MMBtu/MWh * FIP or FOP, as specified in the Energy Offer Curve
Qualifying Facility (QF) | -$ 50/MWh
Wind | -$100/MWh
PhotoVoltaic (PV) | -$50/MWh
Other Renewables | -$ 50/MWh

## Slide 10: R5.5 – NPRR 588- Clarifications for PV Generation Resources
7.9.1.3 Minimum and Maximum Resource Prices
(2) Minimum Resource Prices of source Settlement Points are:
MINRESPR j = Min ( MINRESRPR j, r ) r
Where:
Minimum Resource Prices for Resources located at source Settlement Points (MINRESRPR j, r) are:
PhotoVoltaic (PV) = -$10;
(3) Maximum Resource Prices of sink Settlement Points are:
MAXRESPR k = Max (MAXRESRPR k, r ) r
Maximum Resource Prices for Resources located at sink Settlement Points (MAXRESRPR k, r ) are:
(m) PV = $0/MWh;