## Slide 1
Real-Time Co-optimization of Energy & Ancillary Services
Examples of Load Resource Settlement Options

## Slide 2: RT Energy + Ancillary Service Co-Optimization
Homework: Provide example of Settlement for Load Resource buy back exemption impact
  Language per ERCOT Concept Paper for Real-Time Market Improvements:
  Co-optimization of Energy and Ancillary Services & Multi-Interval Real-Time Market
  2.4 Telemetry Changes for LR with UFR (blocky AS)
    Upon deployment will be exempt from AS imbalance charge
  2. In RT, LR with UFR carrying RRS responsibility will be considered to be price takers (i.e. RRS offer from these LR = 0$/MW). i.e no reduction of RRS demand curve by the amount of RRS responsibility from Load Resources.
  3. However, when deployed, LR will be considered to be still providing RRS till the 3 hour limit after recall.
Notes: Slide #5

## Slide 3: RT Energy + Ancillary Service Co-Optimization
GTBD after Load Drop
GTBD before Load Drop
Reserves before Load Drop
Reserves after Load Drop
t
t + 3 hours
MW
Load Resource deployment due to Frequency event
with a 3 hour return to service
Notes: Slide #5

## Slide 4: RT Energy + Ancillary Service Co-Optimization
Provide example of Settlement of Load Resource buy back exemption impact
  Settlement of current ORDC with buy back
  Resource has full DAM Hedge and is deployed in RT:
Non-Controllable Load Resource - Current ORDC with Buy Back |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Time | DAM Purchase Award (MW) | DAM AS Award (MW) | DAM SPP ($/MWh) | DAM MCPC ($/MWh) | DAM Energy Amount ($) | DAM AS Payment ($) | DAM Total ($) | RTSPP ($/MWh) | Price Adder P_S ($/MWh) | RTSPP New ($/MWh) | RTAML (MWh) | LZ Energy Imbalance (MWh) | RT Energy Imbalance Pmnt/Chrg ($) | RT Online Reserve Imbalance (MWh) | RT Online Reserve Imbalance Pmnt/Chrg ($) | RT Total Imbalance Payment (Energy + AS + RUC Awd) ($) | Daily Net Payment or Charge to Resource (DAM + RT)
HE16 :00 | 20 | 20 | $ 582 | $ 572 | $11,643.00 | $(11,447.80) | $ 195.20 | $ 738 | $ 351 | $ 1,089 | 0 | 20 | $ (21,784.40) | -20 | $ 7,015.00 | $(14,769.40) | $ (14,574.20)
HE16 :15 | 20 | 20 | $ 582 | $ 572 | $11,643.00 | $(11,447.80) | $ 195.20 | $ 180 | $ 419 | $ 599 | 0 | 20 | $ (11,971.40) | -20 | $ 8,371.60 | $ (3,599.80) | $ (3,404.60)
HE16 :30 | 20 | 20 | $ 582 | $ 572 | $11,643.00 | $(11,447.80) | $ 195.20 | $ 98 | $ 292 | $ 390 | 0 | 20 | $ (7,799.40) | -20 | $ 5,831.80 | $ (1,967.60) | $ (1,772.40)
HE16 :45 | 20 | 20 | $ 582 | $ 572 | $11,643.00 | $(11,447.80) | $ 195.20 | $ 615 | $ 441 | $ 1,057 | 0 | 20 | $ (21,131.80) | -20 | $ 8,829.80 | $(12,302.00) | $ (12,106.80)
HE17 :00 | 20 | 20 | $ 151 | $ 142 | $ 3,029.80 | $ (2,838.00) | $ 191.80 | $ 173 | $ 462 | $ 635 | 0 | 20 | $ (12,708.00) | -20 | $ 9,249.20 | $ (3,458.80) | $ (3,267.00)
HE17 :15 | 20 | 20 | $ 151 | $ 142 | $ 3,029.80 | $ (2,838.00) | $ 191.80 | $ 346 | $ 508 | $ 853 | 0 | 20 | $ (17,066.80) | -20 | $ 10,151.60 | $ (6,915.20) | $ (6,723.40)
HE17 :30 | 20 | 20 | $ 151 | $ 142 | $ 3,029.80 | $ (2,838.00) | $ 191.80 | $ 180 | $ 445 | $ 625 | 0 | 20 | $ (12,501.60) | -20 | $ 8,895.20 | $ (3,606.40) | $ (3,414.60)
HE17 :45 | 20 | 20 | $ 151 | $ 142 | $ 3,029.80 | $ (2,838.00) | $ 191.80 | $ 147 | $ 411 | $ 558 | 0 | 20 | $ (11,150.00) | -20 | $ 8,216.40 | $ (2,933.60) | $ (2,741.80)
HE18 :00 | 20 | 20 | $ 68 | $ 58 | $ 1,352.60 | $ (1,156.40) | $ 196.20 | $ 101 | $ 252 | $ 353 | 0 | 20 | $ (7,067.80) | -20 | $ 5,042.00 | $ (2,025.80) | $ (1,829.60)
HE18 :15 | 20 | 20 | $ 68 | $ 58 | $ 1,352.60 | $ (1,156.40) | $ 196.20 | $ 76 | $ 172 | $ 248 | 0 | 20 | $ (4,962.60) | -20 | $ 3,439.80 | $ (1,522.80) | $ (1,326.60)
HE18 :30 | 20 | 20 | $ 68 | $ 58 | $ 1,352.60 | $ (1,156.40) | $ 196.20 | $ 60 | $ 49 | $ 109 | 0 | 20 | $ (2,172.40) | -20 | $ 980.40 | $ (1,192.00) | $ (995.80)
HE18 :45 | 20 | 20 | $ 68 | $ 58 | $ 1,352.60 | $ (1,156.40) | $ 196.20 | $ 54 | $ 17 | $ 71 | 0 | 20 | $ (1,425.40) | -20 | $ 344.40 | $ (1,081.00) | $ (884.80)
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | $ (53,041.60)
Notes: Slide #5

## Slide 5: RT Energy + Ancillary Service Co-Optimization
RT Co-Optimization Proposed - EXEMPT from AS Imbalance |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Note: The current RT Online Price adder is used as a proxy for the RT AS MCPC |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Time | DAM Purchase Award (MW) | DAM AS Award (MW) | DAM SPP ($/MWh) | DAM MCPC ($/MWh) | DAM Energy Amount ($) | DAM AS Payment ($) | DAM Total ($) | RTSPP ($/MWh) | RT MCPC | RTAML (MWh) | LZ Energy Imbalance (MWh) | RT Energy Imbalance Pmnt/Chrg ($) | RTM AS Award (MW) | AS Imbalance DA Award - RT Award | RT Online AS Imbalance Pmnt/Chrg ($) | Daily Net Payment or Charge to Resource (DAM + RT)
HE16 :00 | 20 | 20 | $ 582 | $ 572 | $11,643.00 | $(11,447.80) | $ 195.20 | $ 1,089 | $ 351 | 0 | 20 | $(21,784.40) | 20 | 0 | - | $ (21,589.20)
HE16 :15 | 20 | 20 | $ 582 | $ 572 | $11,643.00 | $(11,447.80) | $ 195.20 | $ 599 | $ 419 | 0 | 20 | $(11,971.40) | 20 | 0 | - | $ (11,776.20)
HE16 :30 | 20 | 20 | $ 582 | $ 572 | $11,643.00 | $(11,447.80) | $ 195.20 | $ 390 | $ 292 | 0 | 20 | $ (7,799.40) | 20 | 0 | - | $ (7,604.20)
HE16 :45 | 20 | 20 | $ 582 | $ 572 | $11,643.00 | $(11,447.80) | $ 195.20 | $ 1,057 | $ 441 | 0 | 20 | $(21,131.80) | 20 | 0 | - | $ (20,936.60)
HE17 :00 | 20 | 20 | $ 151 | $ 142 | $ 3,029.80 | $ (2,838.00) | $ 191.80 | $ 635 | $ 462 | 0 | 20 | $(12,708.00) | 20 | 0 | - | $ (12,516.20)
HE17 :15 | 20 | 20 | $ 151 | $ 142 | $ 3,029.80 | $ (2,838.00) | $ 191.80 | $ 853 | $ 508 | 0 | 20 | $(17,066.80) | 20 | 0 | - | $ (16,875.00)
HE17 :30 | 20 | 20 | $ 151 | $ 142 | $ 3,029.80 | $ (2,838.00) | $ 191.80 | $ 625 | $ 445 | 0 | 20 | $(12,501.60) | 20 | 0 | - | $ (12,309.80)
HE17 :45 | 20 | 20 | $ 151 | $ 142 | $ 3,029.80 | $ (2,838.00) | $ 191.80 | $ 558 | $ 411 | 0 | 20 | $(11,150.00) | 20 | 0 | - | $ (10,958.20)
HE18 :00 | 20 | 20 | $ 68 | $ 58 | $ 1,352.60 | $ (1,156.40) | $ 196.20 | $ 353 | $ 252 | 0 | 20 | $ (7,067.80) | 20 | 0 | - | $ (6,871.60)
HE18 :15 | 20 | 20 | $ 68 | $ 58 | $ 1,352.60 | $ (1,156.40) | $ 196.20 | $ 248 | $ 172 | 0 | 20 | $ (4,962.60) | 20 | 0 | - | $ (4,766.40)
HE18 :30 | 20 | 20 | $ 68 | $ 58 | $ 1,352.60 | $ (1,156.40) | $ 196.20 | $ 109 | $ 49 | 0 | 20 | $ (2,172.40) | 20 | 0 | - | $ (1,976.20)
HE18 :45 | 20 | 20 | $ 68 | $ 58 | $ 1,352.60 | $ (1,156.40) | $ 196.20 | $ 71 | $ 17 | 0 | 20 | $ (1,425.40) | 20 | 0 | - | $ (1,229.20)
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | $ (129,408.80)
RT Co-Optimization Proposed - If NOT EXEMPT from AS Imbalance |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Note: The current RT Online Price adder is used as a proxy for the RT AS MCPC |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Time | DAM Purchase Award (MW) | DAM AS Award (MW) | DAM SPP ($/MWh) | DAM MCPC ($/MWh) | DAM Energy Amount ($) | DAM AS Payment ($) | DAM Total ($) | RTSPP ($/MWh) | RT MCPC | RTAML (MWh) | LZ Energy Imbalance (MWh) | RT Energy Imbalance Pmnt/Chrg ($) | RTM AS Award (MW) | AS Imbalance DA Award - RT Award | RT Online AS Imbalance Pmnt/Chrg ($) | Daily Net Payment or Charge to Resource (DAM + RT)
HE16 :00 | 20 | 20 | $ 582 | $ 572 | $11,643.00 | $(11,447.80) | $ 195.20 | $ 1,089 | $ 351 | 0 | 20 | $(21,784.40) | 0 | 20 | 7,015 | $ (14,574.20)
HE16 :15 | 20 | 20 | $ 582 | $ 572 | $11,643.00 | $(11,447.80) | $ 195.20 | $ 599 | $ 419 | 0 | 20 | $(11,971.40) | 0 | 20 | 8,372 | $ (3,404.60)
HE16 :30 | 20 | 20 | $ 582 | $ 572 | $11,643.00 | $(11,447.80) | $ 195.20 | $ 390 | $ 292 | 0 | 20 | $ (7,799.40) | 0 | 20 | 5,832 | $ (1,772.40)
HE16 :45 | 20 | 20 | $ 582 | $ 572 | $11,643.00 | $(11,447.80) | $ 195.20 | $ 1,057 | $ 441 | 0 | 20 | $(21,131.80) | 0 | 20 | 8,830 | $ (12,106.80)
HE17 :00 | 20 | 20 | $ 151 | $ 142 | $ 3,029.80 | $ (2,838.00) | $ 191.80 | $ 635 | $ 462 | 0 | 20 | $(12,708.00) | 0 | 20 | 9,249 | $ (3,267.00)
HE17 :15 | 20 | 20 | $ 151 | $ 142 | $ 3,029.80 | $ (2,838.00) | $ 191.80 | $ 853 | $ 508 | 0 | 20 | $(17,066.80) | 0 | 20 | 10,152 | $ (6,723.40)
HE17 :30 | 20 | 20 | $ 151 | $ 142 | $ 3,029.80 | $ (2,838.00) | $ 191.80 | $ 625 | $ 445 | 0 | 20 | $(12,501.60) | 0 | 20 | 8,895 | $ (3,414.60)
HE17 :45 | 20 | 20 | $ 151 | $ 142 | $ 3,029.80 | $ (2,838.00) | $ 191.80 | $ 558 | $ 411 | 0 | 20 | $(11,150.00) | 0 | 20 | 8,216 | $ (2,741.80)
HE18 :00 | 20 | 20 | $ 68 | $ 58 | $ 1,352.60 | $ (1,156.40) | $ 196.20 | $ 353 | $ 252 | 0 | 20 | $ (7,067.80) | 0 | 20 | 5,042 | $ (1,829.60)
HE18 :15 | 20 | 20 | $ 68 | $ 58 | $ 1,352.60 | $ (1,156.40) | $ 196.20 | $ 248 | $ 172 | 0 | 20 | $ (4,962.60) | 0 | 20 | 3,440 | $ (1,326.60)
HE18 :30 | 20 | 20 | $ 68 | $ 58 | $ 1,352.60 | $ (1,156.40) | $ 196.20 | $ 109 | $ 49 | 0 | 20 | $ (2,172.40) | 0 | 20 | 980 | $ (995.80)
HE18 :45 | 20 | 20 | $ 68 | $ 58 | $ 1,352.60 | $ (1,156.40) | $ 196.20 | $ 71 | $ 17 | 0 | 20 | $ (1,425.40) | 0 | 20 | 344 | $ (884.80)
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | $ (53,041.60)
Notes: Slide #5