## Slide 1: Price Responsive Load / Retail DR RMS Update
Paul Wattles
Carl Raish
October 6, 2015

## Slide 2: RMS topics
2014 analysis - status report
2015 snapshot date review
Next steps

## Slide 3: PUC Rule
Pursuant to PUC Subst. Rule §25.505(e) (5), “Load Serving Entities (LSEs) shall provide ERCOT with complete information on load response capabilities that are self-arranged or pursuant to bilateral agreements between LSEs and their customers”

## Slide 4: Pricing Events – 2014
  ERCOT identified 9 days in calendar year 2014 with pricing events
    price for 4 or more consecutive intervals exceeded $200 in all four competitive load zones.
  One of the days, January 6, was an EEA day when prices were at the cap until various forms of demand response kicked in
  Three of the days were on a Sunday: March 2 and 16, September 21
  Graphs on the following slides compare actual prices on those nine days to the average price for that day-type and month

## Slide 5: Pricing Events – 2014
Jan 6 – EEA event
Feb 10
Mar 2 - Sunday
Mar 3

## Slide 6: Pricing Events – 2014
Mar 16 - Sunday
Apr 7
May 30
Sep 21 - Sunday

## Slide 7: Pricing Events – 2014 (continued)
Nov 13

## Slide 8
4-CP

## Slide 9: Number of ESIIDs with 4 CP Responses – 2014

## Slide 10: Hour-ending 17:00 MW Reductions on 4 CP Days - 2014
MW Load Reduction for Responding 4-CP ESIIDS

## Slide 11: Hour-ending 17:00 Reductions on 4 CP Days - 2014

## Slide 12: 4 CP 15-Minute Response 2009 - 2014

## Slide 13: 4-CP Interval Reductions on 4 CP Days - 2014
Percentage of Load Reduction based on Customer Peak

## Slide 14
Other Load Control

## Slide 15: 2014 OLC Analysis
May Composite Day
Early Oct Composite Day
Mid October Composite Day
5 Reps reported OLC programs in 2014
~19,200 Res and 64 Bus customers
3 Reps reported 7 deployments in 2014 affecting 3,200 Res and 5 Bus customers
4 events (3 in Aug, 1 in Oct) showed no evidence of any load reduction
May and October days combined into composite graphs to approximate the total OLC load reduction that could occur with same-day deployment

## Slide 16
Peak Rebate

## Slide 17: 2014 PR Analysis
August Composite Day
September Composite Day
6 Reps reported PR programs in 2014
~ 410,700 Res and 30,200 Bus customers
  With DLC: Res 4,400 Bus 4
4 Reps reported 9 deployments in 2014 affecting 32,100 Res and 143 Bus customers
  With DLC: Res 4,400 Bus 4
3 events (1 in Sep, 2 in Oct) showed no evidence of any load reduction
6 events showed obvious reductions ranging from 27 – 40 MW
August and September days are combined into composite graphs to approximate the total PR load reduction that could occur with same-day deployment

## Slide 18
Real Time Pricing

## Slide 19: 2014 RTP Analysis
11 Reps reported RTP programs in 2014
~ 1,000 Res and 9,700 Bus customers
  None with DLC
2 pricing events days (Jan 6 and Mar 3) with evidence of load reduction
  Jan 6: ~4,500 customers ~12.9 MW of load reduction (~8.8 MW from BUSIDRRQ)
  Mar 3 ~5,000 customers ~7.4 MW load reduction (~4.4 MW from BUSIDRRQ)
Note: EEA related Load reduction led to price drop, and RTP related load reduction mostly occurred following the price drop
Jan 6, 2014 – EEA Day
Mar 3, 2014

## Slide 20
Block and Index

## Slide 21: 2014 BI Analysis
16 Reps reported BI programs in 2014
~ 6,800 Bus customers
  None with DLC
2 pricing events days (Jan 6 and Mar 3) with evidence of load reduction
  Jan 6: ~5,400 customers ~507.9 MW of load reduction (~330.4 MW from BUSIDRRQ)
  Mar 3 ~5,700 customers ~229.3 MW load reduction (~43.6 MW from BUSIDRRQ)
Note: EEA related Load reduction led to price drop, and BI related load reduction during high price intervals did occur prior to the price drop
  Jan 6: 455 MW in interval 30 when price was $2,800
  Mar 3: 179 MW in interval 28 when price was $4,990
Jan 6, 2014 – EEA Day
Mar 3, 2014

## Slide 22: Combined Price Response - 2014
Category | Response (MW)
4-CP | 710
Other Load Control | 5
Peak Rebate | 40
Real Time Pricing | 5
Block and Index | 180
Critical Peak Pricing | 0
Time Of Use | Analysis in Progress
Total | 940
Response reported for ERCOT competitive areas only
Customers responding to 4-CP and participating in RTP or BI were excluded from RTP and BI totals.
  4-CP customers on RTP reduced load by 9 MW during January pricing event
  4-CP customers on BI reduced load by 330 MW during January pricing event

## Slide 23: Updated Categories pg. 1 of 3
Demand Response category (improved) definitions:
RTP – Real Time Pricing - retail prices for all hours or intervals based on ERCOT Real-Time Settlement Point Prices for the premise Load Zone, calculated every 15 minutes, or other real-time wholesale price indicator(s).
BI – Block & Index – fixed pricing for a defined volume of usage, coupled with pricing indexed to the wholesale market for usage exceeding the block. Block prices and volumes may vary by time of day/week. (removed last line from definition - Option could include if usage dips below the block.)
PR – Peak Rebates – a retail offering in which the customer is eligible for a financial incentive paid for load reductions taken during periods of time identified by the LSE, and communicated to the customer during the prior day or the event day, or both. LSE has defined a method to identify whether a customer has responded and to quantify the response amount. Payment (rebate) to customer is based upon customer’s response.
Peak Rebate examples -
No DLC: The REP sends an email one day prior if high prices are forecasted, and sends a reminder text/tweet the morning of the following day. The REP identifies responding customers using a recent similar weather day as a baseline to estimate what the customer’s load would have been. If the customer’s actual load during the predicted intervals was lower than the baseline, the REP agrees to pay the customer $100 / kw of reduction.
DLC: REP sends email one day prior if high prices are forecasted, and sends a reminder text/tweet the morning of the following day. When high prices materialize, the REP sends a signal to the customer’s web-enabled thermostat to increase its set point by 3 degrees. The REP establishes a baseline for the customer to estimate what the customer’s load would have been. If the customer’s actual load during the predicted intervals was lower than the baseline, the REP agrees to pay the customer $100 / kw of reduction.

## Slide 24: Updated Categories pg. 2 of 3
Demand Response category definitions:
CPP – Critical Peak Pricing – prices that rise during critical peaks: limited duration periods of time identified by the LSE that usually correlate to high prices in the real-time wholesale market. Critical peak events may occur a limited number of times per year and typically are communicated a day in advance.
TOU – Time of Use — prices that vary across defined blocks of hours, with predefined prices and schedules. (As used here, does not apply to seasonal adjustments).
TOU Example – free evening hours
OLC – Other Direct Load Control – contracts that allow the LSE or a third party to control the customer’s load remotely for economic or grid reliability purposes. This category applies to Direct Load Control (DLC) with different deployment criteria than described elsewhere. (Avoid double counting if DLC data was reported in other categories.). Customer incentive is predefined and does not vary based upon the response.
OLC Example -
OLC (always has DLC) REP identifies a day on which high prices have, or are about to, materialize. The REP sends a signal to the customer’s web-enabled thermostat to increase its set point by 3 degrees. The REP agrees to pay the customer $10 / month for each summer month, and the customer agrees to allow the thermostat to be set higher 10 times during the summer for periods up to 2 hours long. If the customer overrides the REP thermostat setting during a month, the customer’s payment is reduced by $3.
OTH – Other Voluntary Demand Response Product – any retail product not covered in the other categories that includes a demand response incentive or signal.

## Slide 25: Updated Categories pg. 3 of 3
Demand Response category definitions:
NOTE – will not use 4CP and FO categories for summer 2015 data collection
4CP – Four Coincident Peak – predictor signals or direct load control provided to customers in advance of potential Four Coincident Peak (4CP) intervals during summer months (June through September). Reducing load during such intervals lowers transmission charges. 4CP charges apply to large customers (peak demand ≥700 kW) in competitive choice areas, and also to NOIEs at the boundary meter level.
FO – Financial Option – product where LSE purchases an option from the customer that is backed by a specified level of DR and uses it for portfolio trades in the wholesale market.
4CP - ERCOT can do the 4CP analysis without the need to ask the LSEs to provide data in the survey.
FO – category has not been used for 2 years

## Slide 26: Snapshot for Summer 2015
2015 Summer data collection timeline
September 30, 2015 - snapshot by REPs for which ESI IDs are in programs
November 4, 2015 - file submission to ERCOT*
November 18, 2015 - error correction file submission to ERCOT
  * pushed file submission back by 2 weeks to allow any error handling to be completed prior to Thanksgiving Holiday
  REP should make all necessary corrections and re-send the full file to ERCOT. ERCOT will use the last file sent for data analysis.
  ERCOT will send survey monkey after receipt of ‘clean data’ or declaring ‘uncle’
December 1, 2015 – ERCOT will send Survey Monkey links to REPs to gather REP-specific event information
December 11, 2015 – Survey Monkey responses due

## Slide 27: Next Steps – for future
Still for future discussion
Future years (starting 2016?)
  Evaluate quarterly submissions for 2016
  Ask REPs to evaluate winter programs for future consideration
    Please review categories to see if definitions fit or if new categories would need to be added
    Consider possible dates and/or frequency of a winter file submission
Protocol Revision and/or Market Guide Revision?
Review categories each year to see if adjustments need to be made
Review reporting of events via Survey Monkey to see if there is a better method to leverage

## Slide 28: Take Aways
REPs
  Prepare to take the snapshot for Sept 30th
  Log self-initiated events in preparation for the survey
  Map product types to the categories in the guide
  If unsure which category to use – please ask
    Carl Raish (carl.raish@ercot.com)
    Paul Wattles (paul.wattles@ercot.com)
    Karen Farley (karen.farley@ercot.com)
ERCOT
  ERCOT will continue work on TOU analysis for future report to market.

## Slide 29: Questions?
ON
OFF