## Slide 1
Ancillary Services Methodology Changes for 2016
Bill Blevins
Manager Operations Planning
TAC
29-OCTOBER-2015

## Slide 2: Items for discussion
  Schedule
  Proposed changes to Regulation Service
  Proposed changes to Non-Spin Reserve Service (NSRS)
  Postings of AS Requirements

## Slide 3: Schedule for discussion with Stakeholders
4-Sept | QMWG | Presented
17-Sept | OWG | Presented
7-Oct | WMS | Endorsed
8-Oct | ROS | Endorsed
29-Oct | TAC | 
08-Dec | BOD | 
Notes: 3.16 Standards for Determining Ancillary Service Quantities
The ERCOT Board shall review and approve ERCOT's methodology for determining the minimum Ancillary Service requirements, the monthly percentage of Load Resources, Controllable Load Resources and DC Ties allowed to provide RRS, and the maximum amount of Reg-Up and Reg-Down that can be provided by Resources providing FRRS-Up and FRRS-Down.
Last done by BOD Dec 2014.

## Slide 4: Regulation Performance-CPS1 Score
ERCOT has to maintain rolling 12 months average CPS1 Score above 100% Per NERC standard BAL-001-1

## Slide 5: Drivers for changes to Regulation Requirements
CPS1 is significantly higher than required and on an increasing trend.
By using last 30 days, transition months tend to drive requirements for the following month. (e.g. April is used to set quantity for June)
Extreme events tend to drive over-procurement for a particular hour in subsequent months, even though the event is unlikely to repeat.
Significant changes in regulation requirements from one hour to the next, which may not be necessary.

## Slide 6: Possible Changes to Regulation Service
  Remove consideration of the last 30 days from Regulation Analysis and instead use the Regulation data using same month of the previous two years. (e.g. April 2014 and April 2015 to calculate April 2016 requirements)
  Use five minute average instead of one minute average regulation deployment for exhaustion rate.
  Use 95th percentile of 5 minute net-load/deployments instead of 98.8th percentile.
  Update the GE Tables
  Increase CPS1 trigger to 140% instead of 100%
Notes: Item E. is a metric so that using the 95th percentile will not decrease regulation if CPS1 scores significantly . This adjustment will be applied to the month that scored below 140% unless the rolling average goes below 140% and then it will be applied to the next month until the rolling 12 month CPS1 average increases above 140%.

## Slide 7: Proposed Regulation-Up Requirement
Chart: Regulation-Up Daily Total (MW)
| 42005 | 42036 | 42064 | 42095 | 42125 | 42156 | 42186 | 42217 | 41883 | 41913 | 41944 | 41974
Current | 9983 | 10197 | 10783 | 10796 | 10696 | 11583 | 11346 | 10481 | 11336 | 10714 | 10751 | 9430
Proposed | 7476 | 7565 | 8194 | 8408 | 8283 | 8338 | 8166 | 8291 | 8903 | 7632 | 6921 | 7546

## Slide 8: Proposed Regulation-Down Requirement
Chart: Regulation-Down Daily Total (MW)
| 42005 | 42036 | 42064 | 42095 | 42125 | 42156 | 42186 | 42217 | 41883 | 41913 | 41944 | 41974
Current | 9089 | 8891 | 9429 | 9515 | 9805 | 10988 | 10809 | 10118 | 10160 | 10524 | 10083 | 8664
Proposed | 6841 | 6790 | 6925 | 7293 | 7877 | 8078 | 7483 | 7705 | 7961 | 7144 | 6271 | 7447

## Slide 9: Drivers for NSRS Changes
Feedback we received last year to revisit NSRS Methodology
Incorporate effects of net load ramps

## Slide 10: Suggested Changes to Non-Spin Service
  Remove last 30 days from NSRS Analysis and instead use the same month for previous three years
  Use the 3-hour ahead net forecast error instead of 6-hour ahead
  Use net forecast error only on the under-forecast
  Use dynamic percentile between 70th and 95th percentile based on the risk of net load ramp

## Slide 11: Possible Changes to Non-Spin Reserve Service(NSRS)
 | Current Methodology | Proposed Methodology
Data Used |  | 
Forecast | 6hour-ahead Net Load Error | 3hour-ahead Net Load Error
Over & Under Forecast | Both | Under Forecast
Percentile | 95th | Dynamically determined based on risk of net load ramp
Cap | 2000MW | No Cap
Floor | 1375 MW (Peak Hours) | 1375 MW (Peak Hours)
Target Period
Same Period
Previous Year
15 days
Not considered
30days prior to study
30
30
15
30
Target Period
Same Period
Previous 3 Years
30
30
30
30

## Slide 12: Proposed NSRS Requirement
Chart: NSRS Daily Total (MW)
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov(*) | Dec(*)
Current | 44224 | 47780 | 48000 | 48000 | 43496 | 46004 | 43880 | 45528 | 37076 | 42424 | 47608 | 47420
Proposed | 32124.9133 | 37125.6569 | 36288.1924 | 35693.7855 | 33950.1033 | 37406.0934 | 34259.2382 | 32771.4028 | 34225.7024 | 35671.2854 | 34403.1974 | 38098.9612

## Slide 13: Comparison NSRS Procurement change
Current Methodology
Proposed Methodology
Notes: Font sizes should be increased if possible

## Slide 14: Posting of AS Requirements
  Responsive Reserve is already posted in December for the next year.
  Regulation for each month can be posted for the next year in December.
  NSRS for each month can be posted for the next year in December.
Notes: Font sizes should be increased if possible

## Slide 15
Discussion

## Slide 16
Appendix

## Slide 17: Reg-Up Requirement for Jan. 2015
A: Use data from the same month of last 2 years
B: 5-min exhaustion rate
C: 95th percentile
Chart: Jan. 2015 Reg-Up Requirement (MW)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Current | 363 | 294 | 283 | 299 | 420 | 597 | 830 | 475 | 413 | 408 | 400 | 416 | 370 | 420 | 295 | 306 | 400 | 593 | 464 | 273 | 313 | 361 | 515 | 475
A | 425 | 262 | 282 | 349 | 407 | 585 | 817 | 564 | 444 | 452 | 501 | 432 | 324 | 634 | 250 | 296 | 345 | 643 | 562 | 313 | 341 | 342 | 436 | 395
A+B | 355 | 262 | 282 | 291 | 407 | 585 | 817 | 470 | 404 | 452 | 501 | 432 | 324 | 634 | 250 | 269 | 345 | 643 | 562 | 313 | 310 | 342 | 436 | 395
A+B+C | 262 | 258 | 252 | 326 | 423 | 478 | 647 | 342 | 308 | 282 | 312 | 295 | 279 | 253 | 200 | 207 | 221 | 319 | 475 | 239 | 199 | 305 | 314 | 369

## Slide 18: Reg-Up Requirement for Apr. 2015
Chart: April 2015 Reg-up Requirement (MW)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Current | 453 | 458 | 327 | 327 | 412 | 558 | 803 | 397 | 494 | 395 | 414 | 387 | 443 | 395 | 365 | 338 | 356 | 378 | 536 | 445 | 529 | 454 | 557 | 575
A | 546 | 451 | 359 | 349 | 400 | 525 | 746 | 404 | 501 | 430 | 508 | 481 | 452 | 437 | 428 | 395 | 351 | 427 | 471 | 445 | 465 | 428 | 530 | 606
A+B | 546 | 376 | 326 | 349 | 400 | 525 | 746 | 404 | 501 | 430 | 508 | 481 | 452 | 437 | 389 | 359 | 351 | 388 | 392 | 445 | 465 | 428 | 530 | 606
A+B+C | 409 | 266 | 218 | 253 | 297 | 446 | 618 | 304 | 402 | 338 | 380 | 413 | 356 | 374 | 301 | 288 | 289 | 286 | 263 | 335 | 382 | 310 | 387 | 493
A: Use data from the same month of last 2 years
B: 5-min exhaustion rate
C: 95th percentile

## Slide 19: Reg-Up Requirement for June 2015
Chart: June 2015 Reg-up Requirement (MW)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Current | 659 | 428 | 410 | 352 | 494 | 525 | 738 | 459 | 510 | 481 | 681 | 509 | 422 | 397 | 392 | 379 | 311 | 454 | 356 | 472 | 448 | 536 | 559 | 611
A | 633 | 477 | 362 | 307 | 318 | 486 | 622 | 455 | 465 | 557 | 604 | 507 | 493 | 463 | 415 | 404 | 332 | 366 | 380 | 438 | 404 | 490 | 562 | 631
A+B | 633 | 398 | 329 | 307 | 318 | 486 | 622 | 455 | 465 | 557 | 604 | 507 | 493 | 463 | 377 | 368 | 332 | 332 | 317 | 438 | 404 | 490 | 562 | 631
A+B+C | 437 | 321 | 215 | 246 | 237 | 367 | 502 | 358 | 405 | 460 | 455 | 425 | 373 | 356 | 284 | 286 | 248 | 241 | 248 | 314 | 311 | 361 | 467 | 421
A: Use data from the same month of last 2 years
B: 5-min exhaustion rate
C: 95th percentile

## Slide 20: Proposed NSRS Requirement
A: Same month of last 3 years
B: Use 3-hour ahead forecast error C: Use net under-forecast only D: Use dynamically determined percentile based on risk of net load ramp

## Slide 21: Proposed NSRS Requirement
A: Same month of last 3 years
B: Use 3-hour ahead forecast error C: Use net under-forecast only D: Use dynamically determined percentile based on risk of net load ramp

## Slide 22: Proposed NSRS Requirement
A: Same month of last 3 years
B: Use 3-hour ahead forecast error C: Use net under-forecast only D: Use dynamically determined percentile based on risk of net load ramp

## Slide 23: Proposed NSRS Requirement

## Slide 24: Projected NSRS Requirement
 | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
1 | 737 | 1004 | 1071 | 1004 | 797 | 834 | 770 | 539 | 720 | 824 | 792 | 1076
2 | 737 | 1004 | 1071 | 1004 | 797 | 834 | 770 | 539 | 720 | 824 | 792 | 1076
3 | 1086 | 1388 | 1236 | 1698 | 1550 | 1517 | 1370 | 1228 | 1437 | 1600 | 1591 | 1491
4 | 1086 | 1388 | 1236 | 1698 | 1550 | 1517 | 1370 | 1228 | 1437 | 1600 | 1591 | 1491
5 | 1086 | 1388 | 1236 | 1698 | 1550 | 1517 | 1370 | 1228 | 1437 | 1600 | 1591 | 1491
6 | 1086 | 1388 | 1236 | 1698 | 1550 | 1517 | 1370 | 1228 | 1437 | 1600 | 1591 | 1491
7 | 1747 | 2430 | 2220 | 2066 | 1814 | 2114 | 1977 | 1733 | 1641 | 1815 | 1917 | 1872
8 | 1747 | 2430 | 2220 | 2066 | 1814 | 2114 | 1977 | 1733 | 1641 | 1815 | 1917 | 1872
9 | 1747 | 2430 | 2220 | 2066 | 1814 | 2114 | 1977 | 1733 | 1641 | 1815 | 1917 | 1872
10 | 1747 | 2430 | 2220 | 2066 | 1814 | 2114 | 1977 | 1733 | 1641 | 1815 | 1917 | 1872
11 | 1709 | 1561 | 1796 | 1405 | 1577 | 2137 | 1698 | 1942 | 2008 | 1929 | 1483 | 1499
12 | 1709 | 1561 | 1796 | 1405 | 1577 | 2137 | 1698 | 1942 | 2008 | 1929 | 1483 | 1499
13 | 1709 | 1561 | 1796 | 1405 | 1577 | 2137 | 1698 | 1942 | 2008 | 1929 | 1483 | 1499
14 | 1709 | 1561 | 1796 | 1405 | 1577 | 2137 | 1698 | 1942 | 2008 | 1929 | 1483 | 1499
15 | 1378 | 1426 | 1375 | 1375 | 1375 | 1375 | 1375 | 1375 | 1375 | 1375 | 1442 | 1924
16 | 1378 | 1426 | 1375 | 1375 | 1375 | 1375 | 1375 | 1375 | 1375 | 1375 | 1442 | 1924
17 | 1378 | 1426 | 1375 | 1375 | 1375 | 1375 | 1375 | 1375 | 1375 | 1375 | 1442 | 1924
18 | 1378 | 1426 | 1375 | 1375 | 1375 | 1375 | 1375 | 1375 | 1375 | 1375 | 1442 | 1924
19 | 1375 | 1473 | 1375 | 1375 | 1375 | 1375 | 1375 | 1375 | 1375 | 1375 | 1375 | 1662
20 | 1375 | 1473 | 1375 | 1375 | 1375 | 1375 | 1375 | 1375 | 1375 | 1375 | 1375 | 1662
21 | 1375 | 1473 | 1375 | 1375 | 1375 | 1375 | 1375 | 1375 | 1375 | 1375 | 1375 | 1662
22 | 1375 | 1473 | 1375 | 1375 | 1375 | 1375 | 1375 | 1375 | 1375 | 1375 | 1375 | 1662
23 | 737 | 1004 | 1071 | 1004 | 797 | 834 | 770 | 539 | 720 | 824 | 792 | 1076
24 | 737 | 1004 | 1071 | 1004 | 797 | 834 | 770 | 539 | 720 | 824 | 792 | 1076
Total | 32125 | 37126 | 36288 | 35694 | 33950 | 37406 | 34259 | 32771 | 34226 | 35671 | 34403 | 38099

## Slide 25: NSRS Net Load Ramp – Up and Risk Factor
Net Load Ramp-Up is the increase in Net Load over an hour.
The Net Load Ramp–Up Risk Factor is calculated by normalizing hourly ramp-up values by seasonal peak value
The Net Load Ramp-Up Risk Factor is averaged over 4 hour blocks.

## Slide 26: How is Risk Factor Used
Chart: Percentile- Risk Factor Mapping Function
Higher Risk Factor corresponds to a higher Percentile value for the Net Load Forecast Error.
Notes: Give example
Select one high risk
One low risk