## Slide 1
2016 Long-Term Load Forecast
Calvin Opheim
ERCOT
Manager, Forecasting & Analysis
SAWG
October 28, 2015

## Slide 2: Outline of Today’s Presentation
Summary of Results
Comparison to 2014 Long-Term Load Forecast
Forecasting Framework / Model Data Input
Normal Weather (50/50) Forecast
Assumptions and Challenges
Active Models

## Slide 3
Summary

## Slide 4: ERCOT Summer Peak Forecast

## Slide 5: ERCOT Annual Energy Forecast

## Slide 6: Forecast Adjustments
Freeport LNG Facility
  Incremental load of 655 MW was added to the forecast
  Timeline for the load addition was from Freeport’s website
  (http://www.freeportlng.com/Project_Status.asp)
  This load was not
  included in the
  previous forecast
  No reduction in the
  facility load was
  assumed for 4 CP
  and/or high price
  intervals

## Slide 7: Summary
Summer Peak Forecast
  Consistent with the previous forecast (within ~ 1%)
  Slower growth in the outer years (2023 on)
  Forecasted growth rate is 1.1% (2016 – 2025)
  Previous forecast growth rate was 1.3% (2014 – 2023)
Energy Forecast
  Consistent with the previous forecast (within ~ 1%)
  except for 2024
  The energy forecast is less than the previous forecast after 2020

## Slide 8: Historical and Forecasted Summer Peak Demand

## Slide 9: Historical and Forecasted Energy

## Slide 10
Forecasting Framework

## Slide 11: Weather Zones
Premise models and load models are developed for each weather zone

## Slide 12: Forecasting Premises
Premise Models
  Forecasted premise counts are used as the driver of future demand/energy growth in the majority of weather zones
  Economic variables were used as input in the premise forecast models
  Variables used include population, non-farm employment, and housing stock
  Also included error correction term

## Slide 13: Forecasting Premises
Monthly Economic Measures
  Non-farm employment
  Population
  Housing stock
  Moody’s base scenario was used for economic forecasts
Data Availability
  County level
  Counties are mapped into a weather zone
Growth Driver in Premise Models

## Slide 14: Forecasting Premises – Challenges
Premise counts were increased significantly via opt-in
Forecasting premises is problematic

## Slide 15: Forecasting Premises – Challenges
Premise counts were increased significantly via opt-in
Forecasting premises is problematic

## Slide 16: Forecasting Premises – Challenges
Premise counts are relatively flat
No significant benefit in forecasting premises

## Slide 17: Forecasting Premises – Challenges
Premise Models - Exceptions
  Unable to forecast premise counts in three weather zones
  Impacted by an entity opting-in (Far West and West)
  Flat premise growth (North)
Modeling Solution
  These three weather zones required traditional economic variables (population and non-farm employment) as the driver of future demand/energy growth in the hourly models

## Slide 18: Load Forecasting Models
Hourly Models
  Hourly models were created for each weather zone
  Over 48,000 hourly observations including load, weather data, and calendar variables (day-of-week, holidays, etc.)
  Historical data from January, 2010 through August, 2015 was used to create the models
Rationale
  Typically use 5 years of historical data in model development
  Allows for a more recent snapshot of appliance stock, energy efficiency impacts, demand response impacts, price responsive load, etc.

## Slide 19: Load Forecasting Models - Data Input
Weather Data
  Temperature, Temperature Squared
  Cooling Degree Days/Hours
  Heating Degree Days/Hours
  Cloud Cover
  Wind Speed
  May also include values from a previous day(s)
Two or three weather stations located in each weather zone

## Slide 20: Load Forecasting Models - Data Input
Calendar
  Month
  Day of the week
  Holidays
  Hour
  Interact Hour with Day of the week
Interactions
  May interact weather variables with calendar variables
  Example: Temperature with Hour

## Slide 21: Load Forecasting Models - Data Input
Monthly Premise Count by Customer Class
  Instead of using economic measures as the driver of future load growth, use the actual number of premises for each customer class
  Customer class is determined by the load profile assignment
  Three classes
    Residential (includes lighting)
    Commercial
    Industrial

## Slide 22: Load Forecasting Models - Data Input
Monthly Economic Data
  For the three weather zones without a premise forecast (Far West, West, and North), use population and non-farm employment as the driver of future load growth
Moody’s Base Scenario

## Slide 23
Normal Weather Forecast

## Slide 24: Normal Weather (50/50) Forecast
Performed at the Weather Zone Level
  Historical weather from calendar years 2002 – 2014 is used as input into each hourly weather zone forecast model

## Slide 25: Normal Weather (50/50) Forecast
Performed at the Weather Zone Level
  Forecasted values are sorted from high to low for each year
  The sorted values are averaged by rank
  Example:
  Below are the top 5 peak values for Coast for 2016

## Slide 26: Normal Weather (50/50) Forecast
Performed at the Weather Zone Level

## Slide 27: Normal Weather (50/50) Forecast
Performed at the Weather Zone Level
  This process is completed for every weather zone, for each forecasted year (2016 – 2025)
ERCOT (50/50) Forecast
  After the weather zone (50/50) hourly load forecasts are completed, the results are mapped into a representative historical calendar by rank
  The 2003 calendar was selected (as has been our convention in the past)

## Slide 28
Assumptions and Challenges

## Slide 29: Load Forecasting Assumptions
Current Modeling Framework Assumes:
  Inherent levels from the input data for
    Appliance stock / energy efficiency
    Demand Response, 4 CP Impact, behind-the-meter DG, Price Responsive Load
    Electric Vehicles
  No increase in territory to be served by ERCOT
  No discrete increase for additional LNG facilities (except for Freeport)
  No discrete increase in load for a Tesla plant or other large unanticipated load
No incremental adjustments (positive or negative) to the load forecast have been applied for the above

## Slide 30: Load Forecasting Challenges
Weather Volatility:
  Extreme weather events (record heat and cold, drought, flood, etc.) seem to occur fairly frequently
Economic Uncertainty
  Accuracy of economic forecasts
  Recession has occurred every decade since the 60s
Policy Impacts
  Behind the meter DG growth
  Energy Efficiency growth
  Increased price caps
  Loads in SCED

## Slide 31
Active Models

## Slide 32: Modeling Structure
ERCOT maintains an ensemble of load forecast models
  Neural Network models based on a single linear node
  Linear Regression model representation of the single linear node Neural Network model
    Uses the exact same variables, relationships as the single linear node Neural Network model
    Is easier to share the model form with Market Participants (i.e., the variables are easier to interpret than those from the Neural Network model)
    Results are very close to the Neural Network model
  Neural Network models based on linear and higher order nodes
  Models are maintained for daily energy forecasting, hourly energy forecasting, and a combination

## Slide 33
Appendix

## Slide 34: ERCOT 2016 Forecasts

## Slide 35: Weather Zone 2016 Forecasts

## Slide 36: Weather Zone 2016 Forecasts

## Slide 37: Weather Zone 2016 Forecasts

## Slide 38: Weather Zone 2016 Forecasts

## Slide 39: Weather Zone 2016 Forecasts

## Slide 40: Weather Zone 2016 Forecasts

## Slide 41: Weather Zone 2016 Forecasts

## Slide 42: Weather Zone 2016 Forecasts

## Slide 43: Questions?