## Slide 1: Should CDR be Further Adjusted to Better Account for EE, DR, DG and Renewables? YES! Or MAYBE!
Cyrus Reed, Lone Star Chapter, Sierra Club
Demand Side Working Group
November 5, 2015

## Slide 2: Overview
1. Why CDR is Important
2. Specific Recommendations
  A. IOU Efficiency Programs -- goals and achievements
  B. NOIE Efficiency Programs -- What we know and way forward
  E. Accounting for Building Code Efficiencies and Appliance Standards
  F. Account for DG growth?
  I. Price-Responsive DR?
  J. Market-Based DR?
3. Conclusions and Next Steps

## Slide 3: Why do we care?
Load Forecasting for CDR, SARA, Long Term Study and for Regional Planning is Important
The CDR is the one document read by policy makers, investors and others to determine the adequacy of our market to provide energy, though long-term forecasting should be as accurate as possible for all the reports
CDR was fixed recently to account for larger role of coastal and West Texas wind and anticipate solar – these changes have made a different in the debate
The role of EE, DR, and DG is being recognized more and more, but has not been fully incorporated into CDR though a high EE forecast has been incorporated into Long Term Study
ERCOT’s recent change to a premise count/neural network big improvement that better incorporates existing energy efficiency efforts, but…

## Slide 4: A few caveats/thoughts
Historical impacts of EE programs are already reflected in the historical data used to develop forecasts. Thus, only changes in EE that deviate from historical trends and are big enough to change the overall trends in electricity sales growth and electricity demand should be recognized in models relying on time-series data.
EE programs and policies are having an impact on slowing the growth in electricity sales and peak demand.
However, manner in which ERCOT presents its forecasts makes tEE impacts “invisible.” We can’t look that ERCOT’s CDR and see that EE programs over the past 10 years lowered energy demand by X% relative to what would have happened absent the programs, or look at energy use over past 10 years and see the same
Making EE more visible in ERCOT’s forecasts will be helpful to policy makers
Greater visibility would create a better link between the legislature’s goal for EE and ERCOT’s planning documents, help Texas get credit for EE toward future CPP goals, and better recognize how some recent important EE steps will impact future demand.
ERCOT may want to look at the report put out by Energy Systems Laboratory, which attempts to quantify the annual and ozone season savings for an example of how to better reflect these savings from EE.
Yes, the IOU program impacts have “plateaued.” But, CPS Energy,, Pedernales and possibly Austin Energy’s programs are ramping up. More-stringent building codes and AC appliance standards soon go into effect. Other steps to enhance EE or DR are being undertaken such as PACE financing, and Loads in SCED.
Recent forecast accuracy has been very good. But, better methods and reporting may soon be needed as these new incremental EE impacts start slowing demand growth and creating deviations from historical patterns.

## Slide 5: 1. What DR/EE is currently covered in SARA and CDR
SARA (2015)
  “ERS and LR that provide operating reserves are excluded from the SARA”
CDR (2015)
  Load Resources – Responsive Reserves (1,251 MWs)
  Non-Spin Reserves – 0 Mws
  ERS – 1,071
  Investor-Owned Utilities EE --208 MWs
    Only appears to incorporate load management programs, which are roughly 60% of total programs
    Total Specific Demand Side already in CDR –2,530 MWs

## Slide 6: Is ERS and LR correct?
LR
Might consider updating from 1251 to reflect new methodology that went up to 1351 in August of 2015
ERCOT shows more than 3400 MW qualified and up to 1650 have been used (including self arranged)
Recommendation: Move LR from 1251 to 1351 MWs
ERS
Includes both load and generation
1071 MWs has been upper limit and using this number or somewhere in the range reasonable

## Slide 7: Investor-Owned Utilities EE Programs
Most utilities in Texas are not only meeting their goals but exceeding them
Previously in CDR, ERCOT took 50 percent of goal (0.2%)of whole state in IOU territory
In latest CDRs, taking a base of 208 MWs of load management programs and putting out to future as if load management will remain exactly the same now and into future
SARA Could be Adjusted to Take Into Account some Percentage of EE and DR Demand Reduction in that Upcoming Year
Given that some EE is likely reflected in history and some programs are DR, taking DR as the base is fairly reasonable.
However more reasonable to base on actual achievements rather than goal
We could at least adjust the next calendar year based upon April Filings if there were increases
Proposal: Adjust upward the amount of DR/EE from IOU based upon filing in April or take 75% of total
Or do Load management plus 50% of planned EE;

## Slide 8: 2013 EE Numbers in CDR and in IOU Reports
Utility | 2014 | 2015 Expected | 2016 Expected | CDR 2015 | Cyrus Proposal
Oncor | 127.1 | 110.3 | 138.1 |  | 
Centerpoint | 159.2 | 160.9 | 141.5 |  | 
AEP TNC | 8.1 | 5.72 | 5.72 |  | 
AEP TCC | 40.1` | 33.07 | 33.07 |  | 
TNMP | 9.1` | 9.2 | 9.1 |  | 
Sharyland | 0.3 | 2 | 1.5 |  | 
Total | 343.9 | 321.19 | 328.99 | 208 MWs | 246 Mws

## Slide 9: NOIE Efficiency
NOIE have efficiency programs as well though they are not statutorily required
SB 924 (2011) requires all Cooperatives and Municipal Utilities to report their EE programs, goals and achievements to SECO annually
The First reports were delivered in April of 2012 and only covered 2011 year;
Current reports submitted in October of this year and cover 2014 – look back not forward
Not helpful for CDR generally
The Reports are improving but sometimes measure different types of programs and results (DR, DG and EE)
SECO has sent the reports to ESL for analysis of any EE savings, which is required by statute
ESL has not been able to verify much
But… we support allowing ERCOT to work with NOIEs where verifiable programs and savings exist and there are plans to continue and expand – this language was incorporated in NPPR 550
WE believe, however, that well established programs in Austin Energy and CPS Energy can be incorporated into CDR to the extent they are not included in historical data

## Slide 10: Some NOIE Numbers, 2014-2015 and Beyond
Utility | Austin Energy | CPS Energy | Pedernales Electric Coop | Bluebonnet Electric Coop
2014 Energy Savings | 127,600 MWhs | 98,240 MWhs | 9,723 MWhs | 
2014 Peak Demand Reduction | 67 MWs | 153 MWs | 16.25 MWs | 20 MWs (dispatchable)
2015 Energy Savings | 111,800 (through August) | 127,705 MWhs | NA | NA
2015 Peak Demand Reductions | 65 MWs + 9 MWs ERS | 189 MWs (some in ERS program) | NA | NA
2020 Goals | 800 MWs between 2007-2020 (about 50 MWs –averages about 1 percent energy savings) | 771 MWs between 2009 and 2020 (about 70 MWs per year) | 20 percent of growth through DR and EE | Try and reach overall 20 percent reduction in peak use
2025 Goals | At least another 100 MWs and up to 300 MWs more | To be defined in STEP II |  | 

## Slide 11: Political Subdivision & State Agency EE Programs
Under SB 700, all state agencies and certain universities required to do annual reporting on energy, water and gas usage, and set a goal to reduce energy use
Under SB 5(2001) and more Recent SB 898 (2011), political subdivisions, educational facilities and state agencies in 41 non-attainment areas are required to look at annual 5% reduction in energy use and report to SECO on their savings achieved
Reports for previous year due in November each year
Reports Analyzed by Energy Systems Lab to assess energy savings and emission reductions
Reporting in KWhs not in Demand Reduction
ESL currently does annual Emissions and Energy Savings Report – which includes SB 5 and SB 898 and includes projections –
Work with ESL to develop methodology to convert EE Savings into Projected Demand Savings but do not adjust CDR at present

## Slide 12: Impact of energy codes and appliance standards
Studies indicate that utility EE programs, plus implementation of stronger appliance standards and energy construction code driving down total & peak demand
One recent study found that even moderate codes and appliance standards would reduce overall demand by 6.8% nationally by 2025
Federal HVAC standard in Southern States moves to 14 SEER rating in 2015, with 18 month grace period. By mid-2016, only 14 SEER and above will be sold. About 7 percent less energy per HVAC
SECO adopted 2009 IECC and 2009 IRC codes in 2010 and made them state law by 2012
ESL found 2015 codes reduce energy savings by 10-23% compared to 2009 codes with similar peak demand savings
2012 Report found that adopting of energy codes in Texas had reduced peak demand between 2002-2009 by 684 MWs; 2014 report
Texas Legislature approved HB 1736, which requires that the 2015 IRC energy codes be adopted statewide for all new homes built after September of 2016
SECO just proposed rules to adopt both the 2015 IECC and 2015 IRC by September of 2016 for all new construction, as well as for state buildings. Final rule expected next month.
Recommendation: Do downward adjustment in 2017 based on new energy codes and appliance standards (see ESL study)

## Slide 13: Energy Systems Lab shows large energy savings from efficiency, building codes and HVACs
Chart: Annual Electricity Savings from Efficiency Programs according to Energy Systems Lab
| 2009.0 | 2010.0 | 2011.0 | 2012.0 | 2013.0
New Home, Multifamily and Commercial Construction Meeting New Energy Codes | 71966 | 175885 | 315876 | 503340 | 704920
New Efficient SEER 13 Air Conditioners | 372351 | 353732 | 336046 | 319243 | 303281
Utility Efficiency Programs | 538841 | 976984 | 1437883 | 1831318 | 2267414
SECO Grant and Loan Programs | 71910 | 154786 | 347175 | 508375 | 705060

## Slide 14: Many of the utility EE programs already cover Renewable DR Programs and NO further Adjustment Needed (Example: AEP, CPS Energy) However, to the extent that self-generators start to report to ERCOT or Utilities report these connections or distributive resources to PUC this distributed generation could be added into ERCOT projections as a new resource Austin Energy has 100 MW goal for distributed solar by 2025, with at least 70 MW by 2020; CPS Energy already covers solar MWs in STEP, but has just started two new programs – SolarHost (10 MW) and Roofless Solar (1 MW) Open access database run by NREL is incomplete, but still shows some 20-50 MWs above utility programs and utility-scale New third-party rules, community solar and PACE – SB 385 – could lead to major increases in DG Recommendation – start to capture some of this DG growth in CDR and assume faster rates of adoption; Review CPS Energy or other programs to see if 2017 CDR should be adjusted
  Distributed Generation -- Already covered above?

## Slide 15: Some Solar PV Numbers
Type | Example | Size | Years
Utility-Scale (over 10 MWs) | Webberville, First Solar, Alamo 1, 2,3,4, Blue Wing | 154 MWs | 2010-2015
Medium-Scale (1 MW to 9.9 MW) | Municipal/WWTP (Bexar, Denton, Dallas, Tarrant) | 9.9 MWs | 2014-15
Austin Area Commercial and Residential | Municipal/Commercial/Residential | 35 MWs | 2004-2015
San Antonio Commercial and Residential | Municipal/Commercial/Residential | 9.5 MWs | 2010-2015
Houston Gulf Coast Area | Residential and Commercial | 1.9 MWs | 2010-15
Dallas Area (zip codes in 75000 to 76000) | Residential and Commercial | 18.9 MWs | 2009-15
About 220 MWs of solar PV, including 154 MWs of utility-scale power plants already accounted for, but some DG that may not be covered by energy efficiency program reporting. Numbers below include NREL database plus report from Austin Energy.
CDR could consider some PV DG going forward

## Slide 16: Others
Price responsive DR –Some recent ERCOT analysis found there have been between approximately 200 and 800 MWs of price-responsive DR on 2014 on 4 CP Days not covered by ancillary services or ERS.
Recent ERCOT analysis suggests 300 MW to 800 MWs of 4 CP reduction in each of the last three seasons at the transmission level
REPs also reported some price responsive programs with MW reductions during high prices
Market-based DR – no adjustment needed yet until market rules in place. LOADS in SCED 1.0 or 2.0 may give us actual Market-based DRs that can be projected
Recommendation: Adjust CDR by 50% of average CP peak reduction due to price responsive DR? So 200 to 400 MWs of reduction if these amount is not already captured in historical data. Continue to assess the use of price-responsive DR or actual SCED DR deployments.

## Slide 17: Conclusions/Recommendations
  Adjust Spinning Reserve slightly to reflect recent methodology change (add 100 MWs);
  Upward adjustment in CDR for IOU programs each year as programs are rolled out to better reflect reality – suggest 75 % of expected or 60% to reflect DR and 50% of remainder
  Include where appropriate NOIE figures for energy efficiency programs, especially for CPS and Austin Energy if they expect to upgrade their historic levels of EE and DR
  Adjust for distributed generation not covered in other programs, especially for new programs like CPS Energy’s
  Adjust for price-responsive load shedding as appropriate; and
  Create a downward adjustment on load growth due to new energy building codes and appliance standards – perhaps 10% of expected peak load growth due to new premises

## Slide 18: What if we made these changes? How it impacts the CDR Note: Some of these might be “resources” rather than forecast adjustments
Category | 2015 CDR for 2017 | Revised CDR for 2017
Summer Peak Demand | 70,871 | 70,871
LR | (1251) | (1351)
ERS | (1071) | (1071
TDSP Standard Offer | (208) | (246)
NOIE | 0 | 0 (assuming no new programs)
Building Code and Appliance Standards | 0 | (85)
DG | 0 | 0 (assuming no big new growth and no DRE)
Price Responsive DR | 0 | (200)
Firm Peak Load | 68,341 | 67,918