## Slide 1
Reliability Deployment Price Adder
ERCOT
QSE Managers Working Group
11/6/2015

## Slide 2: Overview
ERCOT Market Analysis Group has been observing some telemetry issues that have caused the Reliability Deployment Price Adder to not be run as intended. Some of these instances were likely caused by confusion around the opt-out of RUC settlement and some were simply incorrect telemetry.
Our intent is to implement a RUC commitment validation prior to running the RTRDP pricing run
We are working on this solution and will communicate to the market when this change will go into production

## Slide 3: Current Implementation Examples
Current implementation of the Reliability Deployment Price Adder (NPRR 626) (RTRDP) SCED runs are triggered by either load deployments or a Resource Status Telemetry of ONRUC.
  Resource is not RUCed and telemeters ONRUC at anytime
  Resource is RUCed and has not opted-out and telemeters other than ONRUC at anytime during the RUC block
  Resource is RUCed and has opted-out, on their COP, and telemeters ONRUC instead of ONOPTOUT

## Slide 4: Potential Solutions
Regardless of when the RUC is communicated use a Resource Status telemetry snapshot when the following are true:
    The resource has a confirmed RUC commitment
    First hour of the RUC commitment block
    Online resource status available for SCED dispatch
  This Resource status snapshot would be used for the entire RUC block including any extensions of the RUC commitment block.
  This status would be used for
    QSE’s settlement for the entire RUC commitment block
    RUC trigger for the RTRDP pricing run
  If snapshot is ONOPTOUT then Resource is
    opted-out of RUC settlement
    RTRDP pricing run will not be initiated
  If snapshot is ON or ONRUC then Resource
    will be settled as per RUC settlement
    RTRDP pricing runs will be initiated for the entire block
  Compliance around RUC startup

## Slide 5: Potential Solutions
Put in place additional telemetry compliance when unit is committed by a RUC process

## Slide 6
QUESTIONS / COMMENTS???